Version 1.0

May 2013

Revision History

| Ver. | Date | Description |
| --- | --- | --- |
| 1.0 | May 22, 2013 | First release |

Contents

Introduction	1

Windows server 2012	2

Intel Onboard SAS/SATA RSTe RAID	2

BIOS Required	2

Drivers Required	2

Software Required	2

Configuring Intel Onboard SAS/SATA RSTe RAID	2

Installation Tips	2

Chipset Driver Package Installation	3

Gigabit Ethernet Driver Installation	3

VGA Driver Installation	4

RAID Utility Installation	4

Network Utility Installation	4

Intel Onboard SAS/SATA ESRTII RAID	5

BIOS Required	5

Drivers Required	5

Software Required	5

Configuring Intel Onboard SAS/SATA ESRTII RAID	5

Installation Tips	5

Chipset Driver Package Installation	6

Gigabit Ethernet Driver Installation	6

VGA Driver Installation	7

RAID Utility Installation	7

Network Utility Installation	7

Intel Integrated RAID Module	7

BIOS Required	8

Drivers Required	8

Software Required	8

Configuring Intel Integrated RAID Module	8

Installation Tips	8

Chipset Driver Package Installation	9

Gigabit Ethernet Driver Installation	9

VGA Driver Installation	10

RAID Utility Installation	10

Network Utility Installation	10

Windows server 2008 R2	11

Intel Onboard SAS/SATA RSTe RAID	11

BIOS Required	11

Drivers Required	11

Software Required	11

Configuring Intel Onboard SAS/SATA RSTe RAID	11

Installation Tips	11

Chipset Driver Package Installation	12

Gigabit Ethernet Driver Installation	12

VGA Driver Installation	13

RAID Utility Installation	13

Network Utility Installation	13

Intel Onboard SAS/SATA ESRTII RAID	14

BIOS Required	14

Drivers Required	14

Software Required	14

Configuring Intel Onboard SAS/SATA ESRTII RAID	14

Installation Tips	14

Chipset Driver Package Installation	15

Gigabit Ethernet Driver Installation	15

VGA Driver Installation	16

RAID Utility Installation	16

Network Utility Installation	16

Intel Integrated RAID Module	16

BIOS Required	17

Drivers Required	17

Software Required	17

Configuring Intel Integrated RAID Module	17

Installation Tips	17

Chipset Driver Package Installation	18

Gigabit Ethernet Driver Installation	18

VGA Driver Installation	19

RAID Utility Installation	19

Network Utility Installation	19

Windows Server 2008	20

Intel Onboard SAS/SATA RSTe RAID	20

BIOS Required	20

Drivers Required (64 bit)	20

Drivers Required (32 bit)	20

Software Required	20

Configuring Intel Onboard SAS/SATA RSTe RAID	21

Installation Tips	21

Chipset Driver Package Installation	22

Gigabit Ethernet Driver Installation	22

VGA Driver Installation	22

RAID Utility Installation	23

Network Utility Installation	23

Intel Onboard SAS/SATA ESRTII RAID	23

BIOS Required	23

Drivers Required (64 bit)	23

Drivers Required (32 bit)	24

Software Required	24

Configuring Intel Onboard SAS/SATA ESRTII RAID	24

Installation Tips	24

Chipset Driver Package Installation	25

Gigabit Ethernet Driver Installation	25

VGA Driver Installation	25

RAID Utility Installation	26

Network Utility Installation	26

Intel Integrated RAID Module	26

BIOS Required	26

Drivers Required (64 bit)	26

Drivers Required (32 bit)	27

Software Required	27

Configuring Intel Integrated RAID Module	27

Installation Tips	27

Chipset Driver Package Installation	28

Gigabit Ethernet Driver Installation	28

VGA Driver Installation	28

RAID Utility Installation	29

Network Utility Installation	29

Red Hat Enterprise Linux 6 UPDATE 3	30

Intel Onboard SAS/SATA ESRTII RAID	30

BIOS Required	30

Drivers Required (64 bit)	30

Drivers Required (32 bit)	30

Software Required	30

Configuring Intel Onboard SAS/SATA ESRTII RAID	30

Installation Tips	30

Gigabit Ethernet Driver Installation	31

VGA Driver Installation	32

RAID Utility Installation	32

Intel Integrated RAID Module	33

BIOS Required	33

Drivers Required (64 bit)	33

Drivers Required (32 bit)	33

Software Required	33

Configuring Intel Integrated RAID Module	33

Installation Tips	33

Gigabit Ethernet Driver Installation	34

VGA Driver Installation	35

RAID Utility Installation	35

SuSE Linux Enterprise Server 11 SP2	36

Intel Onboard SAS/SATA ESRTII RAID	36

BIOS Required	36

Drivers Required (64 bit)	36

Drivers Required (32 bit)	36

Software Required	36

Configuring Intel Onboard SAS/SATA ESRTII RAID	36

Installation Tips	36

Gigabit Ethernet Driver Installation	38

VGA Driver Installation	38

RAID Utility Installation	38

Intel Integrated RAID Module	39

BIOS Required	39

Drivers Required (64 bit)	39

Drivers Required (32 bit)	39

Software Required	39

Configuring Intel Integrated RAID Module	39

Installation Tips	40

Gigabit Ethernet Driver Installation	41

VGA Driver Installation	41

RAID Utility Installation	41

SuSE Linux Enterprise Server 10 SP4	43

Intel Onboard SAS/SATA ESRTII RAID	43

BIOS Required	43

Drivers Required (64 bit)	43

Drivers Required (32 bit)	43

Software Required	43

Configuring Intel Onboard SAS/SATA ESRTII RAID	43

Installation Tips	43

Gigabit Ethernet Driver Installation	45

VGA Driver Installation	45

RAID Utility Installation	45

Intel Integrated RAID Module	46

BIOS Required	46

Drivers Required (64 bit)	46

Drivers Required (32 bit)	46

Software Required	46

Configuring Intel Integrated RAID Module	46

Installation Tips	47

Gigabit Ethernet Driver Installation	48

VGA Driver Installation	48

RAID Utility Installation	48

VMware ESXi 5.1	50

Intel Integrated RAID Module	50

BIOS Required	50

Drivers Required	50

Configuring Intel Integrated RAID Module	50

Installation Tips	50

Configure the VMware ESXi 5.1 host	51

Downloading the vSphere Client to the PC	51

vSphere Client Installation on the PC	51

Launch vSphere Client on the PC	51

Gigabit Ethernet Driver Installation	53

VGA Driver Installation	53

APPENDIX A: Intel onboard SAS/SATA RSTe RAID CONFIGURATION	54

Enabling Intel Onboard SAS/SATA RSTe RAID	54

Entering Intel onboard SAS/SATA RSTe RAID BIOS Utility	54

Loading Factory Default Setting	54

Creating a RAID Volume	54

Initializing a RAID Volume	54

Assigning a Hot Spare Drive	55

APPENDIX B: Intel onboard SAS/SATA ESRTII RAID CONFIGURATION	56

Enabling Intel Onboard SAS/SATA ESRTII RAID	56

Entering Intel onboard SAS/SATA ESRTII RAID BIOS Utility	56

Loading Factory Default Setting	56

Creating a RAID Volume	56

Initializing a RAID Volume	57

Assigning a Hot Spare Drive	57

Saving and Exiting Intel Onboard SAS/SATA ESRTII RAID Configuration Utility	57

APPENDIX C: Intel Integrated RAID Module	59

Set RAID Controller in EFI Mode or Legacy Mode	59

Entering RAID BIOS Utility (Legacy Mode)	59

Entering RAID EFI Utility (EFI Mode)	59

Loading Factory Default Setting	60

Creating a RAID Volume	60

Initializing a RAID Volume	61

Assigning a Hot Spare Drive	61

APPENDIX D: LSI MEGARAID CONFIGuration	62

Set RAID Controller in EFI Mode or Legacy Mode	62

Entering RAID BIOS Utility (Legacy Mode)	62

Entering RAID EFI Utility (EFI Mode)	62

Loading Factory Default Setting	62

Creating a RAID Volume	63

Initializing a RAID Volume	63

Assigning a Hot Spare Drive	63

# Introduction

The driver required for installing the OS manually is included in Smart Setup Resource Kit, this document provides you a OS installation guide on Altos AT350 F2, including,

Windows Server 2012

Windows Server 2008 R2

Windows Server 2008

Red Hat Enterprise Linux 6 Update 3

SuSE Linux Enterprise Server 11 SP2

SuSE Linux Enterprise Server 10 SP4

VMware ESXi 5.1

# Windows server 2012

## Intel Onboard SAS/SATA RSTe RAID

Below information describes how to manually install Windows Server 2012 on Altos T350 F2 with Intel Onboard SAS/SATA RSTe RAID.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) can support Windows Server 2012.

### Drivers Required

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA RSTe RAID | 3.6.0.1090 (Package 3.6.0.1093) | Smart Setup Resource Kit v2.0 |
| Chipset | Package 9.3.0.1025 | Smart Setup Resource Kit v2.0 |
| Onboard VGA | 4.0.2.4 (Package 20110516i) | Smart Setup Resource Kit v2.0 |
| Onboard Gigabit Ethernet | 12.3.35.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA RSTe RAID Utility | 3.6.0.1090 (Package 3.6.0.1093) | Smart Setup Resource Kit v2.0 |
| PROSet | 17.1.55.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Configuring Intel Onboard SAS/SATA RSTe RAID

Please refer to Appendix A. for Intel Onboard SAS/SATA RSTe RAID configuration.

### Installation Tips

NOTE. Please refer to Altos T350 F2 FAQ (Frequently Asked Questions) to select OS installation in EFI mode or Legacy mode if the OS media supports EFI.

NOTE. Windows Server 2012 cannot detect Intel Onboard SAS/SATA RSTe RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SAS/SATA RSTe RAID driver from Smart Setup Resource Kit DVD to a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Windows Server 2012 DVD. Follow the instructions to do the installation.

- When “Where do you want to install Windows” message displayed, please Insert the USB flash drive which includes the RAID driver and click Load Driver.

- Browse to the folder iaStorS.free.win8.64bit.3.6.0.1090 and click OK.

- It will show the available driver. Please select “Intel(R) C600 Series Chipset SAS RAID Controller (C:\isStorS.free.win8.64bit.3.6.1090\iaStorS.inf)” and click Next.

- After the RAID driver is loaded, please click Drive options to partition the drive or click Next to use default disk partition.

- Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Chipset Driver by expanding the directory in the following order, Altos T350 F2 -> Chipset -> Intel Chipset

- Select Windows Server 2012 then click on Browse.

- Double-click on Setup.exe and follow the instructions to complete the driver installation.

- After the installation is completed, reboot the system.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Gigabit Ethernet Driver by expanding the directory in the following order, Altos T350 F2 -> Network Adapters -> Intel Onboard LAN (Quad Port Ethernet Controller I350-T2).

- Select Windows Server 2012 then click on Browse.

- Double-click on Autorun.exe.

- Follow the instructions, accept the license agreement and use the default setting to complete the driver installation.

- The driver and PROSet utility will be installed together automatically.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup Resource Kit DVD.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Drivers.

- Find the VGA Driver by expanding the directory in the following order, Altos T350 F2 -> Graphics Adapters -> Intel onboard VGA .

- Select Windows Server 2012 64-bit then click on Browse.

- Double-click on Install.bat.

- Accept the license agreement to install the VGA driver.

- After the installation is completed, reboot the system.

- After installing the driver, you would see Matrox G200e (ServerEngines) listed in Display adapters.

### RAID Utility Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Utilities.

- Find the RAID Utility by expanding the directory in the following order, Altos T350 F2 -> Onboard SATA RAID (Utility) -> Intel SAS/SATA SCU RAID (RSTe).

- Select Windows Server 2012 64-bit.

- Double-click on Setup.exe.

- Accept the license and follow the instruction to install the RAID Utility. Reboot the system after the installation completed.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## Intel Onboard SAS/SATA ESRTII RAID

Below information describes how to manually install Windows Server 2012 on Altos T350 F2 with Intel Onboard SAS/SATA ESRTII RAID.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) can support Windows Server 2012.

### Drivers Required

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.0.927.2012 | Smart Setup Resource Kit v2.0 |
| Chipset | Package 9.3.0.1025 | Smart Setup Resource Kit v2.0 |
| Onboard VGA | 4.0.2.4 (Package 20110516i) | Smart Setup Resource Kit v2.0 |
| Onboard Gigabit Ethernet | 12.3.35.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.08.03.02 | Smart Setup Resource Kit v2.0 |
| PROSet | 17.1.55.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Configuring Intel Onboard SAS/SATA ESRTII RAID

Please refer to Appendix B. for Intel Onboard SAS/SATA ESRTII RAID configuration.

### Installation Tips

NOTE. Please refer to Altos T350 F2 FAQ (Frequently Asked Questions) to select OS installation in EFI mode or Legacy mode if the OS media supports EFI.

NOTE. Windows Server 2012 cannot detect Intel Onboard SAS/SATA ESRTII RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SAS/SATA ESRTII RAID driver from Smart Setup Resource Kit DVD to a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Windows Server 2012 DVD. Follow the instructions to do the installation.

- When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the RAID driver and click on “Load Driver”.

- Browse to the folder win8-x64_v15.00.0927.2012 and click OK.

- It will show the available driver. Please select “Intel Embedded Server RAID Technology II (C:\MegaSR1.inf)” as target driver.

- After the RAID driver is loaded, please click Drive options to partition the drive or click Next to use default disk partition.

- Follow the normal procedure to finish the installation n.

### Chipset Driver Package Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Chipset Driver by expanding the directory in the following order, Altos T350 F2 -> Chipset -> Intel Chipset

- Select Windows Server 2012 64-bit then click on Browse.

- Double-click on Setup.exe and follow the instructions to complete the driver installation.

- After the installation is completed, reboot the system.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Gigabit Ethernet Driver by expanding the directory in the following order, Altos T350 F2 -> Network Adapter -> Intel onboard LAN (Quad Port Ethernet Controller I350-T2).

- Select Windows Server 2012 64-bit then click on Browse.

- Double-click on Autorun.exe.

- Follow the instructions, accept the license agreement and use the default setting to complete the driver installation.

- The driver and PROSet utility will be installed together automatically.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup Resource Kit DVD.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Drivers.

- Find the VGA Driver by expanding the directory in the following order, Altos T350 F2 -> Graphics Adapters -> Intel onboard VGA.

- Select Windows Server 2012 64-bit then click on Browse.

- Double-click on Install.bat.

- Accept the license agreement to install the VGA driver.

- After the installation is completed, reboot the system.

- After installing the driver, you would see Matrox G200e (ServerEngines) listed in Display adapters.

### RAID Utility Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Utilities.

- Find the RAID Utility by expanding the directory in the following order, Altos T350 F2 -> Onboard SATA RAID (Utility) -> Intel SAS/SATA SCU RAID (ESRT2).

- Select Windows Server 2012 64-bit.

- Double-click on Setup.exe.

- Accept the license and follow the instruction to install the RAID Utility. Reboot the system after the installation completed.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## Intel Integrated RAID Module

Below information describes how to manually install Windows Server 2012 on Altos T350 F2 with Intel Integrated RAID Module.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) can support Windows Server 2012.

### Drivers Required

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Integrated RAID Module | 6.504.5.0 | Smart Setup Resource Kit v2.0 |
| Chipset | Package 9.3.0.1025 | Smart Setup Resource Kit v2.0 |
| Onboard VGA | 4.0.2.4 (Package 20110516i) | Smart Setup Resource Kit v2.0 |
| Onboard Gigabit Ethernet | 12.3.35.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.08.03.02 | Smart Setup Resource Kit v2.0 |
| PROSet | 17.1.55.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Configuring Intel Integrated RAID Module

Please refer to Appendix C. for Intel Integrated RAID Module.

### Installation Tips

NOTE. Please refer to Altos T350 F2 FAQ (Frequently Asked Questions) to select OS installation in EFI mode or Legacy mode if the OS media supports EFI.

NOTE. Windows Server 2012 cannot detect Intel Integrated RAID Module. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Integrated RAID Module driver from Smart Setup Resource Kit DVD to a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Windows Server 2012 DVD. Follow the instructions to do the installation.

- When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the RAID driver and click on “Load Driver”.

- Browse to the folder that includes the Integrated Hardware RAID driver and click OK.

- It will show the available driver. Please select “megasas2.inf” as target driver.

- After the RAID driver is loaded, please click Drive options to partition the drive or click Next to use default disk partition.

- Follow the normal procedure to finish the installation n.

### Chipset Driver Package Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Chipset Driver by expanding the directory in the following order, Altos T350 F2 -> Chipset -> Intel Chipset

- Select Windows Server 2012 then click on Browse.

- Double-click on Setup.exe and follow the instructions to complete the driver installation.

- After the installation is completed, reboot the system.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Gigabit Ethernet Driver by expanding the directory in the following order, Altos T350 F2 -> Network Adapters -> Intel Onboard LAN (Quad Port Ethernet Controller I350-T2).

- Select Windows Server 2012 64-bit then click on Browse.

- Double-click on Autorun.exe.

- Follow the instructions, accept the license agreement and use the default setting to complete the driver installation.

- The driver and PROSet utility will be installed together automatically.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup Resource Kit DVD.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Drivers.

- Find the VGA Driver by expanding the directory in the following order, Altos T350 F2 -> Graphics Adapters -> Intel onboard VGA.

- Select Windows Server 2012 64-bit then click on Browse.

- Double-click on Install.bat.

- Accept the license agreement to install the VGA driver.

- After the installation is completed, reboot the system.

- After installing the driver, you would see Matrox G200e (ServerEngines) listed in Display adapters.

### RAID Utility Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Utilities.

- Find the RAID Utility by expanding the directory in the following order, Altos T350 F2 -> SAS RAID  (Utility) -> Intel HW RAID SAS Module.

- Select Windows Server 2012 64-bit.

- Double-click on Setup.exe.

- Accept the license and follow the instruction to install the RAID Utility. Reboot the system after the installation completed.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

# Windows server 2008 R2

## Intel Onboard SAS/SATA RSTe RAID

Below information describes how to manually install Windows Server 2008 R2 on Altos T350 F2 with Intel Onboard SAS/SATA RSTe RAID.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) can support Windows Server 2008 R2.

### Drivers Required

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA RSTe RAID | 3.6.0.1090 (Package 3.6.0.1093) | Smart Setup Resource Kit v2.0 |
| Chipset | Package 9.3.0.1025 | Smart Setup Resource Kit v2.0 |
| Onboard VGA | 2.2.1.0 | Smart Setup Resource Kit v2.0 |
| Onboard Gigabit Ethernet | 12.3.35.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA RSTe RAID Utility | 3.6.0.1090 (Package 3.6.0.1093) | Smart Setup Resource Kit v2.0 |
| PROSet | 17.4.95.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Configuring Intel Onboard SAS/SATA RSTe RAID

Please refer to Appendix A. for Intel Onboard SAS/SATA RSTe RAID configuration.

### Installation Tips

NOTE. Please refer to Altos T350 F2 FAQ (Frequently Asked Questions) to select OS installation in EFI mode or Legacy mode if the OS media supports EFI.

NOTE. Windows Server 2008 R2 cannot detect Intel Onboard SAS/SATA RSTe RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SAS/SATA RSTe RAID driver from Smart Setup Resource Kit DVD to a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Windows Server 2008 R2 DVD. Follow the instructions to do the installation.

- When “Where do you want to install Windows” message displayed, please Insert the USB flash drive which includes RAID driver and click Load Driver.

- Browse to the folder iaStorS.free.64bit.3.6.0.1090 and click OK.

- It will show the available driver. Please select “Intel(R) C600 Series Chipset SAS RAID Controller (C:\isStorS.free.64bit.3.6.1090\iaStorS.inf)” and click Next.

- After the RAID driver is loaded, please click Drive options to partition the drive or click Next to use default disk partition.

- Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Chipset Driver by expanding the directory in the following order, Altos T350 F2 -> Chipset -> Intel Chipset

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Setup.exe and follow the instructions to complete the driver installation.

- After the installation is completed, reboot the system.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Gigabit Ethernet Driver by expanding the directory in the following order, Altos T350 F2 -> Network Adapters -> Intel Onboard LAN (Quad Port Ethernet Controller I350-T2).

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Autorun.exe.

- Follow the instructions, accept the license agreement and use the default setting to complete the driver installation.

- The driver and PROSet utility will be installed together automatically.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup Resource Kit DVD.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Drivers.

- Find the VGA Driver by expanding the directory in the following order, Altos T350 F2 -> Graphics Adapters-> Intel onboard VGA.

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Install.bat.

- Accept the license agreement to install the VGA driver.

- After the installation is completed, reboot the system.

- After installing the driver, you would see Matrox G200e (ServerEngines) listed in Display adapters.

### RAID Utility Installation

NOTE. Before installing Intel RAID Utility, please enable .NET Framework 3.51 (or later) features.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Utilities.

- Find the RAID Utility by expanding the directory in the following order, Altos T350 F2 -> Onboard SATA RAID -> Intel SAS/SATA SCU RAID (RSTe).

- Select Windows Server 2008 R2 SP1.

- Double-click on Setup.exe.

- Accept the license and follow the instruction to install the RAID Utility. Reboot the system after the installation completed.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## Intel Onboard SAS/SATA ESRTII RAID

Below information describes how to manually install Windows Server 2008 R2 on Altos T350 F2 with Intel Onboard SAS/SATA ESRTII RAID.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) can support Windows Server 2008 R2.

### Drivers Required

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.0.0927.2012 | Smart Setup Resource Kit v2.0 |
| Chipset | Package 9.3.0.1025 | Smart Setup Resource Kit v2.0 |
| Onboard VGA | 2.2.1.0 | Smart Setup Resource Kit v2.0 |
| Onboard Gigabit Ethernet | 12.3.35.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.08.03.02 | Smart Setup Resource Kit v2.0 |
| PROSet | 17.4.95.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Configuring Intel Onboard SAS/SATA ESRTII RAID

Please refer to Appendix B. for Intel Onboard SAS/SATA ESRTII RAID configuration.

### Installation Tips

NOTE. Please refer to Altos T350 F2 FAQ (Frequently Asked Questions) to select OS installation in EFI mode or Legacy mode if the OS media supports EFI.

NOTE. Windows Server 2008 R2 cannot detect Intel Onboard SAS/SATA ESRTII RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SAS/SATA ESRTII RAID driver from Smart Setup Resource Kit DVD to a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Windows Server 2008 R2 DVD. Follow the instructions to do the installation.

- When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Onboard SAS/SATA ESRTII RAID driver and click on “Load Driver”.

- Specify the folder that includes the Intel onboard SAS/SATA ESRTII RAID driver and the system will show the available driver. Select “Intel Embedded Server RAID Technology II (C:\MegaSR1.inf)” as target driver.

- After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

- Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Chipset Driver by expanding the directory in the following order, Altos T350 F2 -> Chipset -> Intel Chipset

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Setup.exe and follow the instructions to complete the driver installation.

- After the installation is completed, reboot the system.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Gigabit Ethernet Driver by expanding the directory in the following order, Altos T350 F2 -> Network Adapters -> Intel Onboard LAN (Quad Port Ethernet Controller I350-T2).

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Autorun.exe.

- Follow the instructions, accept the license agreement and use the default setting to complete the driver installation.

- The driver and PROSet utility will be installed together automatically.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup Resource Kit DVD.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Drivers.

- Find the VGA Driver by expanding the directory in the following order, Altos T350 F2 -> Graphics Adapters -> Intel Onboard VGA.

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Install.bat.

- Accept the license agreement to install the VGA driver.

- After the installation is completed, reboot the system.

- After installing the driver, you would see Matrox G200e (ServerEngines) listed in Display adapters.

### RAID Utility Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Utilities.

- Find the RAID Utility by expanding the directory in the following order, Altos T350 F2 -> Onboard SATA RAID -> Intel SAS/SATA SCU RAID (ESRT2).

- Select Windows Server 2008 R2 SP1.

- Double-click on Setup.exe.

- Accept the license and follow the instruction to install the RAID Utility. Reboot the system after the installation completed.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## Intel Integrated RAID Module

Below information describes how to manually install Windows Server 2008 R2 on Altos T350 F2 with Intel Integrated RAID Module.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) can support Windows Server 2008 R2.

### Drivers Required

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Integrated RAID Module | 6.540.5.0 | Smart Setup Resource Kit v2.0 |
| Chipset | Package 9.3.0.1025 | Smart Setup Resource Kit v2.0 |
| Onboard VGA | 2.2.1.0 | Smart Setup Resource Kit v2.0 |
| Onboard Gigabit Ethernet | 12.3.35.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.08.03.02 | Smart Setup Resource Kit v2.0 |
| PROSet | 17.4.95.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Configuring Intel Integrated RAID Module

Please refer to Appendix C. for Intel Integrated RAID Module configuration.

### Installation Tips

NOTE. Please refer to Altos T350 F2 FAQ (Frequently Asked Questions) to select OS installation in EFI mode or Legacy mode if the OS media supports EFI.

NOTE. Windows Server 2008 R2 cannot detect Intel Integrated RAID Module. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Integrated RAID Module driver from Smart Setup Resource Kit DVD to a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Windows Server 2008 R2 DVD. Follow the instructions to do the installation.

- When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Integrated RAID Module driver and click on “Load Driver”.

- Browse to the folder that includes the Integrated Hardware RAID driver and click OK.

- It will show the available driver. Please select “megasas2.inf” as target driver.

- After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

- Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Chipset Driver by expanding the directory in the following order, Altos T350 F2 -> Chipset -> Intel Chipset

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Setup.exe and follow the instructions to complete the driver installation.

- After the installation is completed, reboot the system.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Gigabit Ethernet Driver by expanding the directory in the following order, Altos T350 F2 -> Network Adapters -> Intel Onboard LAN (Quad Port Ethernet Controller I350-T2).

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Autorun.exe.

- Follow the instructions, accept the license agreement and use the default setting to complete the driver installation.

- The driver and PROSet utility will be installed together automatically.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup Resource Kit DVD.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Drivers.

- Find the VGA Driver by expanding the directory in the following order, Altos T350 F2 -> Graphics Adapters -> Intel Onboard VGA.

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Install.bat.

- Accept the license agreement to install the VGA driver.

- After the installation is completed, reboot the system.

- After installing the driver, you would see Matrox G200e (ServerEngines) listed in Display adapters.

### RAID Utility Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Utilities.

- Find the RAID Utility by expanding the directory in the following order, Altos T350 F2 -> SAS RAID (Utility) -> Intel HW RAID SAS Module.

- Select Windows Server 2008 R2 SP1.

- Double-click on Setup.exe.

- Accept the license and follow the instruction to install the RAID Utility. Reboot the system after the installation completed.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

# Windows Server 2008

## Intel Onboard SAS/SATA RSTe RAID

Below information describes how to manually install Windows Server 2008 on Altos T350 F2 with Intel Onboard SAS/SATA RSTe RAID.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) is required to support Windows Server 2008.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA RSTe RAID | 3.6.0.1090 (Package 3.6.0.1093) | Smart Setup Resource Kit v2.0 |
| Chipset | Package 9.3.0.1025 | Smart Setup Resource Kit v2.0 |
| Onboard VGA | 2.2.1.0 | Smart Setup Resource Kit v2.0 |
| Onboard Gigabit Ethernet | 12.3.35.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA RSTe RAID | 3.6.0.1090 (Package 3.6.0.1093) | Smart Setup Resource Kit v2.0 |
| Chipset | Package 9.3.0.1025 | Smart Setup Resource Kit v2.0 |
| Onboard VGA | 2.2.1.0 | Smart Setup Resource Kit v2.0 |
| Onboard Gigabit Ethernet | 12.3.35.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA RSTe RAID Utility | 3.5.1.1009 (Package 3.6.0.1093) | Download form Acer Global Download website |
| PROSet | 17.1.55.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Configuring Intel Onboard SAS/SATA RSTe RAID

Please refer to Appendix A. for Intel Onboard SAS/SATA RSTe RAID configuration.

### Installation Tips

NOTE. Please refer to Altos T350 F2 FAQ (Frequently Asked Questions) to select OS installation in EFI mode or Legacy mode if the OS media supports EFI.

NOTE. Windows Server 2008 cannot detect Intel Onboard SAS/SATA RSTe RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SAS/SATA RSTe RAID driver from Smart Setup Resource Kit DVD to a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Windows Server 2008 DVD. Follow the instructions to do the installation.

- When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Onboard SAS/SATA RSTe RAID driver and click on “Load Driver”.

- Specify the folder (iaStorS.free.64bit.3.1.0.1082 for 64-bit Windows Server 2008 and iaStorS.free.32bit.3.1.0.1082 for 32-bit Windows Server 2008) that includes the Intel onboard SAS/SATA RSte RAID driver and the system will show the available driver.

- Select “Intel(R) C600 Series Chipset SAS RAID Controller (C:\isStorS.free.64bit.3.1.1082\iaStorS.inf)” for 64-bit Windows Server 2008 and “Intel(R) C600 Series Chipset SAS RAID Controller (C:\isStorS.free.64bit.3.1.1082\iaStorS.inf)” for 32-bit Windows Server 2008 as target driver.

- After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

- Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Chipset Driver by expanding the directory in the following order, Altos T350 F2 -> Chipset -> Intel Chipset

- Select Windows Server 2008 SP2 then click on Browse.

- Double-click on Setup.exe and follow the instructions to complete the driver installation.

- After the installation is completed, reboot the system.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Gigabit Ethernet Driver by expanding the directory in the following order, Altos T350 F2 -> Network Adapters -> Intel Onboard LAN (Quad Port Ethernet Controller I350-T2).

- Select Windows Server 2008 SP2 then click on Browse.

- Double-click on Autorun.exe.

- Follow the instructions, accept the license agreement and use the default setting to complete the driver installation.

- The driver and PROSet utility will be installed together automatically.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup Resource Kit DVD.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Drivers.

- Find the VGA Driver by expanding the directory in the following order, Altos T350 F2 -> Graphics Adapters -> Intel Onboard VGA.

- Select Windows Server 2008 SP2 then click on Browse.

- Double-click on Install.bat.

- Accept the license agreement to install the VGA driver.

- After the installation is completed, reboot the system.

- After installing the driver, you would see Matrox G200e (ServerEngines) listed in Display adapters.

### RAID Utility Installation

Note. Before installing Intel RAID Utility, please enable .NET Framework 3.0 (or later) features.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Utilities.

- Find the RAID Utility by expanding the directory in the following order, Altos T350 F2 -> Onboard SATA RAID -> Intel SAS/SATA SCU RAID (RSTe).

- Select Windows Server 2008 SP2.

- Double-click on Setup.exe.

- Accept the license and follow the instruction to install the RAID Utility. Reboot the system after the installation completed.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## Intel Onboard SAS/SATA ESRTII RAID

Below information describes how to manually install Windows Server 2008 on Altos T350 F2 with Intel Onboard SAS/SATA ESRTII RAID.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) can support Windows Server 2008.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.0.0927.2012 | Smart Setup Resource Kit v2.0 |
| Chipset | Package 9.3.0.1025 | Smart Setup Resource Kit v2.0 |
| Onboard VGA | 2.2.1.0 | Smart Setup Resource Kit v2.0 |
| Onboard Gigabit Ethernet | 12.3.35.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.0.528.2012 | Smart Setup Resource Kit v2.0 |
| Chipset | Package 9.3.0.1025 | Smart Setup Resource Kit v2.0 |
| Onboard VGA | 2.2.1.0 | Smart Setup Resource Kit v2.0 |
| Onboard Gigabit Ethernet | 12.3.35.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.08.03.03 | Smart Setup Resource Kit v2.0 |
| PROSet | 17.1.55.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Configuring Intel Onboard SAS/SATA ESRTII RAID

Please refer to Appendix B. for Intel Onboard SAS/SATA ESRTII RAID configuration.

### Installation Tips

NOTE. Windows Server 2008 cannot detect Intel Onboard SAS/SATA ESRTII RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SAS/SATA ESRTII RAID driver from Smart Setup Resource Kit DVD to a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Windows Server 2008 DVD. Follow the instructions to do the installation.

- When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Onboard SAS/SATA RSTEII RAID driver and click on “Load Driver”.

- Specify the folder that includes the Intel onboard SAS/SATA ESRTIIR RAID driver and the system will show the available driver. Select “Intel Embedded Server RAID Technology II (C:\MegaSR1.inf)” as target driver.

- After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

- Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Chipset Driver by expanding the directory in the following order, Altos T350 F2 -> Chipset -> Intel Chipset

- Select Windows Server 2008 SP2 then click on Browse.

- Double-click on Setup.exe and follow the instructions to complete the driver installation.

- After the installation is completed, reboot the system.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Gigabit Ethernet Driver by expanding the directory in the following order, Altos T350 F2 -> Network Adapters -> Intel Onboard LAN (Quad Port Ethernet Controller I350-T2).

- Select Windows Server 2008 SP2 then click on Browse.

- Double-click on Autorun.exe.

- Follow the instructions, accept the license agreement and use the default setting to complete the driver installation.

- The driver and PROSet utility will be installed together automatically.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup Resource Kit DVD.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Drivers.

- Find the VGA Driver by expanding the directory in the following order, Altos T350 F2 -> Graphics Adapters -> Intel Onboard VGA.

- Select Windows Server 2008 SP2 then click on Browse.

- Double-click on Install.bat.

- Accept the license agreement to install the VGA driver.

- After the installation is completed, reboot the system.

- After installing the driver, you would see Matrox G200e (ServerEngines) listed in Display adapters.

### RAID Utility Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Utilities.

- Find the RAID Utility by expanding the directory in the following order, Altos T350 F2 -> Onboard SATA RAID -> Intel SAS/SATA SCU RAID (ESRT2).

- Select Windows Server 2008 SP2.

- Double-click on Setup.exe.

- Accept the license and follow the instruction to install the RAID Utility. Reboot the system after the installation completed..

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## Intel Integrated RAID Module

Below information describes how to manually install Windows Server 2008 on Altos T350 F2 with Intel Integrated RAID Module.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) can support Windows Server 2008.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Integrated RAID Module | 6.504.5.0 | Smart Setup Resource Kit v2.0 |
| Chipset | Package 9.3.0.1025 | Smart Setup Resource Kit v2.0 |
| Onboard VGA | 2.2.1.0 | Smart Setup Resource Kit v2.0 |
| Onboard Gigabit Ethernet | 12.3.35.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Integrated RAID Module | 6.504.5.0 | Smart Setup Resource Kit v2.0 |
| Chipset | Package 9.3.0.1025 | Smart Setup Resource Kit v2.0 |
| Onboard VGA | 2.2.1.0 | Smart Setup Resource Kit v2.0 |
| Onboard Gigabit Ethernet | 12.3.35.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.08.03.02 | Smart Setup Resource Kit v2.0 |
| PROSet | 17.1.55.0 (Package 17.4) | Smart Setup Resource Kit v2.0 |

### Configuring Intel Integrated RAID Module

Please refer to Appendix C. for Intel Integrated RAID Module configuration.

### Installation Tips

NOTE. Windows Server 2008 cannot detect Intel Integrated RAID Module. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Integrated RAID Module driver from Smart Setup Resource Kit DVD to a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Windows Server 2008 DVD. Follow the instructions to do the installation.

- When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Integrated RAID Module driver and click on “Load Driver”.

- Browse to the folder that includes the Integrated Hardware RAID driver and click OK.

- It will show the available driver. Please select “megasas2.inf” as target driver.

- After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

- Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Chipset Driver by expanding the directory in the following order, Altos T350 F2 -> Chipset -> Intel Chipset

- Select Windows Server 2008 SP2 then click on Browse.

- Double-click on Setup.exe and follow the instructions to complete the driver installation.

- After the installation is completed, reboot the system.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Gigabit Ethernet Driver by expanding the directory in the following order, Altos T350 F2 -> Network Adapters -> Intel Onboard LAN (Quad Port Ethernet Controller I350-T2).

- Select Windows Server 2008 SP2 then click on Browse.

- Double-click on Autorun.exe.

- Follow the instructions, accept the license agreement and use the default setting to complete the driver installation.

- The driver and PROSet utility will be installed together automatically.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup Resource Kit DVD.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Drivers.

- Find the VGA Driver by expanding the directory in the following order, Altos T350 F2 -> Graphics Adapters -> Intel Onboard VGA.

- Select Windows Server 2008 SP2 then click on Browse.

- Double-click on Install.bat.

- Accept the license agreement to install the VGA driver.

- After the installation is completed, reboot the system.

- After installing the driver, you would see Matrox G200e (ServerEngines) listed in Display adapters.

### RAID Utility Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Utilities.

- Find the Intel onboard SAS/SATA ESRTII RAID Utility by expanding the directory in the following order, Altos T350 F2 -> SAS RAID (Utility) -> Intel HW RAID SAS Module.

- Select Windows Server 2008 SP2.

- Double-click on Setup.exe.

- Accept the license and follow the instruction to install the RAID Utility. Reboot the system after the installation completed.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

# Red Hat Enterprise Linux 6 UPDATE 3

## Intel Onboard SAS/SATA ESRTII RAID

Below information describes how to manually install Red Hat Enterprise Linux 6 Update 3 on Altos T350 F2 with Intel Onboard SAS/SATA ESRTII RAID.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) is required to support Red Hat Enterprise Linux 6 Update 3.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.00.0725.2012 | Smart Setup Resource Kit v2.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 4.0.17 (Package 17.4) | Smart Setup Resource Kit v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.00.0725.2012 | Smart Setup Resource Kit v2.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 4.0.17 (Package 17.4) | Smart Setup Resource Kit v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.05.03.00 | Smart Setup Resource Kit v2.0. |

### Configuring Intel Onboard SAS/SATA ESRTII RAID

Please refer to Appendix B. for Intel Onboard SAS/SATA ESRTII RAID configuration

### Installation Tips

NOTE. Red Hat Enterprise Linux 6 Update 3 cannot detect Intel Onboard SAS/SATA ESRTII RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SAS/SATA ESRTII RAID driver (megasr-15.00.0725.2012-1-rhel63-ga-x86_64.img for 64-bit and megasr-15.00.0725.2012-1-rhel63-ga-x86.img for 32-bit) from Smart Setup Resource Kit DVD onto a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Red Hat Enterprise Linux 6 Update 3.

- At Welcome Menu, please press ESC.

- Type below command and press Enter.

linux dd

- Follow the instruction to select the Driver Disk Source to load the driver for Intel Onboard SAS/SATA ESRTII RAID.

- Follow the instruction and select Intel MegaSR as the install target device for the installation.

- Please Select Software Development Workstation.

- Please follow the general procedure to complete the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup Resource Kit DVD. Please check path of the RAID utility in Windows OS environment first and copy the driver from the Smart Setup Resource Kit DVD to HDD (e.g. \PRO1000\LINUX\igb-<version>.tar.gz to /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod igb

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf igb-<version>.tar.gz

# cd igb-<version>/src/

# make install

# modprobe igb

- Start the network service to bring up both of the network interfaces.

# service network start

- Use the network configuration utility like system-config-network in command line or select System -> Preferences-> Network Connections in GUI to configure the network interfaces.

### VGA Driver Installation

Red Hat Enterprise Linux 6 Update 3 has the built-in driver for onboard VGA. You don’t need to install the VGA driver manually.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup Resource Kit DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup Resource Kit DVD to HDD (e.g. /tmp directory)

NOTE. For 64-bit Red Hat Enterprise Linux 6 Update 3, please install below packages first from the Red Hat Enterprise Linux 6 Update 3 OS DVD.

libstdc++-4.4.6-3.el6.i686.rpm

compat-libstdc++-33-3.2.3-69.i686.rpm

libXau-1.0.5-1.el6.i686.rpm

libxcb-1.5-1.el6.i686.rpm

libX11-1.3-2.el6.i686.rpm

libXext-1.1-3.el6.i686.rpm

libXi-1.3-3.el6.i686.rpm

libXtst-1.0.99.2-3.el6.i686.rpm

- Install RAID Utility

# cd /tmp/

# ./install.csh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, please select Applications -> System Tools -> RAID Web Console 2 StartupUI.

## Intel Integrated RAID Module

Below information describes how to manually install Red Hat Enterprise Linux 6 Update 3 on Altos T350 F2 with Intel Integrated RAID Module.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) is required to support Red Hat Enterprise Linux 6 Update 3.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Integrated RAID Module | 6.505.02.00 | Smart Setup Resource Kit v2.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 4.0.17 (Package 17.4) | Smart Setup Resource Kit v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Integrated RAID Module | 6.505.02.0 | Smart Setup Resource Kit v2.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 4.0.17 (Package 17.4) | Smart Setup Resource Kit v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.05.03.00 | Smart Setup Resource Kit v2.0. |

### Configuring Intel Integrated RAID Module

Please refer to Appendix C. for Intel Integrated RAID Module configuration

### Installation Tips

NOTE. Red Hat Enterprise Linux 6 Update 3 cannot detect Intel Integrated RAID Module. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Integrated RAID Module driver ( megaraid_sas-v06.505.02.00_rhel6.3-1.x86_64.iso for 64-bit and megaraid_sas-v06.505.02.00_rhel6.3-1.686.iso for 32-bit) from Smart Setup Resource Kit DVD onto a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Red Hat Enterprise Linux 6 Update 3.

- At Welcome Menu, please press ESC.

- Type below command and press Enter.

linux dd

- Follow the instruction to select the Driver Disk Source to load the driver for Intel Integrated RAID Module.

- Follow the instruction and select Intel MegaSR as the install target device for the installation.

- Please Select Software Development Workstation.

- Please follow the general procedure to complete the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup Resource Kit DVD. Please check path of the RAID utility in Windows OS environment first and copy the driver from the Smart Setup Resource Kit DVD to HDD (e.g. \PRO1000\LINUX\igb-<version>.tar.gz to /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod igb

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf igb-<version>.tar.gz

# cd igb-<version>/src/

# make install

# modprobe igb

- Start the network service to bring up both of the network interfaces.

# service network start

- Use the network configuration utility like system-config-network in command line or select System -> Preferences-> Network Connections in GUI to configure the network interfaces.

### VGA Driver Installation

Red Hat Enterprise Linux 6 Update 3 has the built-in driver for onboard VGA. You don’t need to install the VGA driver manually.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup Resource Kit DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup Resource Kit DVD to HDD (e.g. /tmp directory)

NOTE. For 64-bit Red Hat Enterprise Linux 6 Update 3, please install below packages first from the Red Hat Enterprise Linux 6 Update 3 OS DVD.

libstdc++-4.4.6-3.el6.i686.rpm

compat-libstdc++-33-3.2.3-69.i686.rpm

libXau-1.0.5-1.el6.i686.rpm

libxcb-1.5-1.el6.i686.rpm

libX11-1.3-2.el6.i686.rpm

libXext-1.1-3.el6.i686.rpm

libXi-1.3-3.el6.i686.rpm

libXtst-1.0.99.2-3.el6.i686.rpm

- Install RAID Utility

# cd /tmp/

# ./install.csh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

To start the RAID Utility, please select Applications -> System Tools -> RAID Web Console 2 StartupUI.

# SuSE Linux Enterprise Server 11 SP2

## Intel Onboard SAS/SATA ESRTII RAID

Below information describes how to manually install SUSE Linux Enterprise Server 11 SP2 on Altos T350 F2 with Intel Onboard SAS/SATA ESRTII RAID.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) is required to support SUSE Linux Enterprise Server 11 SP2.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.00.0725.2012 | Smart Setup Resource Kit v2.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 4.0.17 (Package 17.4) | Smart Setup Resource Kit v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.00.0725.2012 | Smart Setup Resource Kit v2.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 4.0.17 (Package 17.4) | Smart Setup Resource Kit v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.05.03.00 | Smart Setup Resource Kit v2.0. |

### Configuring Intel Onboard SAS/SATA ESRTII RAID

Please refer to Appendix B for Intel Onboard SAS/SATA ESRTII RAID configuration

### Installation Tips

NOTE. SUSE Linux Enterprise Server 11 SP2 cannot detect Intel Onboard SAS/SATA ESRTII RAID. Please load the RAID driver during OS installation.

NOTE. You need an USB Flash drive to load RAID driver during the OS installation.

NOTE. Please extract files from Intel Onboard SAS/SATA ESRTII RAID driver image file (.img file) into USB flash drive. (DUDs\megasr-15.00.0528.2012-1-sles11-sp2-x86_64.img for 64-bit and DUDs\megasr-15.00.0528.2012-1- sles11-sp2-x86.img for 32-bit) from Smart Setup Resource Kit DVD and then write the .img onto an USB flash drive. The steps of write the .img file driver into USB flash drive as below.

  - Copy the image file (.img)  to any linux system.

  - Create a directory, for example, image.

# mkdir image

  - Mount the image file to image directory using the below command.

# mount –o loop megasr-15.00.0725.2012-1-sles11-sp2-XXX.img image

  - Change directory to image

# cd image

  - Copy the contents of the image directory into USB drive. (Contents of the image starts with 01 directory, copy the 01 directory to USB Drive)

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB flash drive and USB optical drive connected.

- Please boot the system from the SuSE Linux Enterprise Server 11 SP2 DVD.

- When you see the boot menu on the screen, please select Installation and press F6 to select Yes. Then press Enter to continue.

- Follow the instruction to load the driver for Intel Onboard SAS/SATA ESRTII RAID.

- Press back to boot the system.

- Follow the instruction to install the OS.

- At the Installation Settings, click on the Software.

- Check C/C++ Compiler and Tools under Development to add C/C++ compiler tools.

- Click on Accept and continue the installation.

- Follow the instruction to complete the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup Resource Kit DVD. Please check path of the Gigabit Ethernet driver  in Windows OS environment first and copy the driver from the Smart Setup Resource Kit DVD to HDD (e.g. \PRO1000\LINUX\igb-<version>.tar.gz  to /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod igb

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf igb-<version>.tar.gz

# cd igb-<version>/src/

# make install

# modprobe igb

- Start the network service to bring up both of the network interfaces.

# service network start

- Network configuration

# YaST2

- Select Network Devices -> Network Settings to configure the network setting.

### VGA Driver Installation

SUSE Linux Enterprise Server 11 SP2 has the built-in driver for onboard VGA. You don’t need to install the VGA driver manually.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup Resource Kit DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Install RAID Utility

# cd /tmp/

# ./install.csh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Computer -> More Applications ->  System -> RAID Web Console 2 StartupUI.

## Intel Integrated RAID Module

Below information describes how to manually install SUSE Linux Enterprise Server 11 SP2 on Altos T350 F2 with Intel Integrated RAID Module.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) is required to support SUSE Linux Enterprise Server 11 SP2.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Integrated RAID Module | 6.505.02.00 | Smart Setup Resource Kit v2.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 4.0.17 (Package 17.4) | Smart Setup Resource Kit v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Integrated RAID Module | 6.505.02.00 | Smart Setup Resource Kit v2.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 4.0.17 (Package 17.4) | Smart Setup Resource Kit v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.05.03.00 | Smart Setup Resource Kit v2.0. |

### Configuring Intel Integrated RAID Module

Please refer to Appendix C for Intel Integrated RAID Module configuration

### Installation Tips

NOTE. SUSE Linux Enterprise Server 11 SP2 cannot detect Intel Integrated RAID Module. Please load the RAID driver during OS installation.

NOTE. You need an USB Flash drive to load RAID driver during the OS installation.

NOTE. Please extract files from Intel Onboard SAS/SATA ESRTII RAID driver image file (.img file) into USB flash drive. (megaraid_sas-v06.505.02.00-1-sles11-sp2.x86_64.iso for 64-bit and megaraid_sas-v06.505.02.00-1-sles11-sp2.686.iso for 32-bit) from Smart Setup Resource Kit DVD and then write the .img onto an USB flash drive. The steps of write the .img file driver into USB flash drive as below.

- Copy the image file (.img)  to any linux system.

- Create a directory, for example, image.

# mkdir image

- Mount the image file to image directory using the below command.

# mount –o loop megaraid_sas-v06.505.02.00-1-sles11-sp2.x86_64.iso image

- Change directory to image

# cd image

- Copy the contents of the image directory into USB drive. (Contents of the image starts with 01 directory, copy the 01 directory to USB Drive)

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB flash drive and USB optical drive connected.

- Please boot the system from the SuSE Linux Enterprise Server 11 SP2 DVD.

- When you see the boot menu on the screen, please select Installation and press F6 to select Yes. Then press Enter to continue.

- Follow the instruction to load the driver for Intel Onboard SAS/SATA ESRTII RAID.

- Press back to boot the system.

- Follow the instruction to install the OS.

- At the Installation Settings, click on the Software.

- Check C/C++ Compiler and Tools under Development to add C/C++ compiler tools.

- Click on Accept and continue the installation.

- Follow the instruction to complete the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup Resource Kit DVD. Please check path of the Gigabit Ethernet driver  in Windows OS environment first and copy the driver from the Smart Setup Resource Kit DVD to HDD (e.g. \PRO1000\LINUX\igb-<version>.tar.gz  to /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod igb

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf igb-<version>.tar.gz

# cd igb-<version>/src/

# make install

# modprobe igb

- Start the network service to bring up both of the network interfaces.

# service network start

- Network configuration

# YaST2

- Select Network Devices -> Network Settings to configure the network setting.

### VGA Driver Installation

SUSE Linux Enterprise Server 11 SP2 has the built-in driver for onboard VGA. You don’t need to install the VGA driver manually.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup Resource Kit DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Install RAID Utility

# cd /tmp/

# ./install.csh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Computer -> More Applications ->  System -> RAID Web Console 2 StartupUI.

# SuSE Linux Enterprise Server 10 SP4

## Intel Onboard SAS/SATA ESRTII RAID

Below information describes how to manually install SUSE Linux Enterprise Server 10 SP4 on Altos T350 F2 with Intel Onboard SAS/SATA ESRTII RAID.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) is required to support SUSE Linux Enterprise Server 10 SP4.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.00.0725.2012 | Smart Setup Resource Kit v2.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 4.0.17 (Package 17.4) | Smart Setup Resource Kit v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.00.0725.2012 | Smart Setup Resource Kit v2.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 4.0.17 (Package 17.4) | Smart Setup Resource Kit v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.05.03.00 | Smart Setup Resource Kit v2.0. |

### Configuring Intel Onboard SAS/SATA ESRTII RAID

Please refer to Appendix B for Intel Onboard SAS/SATA ESRTII RAID configuration

### Installation Tips

NOTE. SUSE Linux Enterprise Server 10 SP4 cannot detect Intel Onboard SAS/SATA ESRTII RAID. Please load the RAID driver during OS installation.

NOTE. You need an USB Flash drive to load RAID driver during the OS installation.

NOTE. Please extract files from Intel Onboard SAS/SATA ESRTII RAID driver image file (.img file) into USB flash drive. (DUDs\megasr-15.00.0528.2012-1-sles11-sp2-x86_64.img for 64-bit and DUDs\megasr-15.00.0528.2012-1- sles11-sp2-x86.img for 32-bit) from Smart Setup Resource Kit DVD and then write the .img onto an USB flash drive. The steps of write the .img file driver into USB flash drive as below.

- Copy the image file (.img)  to any linux system.

- Create a directory, for example, image.

# mkdir image

- Mount the image file to image directory using the below command.

# mount –o loop megasr-15.00.0725.2012-1-sles11-sp2-XXX.img image

- Change directory to image

# cd image

- Copy the contents of the image directory into USB drive. (Contents of the image starts with 01 directory, copy the 01, 02 directory to USB Drive)

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB flash drive and USB optical drive connected.

- Please boot the system from the SuSE Linux Enterprise Server 10 SP4 DVD.

- When you see the boot menu on the screen, please select Installation and press F5 to select Yes. Then press Enter to continue.

- Follow the instruction to load the driver for Intel Onboard SAS/SATA ESRTII RAID.

- Press back to boot the system.

- Follow the instruction to install the OS.

- At the Installation Settings, click on the Software.

- Check C/C++ Compiler and Tools under Development to add C/C++ compiler tools.

- Click on Accept and continue the installation.

- Follow the instruction to complete the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup Resource Kit DVD. Please check path of the Gigabit Ethernet driver  in Windows OS environment first and copy the driver from the Smart Setup Resource Kit DVD to HDD (e.g. \PRO1000\LINUX\igb-<version>.tar.gz  to /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod igb

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf igb-<version>.tar.gz

# cd igb-<version>/src/

# make install

# modprobe igb

- Start the network service to bring up both of the network interfaces.

# service network start

- Network configuration

# YaST2

- Select Network Devices -> Network Settings to configure the network setting.

### VGA Driver Installation

SUSE Linux Enterprise Server 10 SP4 has the built-in driver for onboard VGA. You don’t need to install the VGA driver manually.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup Resource Kit DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Install RAID Utility

# cd /tmp/

# ./install.csh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Computer -> More Applications ->  System -> RAID Web Console 2 StartupUI.

## Intel Integrated RAID Module

Below information describes how to manually install SUSE Linux Enterprise Server 10 SP4 on Altos T350 F2 with Intel Integrated RAID Module.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) is required to support SUSE Linux Enterprise Server 10 SP4.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Integrated RAID Module | 6.505.02.00 | Smart Setup Resource Kit v2.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 4.0.17 (Package 17.4) | Smart Setup Resource Kit v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Integrated RAID Module | 6.505.02.00 | Smart Setup Resource Kit v2.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 4.0.17 (Package 17.4) | Smart Setup Resource Kit v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.05.03.00 | Smart Setup Resource Kit v2.0. |

### Configuring Intel Integrated RAID Module

Please refer to Appendix C for Intel Integrated RAID Module configuration

### Installation Tips

NOTE. SUSE Linux Enterprise Server 10 SP4 cannot detect Intel Integrated RAID Module. Please load the RAID driver during OS installation.

NOTE. You need an USB Flash drive to load RAID driver during the OS installation.

NOTE. Please extract files from Intel Integrated RAID Module driver image file (.iso file) into USB flash drive. (megaraid_sas-v06.505.02.00-1-sles10sp4.x86_64.iso for 64-bit and megaraid_sas-v06.505.02.00-1-sles10sp4.686.iso for 32-bit) from Smart Setup Resource Kit DVD and then write the .img onto an USB flash drive. The steps of write the .img file driver into USB flash drive as below.

- Copy the image file (.img)  to any linux system.

- Create a directory, for example, image.

# mkdir image

- Mount the image file to image directory using the below command.

# mount –o loop megaraid_sas-v06.505.02.00-1-sles10sp4.x86_64.iso image

- Change directory to image

# cd image

- Copy the contents of the image directory into USB drive. (Contents of the image starts with 01 directory, copy the 01, 02 directory to USB Drive)

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB flash drive and USB optical drive connected.

- Please boot the system from the SuSE Linux Enterprise Server 10 SP4 DVD.

- When you see the boot menu on the screen, please select Installation and press F5 to select Yes. Then press Enter to continue.

- Follow the instruction to load the driver for Intel Onboard SAS/SATA ESRTII RAID.

- Press back to boot the system.

- Follow the instruction to install the OS.

- At the Installation Settings, click on the Software.

- Check C/C++ Compiler and Tools under Development to add C/C++ compiler tools.

- Click on Accept and continue the installation.

- Follow the instruction to complete the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup Resource Kit DVD. Please check path of the Gigabit Ethernet driver  in Windows OS environment first and copy the driver from the Smart Setup Resource Kit DVD to HDD (e.g. \PRO1000\LINUX\igb-<version>.tar.gz  to /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod igb

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf igb-<version>.tar.gz

# cd igb-<version>/src/

# make install

# modprobe igb

- Start the network service to bring up both of the network interfaces.

# service network start

- Network configuration

# YaST2

- Select Network Devices -> Network Settings to configure the network setting.

### VGA Driver Installation

SUSE Linux Enterprise Server 10 SP4 has the built-in driver for onboard VGA. You don’t need to install the VGA driver manually.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup Resource Kit DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Install RAID Utility

# cd /tmp/

# ./install.csh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Computer -> More Applications ->  System -> RAID Web Console 2 StartupUI.

# VMware ESXi 5.1

## Intel Integrated RAID Module

Below information describes how to manually install VMware ESXi 5.1  on Altos T350 F2 with Intel Integrated RAID Module.

### BIOS Required

Altos T350 F2 BIOS 01.06.0002 (or later) is required to support VMware ESXi 5.1.

### Drivers Required

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Integrated RAID Module | 2.0.2.0088 | OS built-in |
| Onboard VGA | N/A | OS built-in |
| Onboard Gigabit Ethernet | 2.1.11.1 | OS built-in |

### Configuring Intel Integrated RAID Module

Please refer to Appendix C to configure Intel Integrated RAID Module.

### Installation Tips

NOTE. When you install OS with the Intel Integrated RAID Module, please disable onboard SAS/SATA RAID in BIOS Setup (Advanced -> Mass Storage Controller Configuration):

SAS/SATA Capable Controller            [Disabled]

NOTE. Please use the OS built-in driver of VMware ESXi 5.1 to install the OS.

NOTE. Please enable the Intel Virtualization Technology in BIOS Setup before installation.

Intel(R) Virtualization Technology     [Enabled]
Intel(R) VT for Directed I/O           [Enabled]

- Boot the system with VMware ESXi 5.1 installation CD

- Select ESXi-5.0.0-20120302001-standard Installer from the boot menu.

- At the Welcome screen, press Enter to continue with the installation.

- Accept VMware license by pressing F11.

- At the Select a Disk screen, select the disk drive on which to install ESXi 5.0 update 1 and press Enter.

- Follow the instructions to select the keyboard layout, root password.

- At Confirm Install screen, press F11 to start the installation.

- When the installation is completed, press Enter to reboot the host. Please remove the installation CD before the host rebooted.

### Configure the VMware ESXi 5.1 host

- When the installation is completed, reboot the host into VMware ESXi 5.1.

- Press F2 t configure the host.

- Select Configure Management Network to set IP address.

- Select the network adapter which you want to configure in Network Adapters and set the IP address in IP configuration.

- Press ESC when complete the configuration.

- Press Y to save the change.

### Downloading the vSphere Client to the PC

The vSphere Client is a Windows program that you can use to configure the host and to manage virtual machines.

- On a Windows-based PC, please launch the web browser.

- Please use the browser to connect to IP address of VMware ESXi host server which is installed with VMware ESXi.

- At the welcome page, please click Download the vSphere Client under Getting Started (This will redirect you to VMware website to download the vSphere Client).

### vSphere Client Installation on the PC

NOTE. The vSphere Client requires the Microsoft .NET Framwork 3.5 SP1. If it is not installed, the vSphere Client installer will install it.

NOTE. The installation of vSphere Client might require Internet connectivity.

- To install the vSphere Client on the PC by double-clicking the downloaded VMware-vicient.exe file.

- Choose a language for the installer and click OK.

- Follow the instructions and accept the license agreement to complete the installation.

### Launch vSphere Client on the PC

- Open vSphere Client on the PC.

- Type in the information to login VMware ESXi 5.0

- IP address of VMware ESXi host

- User name (“root” by default)

- Password (set during the VMware ESXi installation)

- When you see the Security Warning pop-up window, please check the checkbox for Install this certificate and do not display any security warnings for “IP address/Name of your system” and click on Ignore.

- Now, you can manage the VMware ESXi hypervisor or create virtual machines with the vSphere Client.

### Gigabit Ethernet Driver Installation

VMwaer ESXi 5.1 has the built-in driver for onboard NIC. You don’t need to install the onboard NIC driver manually.

### VGA Driver Installation

VMwaer ESXi 5.1 has the built-in driver for onboard VGA. You don’t need to install the VGA driver manually.

# APPENDIX A: Intel onboard SAS/SATA RSTe RAID CONFIGURATION

## Enabling Intel Onboard SAS/SATA RSTe RAID

- Please press F2 to Enter BIOS Setup  during POST

- Please press F9 to load default BIOS settings..

- In BIOS Main Page, change Quiet Boot from Enabled to Disabled.

- Select Advanced.

- Select Mass Storage Controller Configuration

- You might see below information:

SAS/SATA Capable Controller       [INTEL(R) RSTe]

- Make sure the setting of SAS/SATA Capable Controller is Intel (R) RSTe.

- Save the setting and exit from BIOS Setup

## Entering Intel onboard SAS/SATA RSTe RAID BIOS Utility

Please press CTRL-I when you see the RAID BIOS during POST.

## Loading Factory Default Setting

NOTE. The Intel onboard SAS/SATA RSTe RAID BIOS utility does not provide the function to load factory default setting.

## Creating a RAID Volume

- Select Create RAID Volume.

- The CREATE VOLUME MENU displayed.

- Type in the name of RAID volume.

- Select RAID level.

- Select desired HDD to create the RAID.

- Select Strip Size.

- Select Capacity.

- Select Create Volume.

- Press Y when “Are you sure you want to create the volume? (Y/N):” displayed.

- Now the RAID volume is created, you can press ESC and select Exit to exit.

## Initializing a RAID Volume

The RAID volume will be automatically initialized once it has been created.

## Assigning a Hot Spare Drive

The Intel onboard SAS/SATA RSTe RAID BIOS utility does not provide the function to create hot spare drive.

NOTE. Please create the hot spare drive with the Intel onboard SAS/SATA RSTe RAID utility in operating system.

# APPENDIX B: Intel onboard SAS/SATA ESRTII RAID CONFIGURATION

## Enabling Intel Onboard SAS/SATA ESRTII RAID

- Please press F2 during POST to enter BIOS Setup.

- Please press F9 to load default BIOS settings.

- In BIOS Main Page, change Quiet Boot from Enabled to Disabled.

Quiet Boot                        [Disabled]

- Select Advanced.

- Select Mass Storage Controller Configuration

- You might see below information:

SAS/SATA Capable Controller       [INTEL(R) RSTe]

- Please change the setting of SAS/SATA Capable Controller from INTEL RSTe to INTEL ESRT2 (LSI*).

SAS/SATA Capable Controller       [INTEL ESRT2 (LSI)]

- Save the setting and exit from BIOS Setup

## Entering Intel onboard SAS/SATA ESRTII RAID BIOS Utility

Please press CTRL-E when you see the RAID BIOS during POST.

## Loading Factory Default Setting

- Select Objects from Management menu.

- Select Adapter. The selectable adapter will be listed.

- Press Enter to select the adapter and the adapter setting will be shown on the screen.

- Select Factory Default.

- Select Yes to load the default settings.

- Press ESC Exit the RAID BIOS Utility

- Press Ctrl + Alt + Del to reboot the server.

## Creating a RAID Volume

- Select Configure  from Management Menu.

- Select New Configuration

- Select Yes to continue. An array selection window displays the devices connected to the current controller.

- Press the arrow keys to choose specific physical drives and press SPACE key to associate the selected drive with the current array. The indicator for selected drive change from READY to ONLINE

- After adding 2 drives to current array, press Enter to finish creating current array.

- Press Enter again to select array to configure.

- Press SPACE key to select the array and press F10 to configure the logical drive.

- The default RAID level for 2 disk drives is RAID1. Just select Accept to use the default setting.

- Press Enter to return to the ARRAY SELECTION MENU.

- Press Enter to end the array configuration.

- Select Yes to Save Configuration and press any key to return to the Configure menu.

## Initializing a RAID Volume

- Press Esc to return to the Management Menu.

- Select Initialize from Management menu. All logical drives should be listed under Logical Drives.

- Press SPACE key to select drives for initialization. The selected drive will be shown in yellow.

- Press F10.

- Select YES to start the initialization process.

- When initialization is complete, press any Esc to continue.

- Press Esc again to return to the Management Menu.

## Assigning a Hot Spare Drive

- Select Objects from Management menu.

- Select Physical Drive from Objects. All of the drives will be listed.

- Select a drive marked as READY and press Enter.

- Select Make Hot Spare and press Enter.

- Select Yes then you will see the HDD is changed from READY to HOTSP.

- Press Esc to return to the Management Menu.

## Saving and Exiting Intel Onboard SAS/SATA ESRTII RAID Configuration Utility

- When RAID configuration, initialization and assigning hot spare are completed, press Esc in the Management Menu and select Yes to exit the Software RAID Configuration Utility.

- Press Ctrl + Alt + Del to reboot the server.

- Now you can start to install OS.

# APPENDIX C: Intel Integrated RAID Module

## Set RAID Controller in EFI Mode or Legacy Mode

- Please enter BIOS Setup during POST

- Please select Boot Options.

- You would see below information.

EFI Optimized Boot    [Disabled]

- To enable EFI mode for the integrated hardware RAID, please enable the EFI Optimized Boot option. When you enable the option, the additional Use Legacy Video for EFI OS option will be displayed. Please also enable the Use Legacy Video for EFI OS option for EFI mode.

EFI Optimized Boot             [Enabled]

Use Legacy Video for EFI OS    [Enabled]

- To enable legacy mode for the integrated hardware RAID, please disable both options.

EFI Optimized Boot             [Disabled]

Use Legacy Video for EFI OS    [Disabled]

- Save the setting and exit from BIOS Setup.

## Entering RAID BIOS Utility (Legacy Mode)

Please press CTRL-G when you see the RAID BIOS during POST. After POST finished, the Adapter Selection page will show on the screen. Please click on Start to launch the configuration menu.

## Entering RAID EFI Utility (EFI Mode)

- Please enter EFI shell during POST.

- In EFI Shell, please type in drivers command to find out EFI SAS Driver number.

This SAS driver number is 192. The number 192 could be different, depending on the result of the EFI SAS driver number checking

- Type dh –d <SAS Driver number> command to find out SAS controller number.

This SAS controller number is 193. The number 193 could be different, depending on result of the EFI SAS controller number checking.

- Please type drvcfg –s <SAS Driver number> <SAS Controller number> command to start EFI RAID BIOS Console

- You will see below options.

Press 1 for EFI WebBIOS

2 for EFI CLI

or any other key to return:

- Please select 1 for EFI WebBIOS.

- Please click Start to launch the configuration menu.

## Loading Factory Default Setting

- In the left panel, please select Controller Properties. The current adapter settings appear.

- Click Next.

- Click Next .

- Change the setting of Set Factory Defaults from No to Yes and then click Submit.

- Click Home button

- Please select Exit in left panel

- Press Ctrl + Alt + Del to reboot the server.

## Creating a RAID Volume

- Launch the configuration menu.

- Select Configuration Wizard in left panel

- Select New Configuration and click Next.

- Select Manual Configuration and click Next.

- Hold on the Ctrl key and select the drives that you want to add into the array. After selecting the drives, please click on Add to Array.

- Click on Accept DG and then click Next.

- Select the array you just created, click Add to SPAN and click Next.

- Select the RAID Level you want to use, create the logical volume by specify the size at Select Size and click Accept to create the logical volume.

- Click Yes.

- Click Next after you create the logical volume.

- Click Accept.

- Click Yes to save the configuration.

- Click Cancel if there is no SSD caching.

## Initializing a RAID Volume

- Click Yes to initialize the RAID volume.

- You would see the RAID volume’s status is Optimal.

- Click Home to go back to the configuration menu.

## Assigning a Hot Spare Drive

- In Physical Drives view, please select a free disk marked as UNCONF GOOD.

- Select Make Global HSP or Make Dedicated HSP options and then click on Go.

- Click Home to go back to the configuration menu. You would see the disk marked as Hot Spare in Physical Drives view.

- Please select Exit.

- Click Yes to exit application.

- Press Ctrl + Alt + Del to reboot the system.

- Now you can start to install the operating system.

# APPENDIX D: LSI MEGARAID CONFIGuration

## Set RAID Controller in EFI Mode or Legacy Mode

- Please enter BIOS Setup during POST

- Please select Boot Options.

- You would see below information.

EFI Optimized Boot    [Disabled]

- To enable EFI mode for the integrated hardware RAID, please enable the EFI Optimized Boot option. When you enable the option, the additional Use Legacy Video for EFI OS option will be displayed. Please also enable the Use Legacy Video for EFI OS option for EFI mode.

EFI Optimized Boot             [Enabled]

Use Legacy Video for EFI OS    [Enabled]

- To enable legacy mode for the integrated hardware RAID, please disable both options.

EFI Optimized Boot             [Disabled]

Use Legacy Video for EFI OS    [Disabled]

- Save the setting and exit from BIOS Setup..

## Entering RAID BIOS Utility (Legacy Mode)

Please press CTRL-H when you see the RAID BIOS during POST. After POST finished, the Adapter Selection page will show on the screen. Please click on Start to launch the configuration menu.

## Entering RAID EFI Utility (EFI Mode)

- Please enter EFI shell during POST.

- In EFI Shell, please type in drvcfg –s.

- You will see below options.

Press 1 for EFI WebBIOS

2 for EFI CLI

or any other key to return:

- Please select 1 for EFI WebBIOS.

- Please click on Start to launch the configuration menu.

## Loading Factory Default Setting

- In the left panel, select Controller Properties. The current adapter settings appear. Please click on Next to change the setting.

- Change the setting of Set Factory Defaults from No to Yes then click on submit.

- Press Home button

- Please select Exit in left panel

- Press Ctrl+Alt+Del to reboot the server.

## Creating a RAID Volume

- Launch the configuration menu.

- Select Configuration Wizard in left panel

- Select New Configuration and click on Next.

- Select Manual Configuration and click on Next.

- Hold the Ctrl key and select the drives that you want to add into the array. After you selecting the drives, click on Add to Array.

- Click on Accept DG and then click on Next.

- Select the array you just created, click on Add to SPAN and then Next.

- Select the RAID Level you want to use, create the logical volume by specify the size at Select Size and click on Accept to create the logical volume.

- Click on Next after you creating the logical volume.

- Click on Accept and Yes to save the configuration.

## Initializing a RAID Volume

- After you create the logical volumes and click on Accept to save the configuration, the new logical volume will be automatically initialized after you click on Yes to confirm the change.

- You will see all the logical drives listed.

- Click on Home to go back to the configuration menu.

## Assigning a Hot Spare Drive

- Select a free disk marked as UNCONF GOOD and listed under Physical Drives.

- Select Make Global HSP or Make Dedicated HSP options and then click on Go.

- Click on Home to go back to the configuration menu. You will see the disk marked as Hot Spare in pink and listed under Physical Drives.

- Now you can reboot the system and install the Operating System. Select Exit, click on Yes and press Ctrl+Alt+Del to reboot the system.