Version 1.0

February 2012

Revision History

| Ver. | Date | Description |
| --- | --- | --- |
| 1.0 | Feb 29, 2012 | First release |

Contents

Introduction	1

Windows server 2008 R2	2

Intel Onboard SATA RAID	2

BIOS Required	2

Drivers Required	2

Software Required	2

Configuring Intel Onboard SATA RAID	2

Installation Tips	2

Chipset Driver Package Installation	3

Gigabit Ethernet Driver Installation	3

VGA Driver Installation	3

TPM Driver Installation (Optional)	3

RAID Utility Installation	4

Network Utility Installation	4

LSI Onboard SATA RAID	4

BIOS Required	4

Drivers Required	4

Software Required	4

Configuring LSI Onboard SATA RAID	5

Installation Tips	5

Chipset Driver Package Installation	5

Gigabit Ethernet Driver Installation	5

VGA Driver Installation	6

TPM Driver Installation (Optional)	6

RAID Utility Installation	6

Network Utility Installation	6

3041E-R	6

BIOS Required	6

Drivers Required	7

Software Required	7

Configuring 3041E-R	7

Installation Tips	7

Chipset Driver Package Installation	8

Gigabit Ethernet Driver Installation	8

VGA Driver Installation	8

TPM Driver Installation (Optional)	8

RAID Utility Installation	8

Network Utility Installation	9

MegaRAID 9240-4i/9260-8i	9

BIOS Required	9

Drivers Required	9

Software Required	9

Configuring MegaRAID 9240-4i/9260-8i	9

Installation Tips	9

Chipset Driver Package Installation	10

Gigabit Ethernet Driver Installation	10

VGA Driver Installation	11

TPM Driver Installation (Optional)	11

RAID Utility Installation	11

Network Utility Installation	11

Windows Server 2008	12

Intel Onboard SATA RAID	12

BIOS Required	12

Drivers Required (64 bit)	12

Drivers Required (32 bit)	12

Software Required	12

Configuring Intel Onboard SATA RAID	12

Installation Tips	12

Chipset Driver Package Installation	13

Gigabit Ethernet Driver Installation	13

VGA Driver Installation	13

TPM Driver Installation (Optional)	14

RAID Utility Installation	14

Network Utility Installation	14

LSI Onboard SATA RAID	14

BIOS Required	14

Drivers Required (64 bit)	14

Drivers Required (32 bit)	15

Software Required	15

Configuring LSI Onboard SATA RAID	15

Installation Tips	15

Chipset Driver Package Installation	16

Gigabit Ethernet Driver Installation	16

VGA Driver Installation	16

TPM Driver Installation (Optional)	16

RAID Utility Installation	16

Network Utility Installation	17

3041E-R	17

BIOS Required	17

Drivers Required (64 bit)	17

Drivers Required (32 bit)	17

Software Required	17

Configuring 3041E-R	18

Installation Tips	18

Chipset Driver Package Installation	18

Gigabit Ethernet Driver Installation	18

VGA Driver Installation	19

TPM Driver Installation (Optional)	19

RAID Utility Installation	19

Network Utility Installation	19

MegaRAID 9240-4i/9260-8i	19

BIOS Required	20

Drivers Required (64 bit)	20

Drivers Required (32 bit)	20

Software Required	20

Configuring MegaRAID 9240-4i/9260-8i	20

Installation Tips	20

Chipset Driver Package Installation	21

Gigabit Ethernet Driver Installation	21

VGA Driver Installation	21

TPM Driver Installation (Optional)	22

RAID Utility Installation	22

Network Utility Installation	22

Red Hat Enterprise Linux 6 UPDATE 1	23

LSI Onboard SATA RAID	23

BIOS Required	23

Drivers Required (64 bit)	23

Drivers Required (32 bit)	23

Software Required	23

Configuring LSI Onboard SATA RAID	23

Installation Tips	23

Gigabit Ethernet Driver Installation	24

VGA Driver Installation	24

RAID Utility Installation	25

3041E-R	25

BIOS Required	25

Drivers Required (64 bit)	25

Drivers Required (32 bit)	25

Software Required	26

Configuring 3041E-R	26

Installation Tips	26

Gigabit Ethernet Driver Installation	26

VGA Driver Installation	27

RAID Utility Installation	27

MegaRAID 9240-4i/9260-8i	27

BIOS Required	28

Drivers Required (64 bit)	28

Drivers Required (32 bit)	28

Software Required	28

Configuring MegaRAID 9240-4i/9260-8i	28

Installation Tips	28

Gigabit Ethernet Driver Installation	29

VGA Driver Installation	29

RAID Utility Installation	30

Red Hat Enterprise Linux 5 UPDATE 6	31

LSI Onboard SATA RAID	31

BIOS Required	31

Drivers Required (64 bit)	31

Drivers Required (32 bit)	31

Software Required	31

Configuring LSI Onboard SATA RAID	31

Installation Tips	31

Gigabit Ethernet Driver Installation	32

VGA Driver Installation	32

RAID Utility Installation	33

3041E-R	33

BIOS Required	33

Drivers Required (64 bit)	33

Drivers Required (32 bit)	34

Software Required	34

Configuring 3041E-R	34

Installation Tips	34

Gigabit Ethernet Driver Installation	34

VGA Driver Installation	35

RAID Utility Installation	35

MegaRAID 9240-4i/9260-8i	36

BIOS Required	36

Drivers Required (64 bit)	36

Drivers Required (32 bit)	36

Software Required	36

Configuring MegaRAID 9240-4i/9260-8i	36

Installation Tips	36

Gigabit Ethernet Driver Installation	37

VGA Driver Installation	37

RAID Utility Installation	38

SuSE Linux Enterprise Server 11 SP1	39

LSI Onboard SATA RAID	39

BIOS Required	39

Drivers Required (64 bit)	39

Drivers Required (32 bit)	39

Software Required	39

Configuring Onboard SATA RAID	39

Installation Tips	39

Gigabit Ethernet Driver Installation	40

VGA Driver Installation	40

RAID Utility Installation	41

3041E-R	41

BIOS Required	41

Drivers Required (64 bit)	41

Drivers Required (32 bit)	42

Software Required	42

Configuring 3041E-R	42

Installation Tips	42

Gigabit Ethernet Driver Installation	43

VGA Driver Installation	43

RAID Utility Installation	44

MegaRAID 9240-4i/9260-8i	44

BIOS Required	44

Drivers Required (64 bit)	44

Drivers Required (32 bit)	44

Software Required	45

Configuring MegaRAID 9240-4i/9260-8i	45

Installation Tips	45

Gigabit Ethernet Driver Installation	45

VGA Driver Installation	46

RAID Utility Installation	46

SuSE Linux Enterprise Server 10 SP4	48

LSI Onboard SATA RAID	48

BIOS Required	48

Drivers Required (64 bit)	48

Drivers Required (32 bit)	48

Software Required	48

Configuring Onboard SATA RAID	48

Installation Tips	48

Gigabit Ethernet Driver Installation	49

VGA Driver Installation	49

RAID Utility Installation	50

3041E-R	50

BIOS Required	50

Drivers Required (64 bit)	50

Drivers Required (32 bit)	50

Software Required	51

Configuring 3041E-R	51

Installation Tips	51

Gigabit Ethernet Driver Installation	51

VGA Driver Installation	52

RAID Utility Installation	52

MegaRAID 9240-4i/9260-8i	53

BIOS Required	53

Drivers Required (64 bit)	53

Drivers Required (32 bit)	53

Software Required	53

Configuring MegaRAID 9240-4i/9260-8i	53

Installation Tips	53

Gigabit Ethernet Driver Installation	54

VGA Driver Installation	55

RAID Utility Installation	55

APPENDIX A: Intel onboard SATA RAID CONFIGURATION	56

Set RAID Controller in Legacy Mode	56

Enabling Intel Onboard SATA RAID	56

Entering Intel onboard SATA RAID BIOS Utility	56

Loading Factory Default Setting	56

Creating a RAID Volume	56

Initializing a RAID Volume	57

Assigning a Hot Spare Drive	57

APPENDIX B: LSI onboard SATA RAID CONFIGURATION	58

Set RAID Controller in Legacy Mode	58

Enabling LSI Onboard SATA RAID	58

Entering Intel onboard SATA RAID BIOS Utility	58

Loading Factory default setting	58

Creating a RAID Volume	59

Initializing a RAID Volume	59

Assigning a Hot Spare Drive	59

Saving and Exiting Onboard RAID Configuration Utility	60

APPENDIX C: 3041E-R RAID CONFIGuration	61

Set RAID Controller in Legacy Mode	61

Entering RAID BIOS Utility	61

Loading Factory Default Setting	61

Creating a RAID Volume	61

Initializing a RAID Volume	61

Assigning a Hot Spare Drive	61

APPENDIX D: mEGARAID  9240-4i/ MEGARAID 9260-8i RAID CONFIGuration	63

Set RAID Controller in EFI Mode or Legacy Mode	63

Entering RAID BIOS Utility (Legacy Mode)	63

Entering RAID EFI Utility (EFI Mode)	63

Loading Factory Default Setting	63

Creating a RAID Volume	64

Initializing a RAID Volume	64

Assigning a Hot Spare Drive	64

# Introduction

IMPORTANT: Acer recommends to use Smart Setup to install the OS on Acer servers.

IMPORTANT: Smart Setup is an OS automatic deployment utility. Please refer to Smart Setup User Guide for more detail.

IMPORTANT: Smart Setup (Quick USB Wizard) can be downloaded from Acer’s website.

For user wants to install the OS manually without Smart Setup, this document provides you a OS installation guide on AR320 F2, including,

Windows Server 2008 R2

Windows Server 2008

Red Hat Enterprise Linux 6 Update 1

Red Hat Enterprise Linux 5 Update 6

SuSE Linux Enterprise Server 11 SP1

SuSE Linux Enterprise Server 10 SP4

# Windows server 2008 R2

## Intel Onboard SATA RAID

Below information describes how to manually install Windows Server 2008 R2 on AR320 F2 with Intel Onboard SATA RAID.

### BIOS Required

AR320 F2 BIOS P03 (or later) can support Windows Server 2008 R2.

### Drivers Required

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SATA RAID | 10.6.1.1001 | Smart Setup v2.0 |
| Chipset | Package 9.2.0.1025 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 11.11.43.0 (Package 16.5) | Smart Setup v2.0 |
| TPM | N/A | OS Built-in |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel Onboard SATA RAID Utility | 10.6.1.1001 | Smart Setup v2.0 |
| PROSet | (Package 16.5) | Smart Setup v2.0 |

### Configuring Intel Onboard SATA RAID

Please refer to Appendix A. for Intel Onboard SATA RAID configuration.

### Installation Tips

NOTE. Windows Server 2008 R2 can detect Intel Onboard SATA RAID. Please still load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SATA RAID driver from Smart Setup DVD to a floppy diskette or USB flash drive.

Please boot the system from the Windows Server 2008 R2 DVD. Follow the instructions to do the installation.

When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Onboard SATA RAID driver and click on “Load Driver”.

Specify the folder that includes the Intel onboard SATA RAID driver and the system will show the available driver. Select “Intel Desktop/Workstation/Server Express Chipset SATA RAID Controller (A:\iaStor.inf)” as target driver.

After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- You can find the folder in Smart Setup DVD by expanding Drivers -> AR320 F2 -> Chipset -> Intel Chipset and  selecting Windows Server 2008 R2 SP1

- Follow the instruction to install the driver and reboot the server after the chipset driver is installed.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup DVD into the optical drive

- Find the Gigabit Ethernet Driver by expanding the Driver directory from Smart Setup DVD in the following order, Drivers -> AR320 F2 -> Network Adapters -> Intel Onboard NIC and selecting Windows Server 2008 R2 SP1. Then click on Setup.

Select Install Drivers and Software.

Follow the instruction, accept the license agreement and use the default setting to complete the driver installation.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup DVD.

- Please insert the Smart Setup DVD into the optical drive.

Find the Onboard VGA Driver by expanding the Driver directory from Smart Setup DVD in the following order, Drivers -> AT310 F 2 -> Graphics Adapters -> Aspeed Onboard VGA and select Windows Server 2008 R2 SP1. Then click on Setup.

Follow the instruction to install the VGA driver and reboot the server after the driver is installed.

After installing the driver, you would see ASPEED Graphics Family listed in Display adapters.

### TPM Driver Installation (Optional)

NOTE: TPM driver is only needed when TPM module is installed.

Windows Server 2008 R2 has built-in driver for TPM. You don’t need to install additional TPM driver manually.

### RAID Utility Installation

Note. Before installing Intel RAID Utility, please enable .NET Framework 3.5 feature.

- Please insert the Smart Setup DVD into the optical drive.

Find the RAID Utility by expanding the directory from Smart Setup DVD in the following order, Utilities -> AR320 F2 -> RAID Controller-> Intel Onboard SATA RAID Utility, select Intel Onboard SATA RAID and then click on Setup.

Follow the instruction and use the default setting to complete the RAID Utility Installation.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## LSI Onboard SATA RAID

Below information describes how to manually install Windows Server 2008 R2 on AR320 F2 with LSI Onboard SATA RAID.

### BIOS Required

AR320 F2 BIOS P03 (or later) can support Windows Server 2008 R2.

### Drivers Required

| Device | Version | Driver Source |
| --- | --- | --- |
| LSI Onboard SATA RAID | 14.05.0816. 2011 | Smart Setup v2.0 |
| Chipset | Package 9.2.0.1025 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 11.11.43.0 (Package 16.5) | Smart Setup v2.0 |
| TPM | N/A | OS Built-in |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| LSI Onboard SATA RAID Utility | 11.06.00-03 | Smart Setup v2.0 |
| PROSet | Package 16.5 | Smart Setup v2.0 |

### Configuring LSI Onboard SATA RAID

Please refer to Appendix B. for LSI Onboard SATA RAID configuration.

### Installation Tips

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy LSI Onboard SATA RAID driver from Smart Setup DVD to a floppy diskette or USB flash drive.

- Please boot the system from the Windows Server 2008 R2 DVD. Follow the instructions to do the installation.

When “Load Driver” message displayed, please plug-in the USB flash which includes the LSI Onboard SATA RAID driver and click on “Load Driver”.

Specify the folder that includes the LSI onboard SATA RAID driver and the system will show the available driver. Select “A:\MegaSR.INF” as target driver.

After loading the RAID driver, you could click OK

Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- You can find the folder in Smart Setup DVD by expanding Drivers -> AR320 F2 -> Chipset -> Intel Chipset and selecting Windows Server 2008 R2 SP1.

- Follow the instruction to install the driver and reboot the server after the chipset driver is installed.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup DVD into the optical drive

- Find the Gigabit Ethernet Driver by expanding the Driver directory from Smart Setup DVD in the following order, Driver -> AR320 F2 -> Network Adapters -> Intel Onboard NIC and selecting Windows Server 2008 R2 SP1. Then click on Setup.

Select Install Drivers and Software.

Follow the instruction, accept the license agreement and use the default setting to complete the driver installation.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup DVD.

- Please insert the Smart Setup DVD into the optical drive.

Find the Onboard VGA Driver by expanding the Driver directory from Smart Setup DVD in the following order, Drivers -> AT310 F 2 -> Graphics Adapters -> Aspeed Onboard VGA and select Windows Server 2008 R2 SP1. Then click on Setup.

Follow the instruction to install the VGA driver and reboot the server after the driver is installed.

After installing the driver, you would see ASPEED Graphics Family listed in Display adapters.

### TPM Driver Installation (Optional)

NOTE: TPM driver is only needed when TPM module is installed.

Windows Server 2008 R2 has built-in driver for TPM. You don’t need to install additional TPM driver manually.

### RAID Utility Installation

- Please insert the Smart Setup DVD into the optical drive.

Find the RAID Utility by expanding the directory from Smart Setup DVD in the following order, Utilities -> AR320 F2 -> RAID Controllers-> LSI Onboard SATA RAID, select LSI Onboard SATA RAID Utility and then click on Setup.

Follow the instruction and use the default setting to complete the RAID Utility Installation.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## 3041E-R

Below information describes how to manually install Windows Server 2008 R2 on AR320 F2 with 3041E-R.

### BIOS Required

AR320 F2 BIOS P03 (or later) can support 3041E-R.

### Drivers Required

| Device | Version | Driver Source |
| --- | --- | --- |
| 3041E-R | 1.34.02 | Smart Setup v2.0 |
| Chipset | Package 9.2.0.1025 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 11.11.43.0 (Package 16.5) | Smart Setup v2.0 |
| TPM | N/A | OS Built-in |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-03 | Smart Setup v2.0 |
| PROSet | Package 16.5 | Smart Setup v2.0 |

### Configuring 3041E-R

Please refer to Appendix C for 3041E-R configuration.

### Installation Tips

NOTE. Though Windows Server 2008 R2 can recognize the 3041E-R, please still update the driver from Smart Setup. Please copy 3041E-R driver to a floppy or USB flash first before the installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

- Please boot the system from the Windows Server 2008 R2 DVD. Follow the instructions to do the installation.

- When you see the “Where do you want to install Windows?” on the screen, please insert the floppy diskette or USB flash with 3041E-R driver and click on Load Driver.

- Click on Browser and select directory of the floppy or USB flash that contains the driver.

- Click on OK. You will see the supported devices listed.

- Select “LSI Adapter, SAS 3000 series, 4-port with 1064E –StorPort (A:\lsi_sas.inf)” and click on Next.

- After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

- After the partition created, click on Next to continue the installation and follow the instructions to finish the installation.

### Chipset Driver Package Installation

- You can find the folder in Smart Setup DVD by expanding Drivers -> AR320 F2 -> Chipset -> Intel Chipset and selecting Windows Server 2008 R2 SP1.

- Follow the instruction to install the driver and reboot the server after the chipset driver is installed.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup DVD into the optical drive

- Find the Gigabit Ethernet Driver by expanding the Driver directory from Smart Setup DVD in the following order, Driver -> AR320 F2 -> Network Adapters -> Intel Onboard NIC and selecting Windows Server 2008 R2 SP1. Then click on Setup.

Select Install Drivers and Software.

Follow the instruction, accept the license agreement and use the default setting to complete the driver installation.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup DVD.

- Please insert the Smart Setup DVD into the optical drive.

Find the Onboard VGA Driver by expanding the Driver directory from Smart Setup DVD in the following order, Drivers -> AT310 F 2 -> Graphics Adapters -> Aspeed Onboard VGA and select Windows Server 2008 R2. Then click on Setup.

Follow the instruction to install the VGA driver and reboot the server after the driver is installed.

After installing the driver, you would see ASPEED Graphic Family listed in Display adapters.

### TPM Driver Installation (Optional)

NOTE: TPM driver is only needed when TPM module is installed.

Windows Server 2008 R2 has built-in driver for TPM. You don’t need to install additional TPM driver manually.

### RAID Utility Installation

- Please insert the Smart Setup DVD into the optical drive.

Find the RAID utility by expanding the directory from Smart Setup DVD in the following order, Utilities -> AR320 F2 -> SAS HBA, select LSI 3041E-R (MSM) and then click on Setup.

Follow the instruction and use the default setting to complete the RAID Utility Installation.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## MegaRAID 9240-4i/9260-8i

Below information describes how to manually install Windows Server 2008 R2 on AR320 F2 with MegaRAID 9240-4i/9260-8i.

### BIOS Required

AR320 F2 BIOS P03 (or later) can support Windows Server 2008 R2.

### Drivers Required

| Device | Version | Driver Source |
| --- | --- | --- |
| MegaRAID 9240-4i/9260-8i | 5.1.112.64 | Smart Setup v2.0 |
| Chipset | Package 9.2.0.1025 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 11.11.43.0 (Package 16.5) | Smart Setup v2.0 |
| TPM | N/A | OS Built-in |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-03 | Smart Setup v2.0 |
| PROSet | Package 16.5 | Smart Setup v2.0 |

### Configuring MegaRAID 9240-4i/9260-8i

Please refer to Appendix D for MegaRAID 9240-4i/9260-8i configuration.

### Installation Tips

NOTE. Please refer to AR320 F2 FAQ (Frequently Asked Questions) to select OS installation in EFI mode or Legacy mode if the OS media supports EFI.

NOTE. The Windows Server 2008 R2 cannot detect MegaRAID 9240-4i/9260-8i. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy MegaRAID 9240-4i/9260-8i driver from Smart Setup DVD to a floppy diskette or USB flash drive.

- Please boot the system from the Windows Server 2008 R2 DVD. Follow the instructions to do the installation.

- When you see the “Where do you want to install Windows?” on the screen, please insert the floppy diskette or USB flash with MegaRAID 9240-4i/9260-8i driver and click on Load Driver.

- Click on Browser and select directory of the floppy or USB flash that contains the driver.

- Click on OK. You will see the supported devices listed.

- Select “load driver: LSI MegaRAID SAS 9240-4i (A:\oemsetup.inf)” and click on Next.

- After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

- After the partition created, click on Next to continue the installation and follow the instructions to finish the installation.

### Chipset Driver Package Installation

- You can find the folder in Smart Setup DVD by expanding Drivers -> AR320 F2 -> Chipset -> Intel Chipset and  selecting Windows Server 2008 R2 SP1

- Follow the instruction to install the driver and reboot the server after the chipset driver is installed.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup DVD into the optical drive

- Find the Gigabit Ethernet Driver by expanding the Driver directory from Smart Setup DVD in the following order, Driver -> AR320 F2 -> Network Adapters -> Intel Onboard NIC and selecting Windows Server 2008 R2 SP1. Then click on Setup.

Select Install Drivers and Software.

Follow the instruction, accept the license agreement and use the default setting to complete the driver installation.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup DVD.

- Please insert the Smart Setup DVD into the optical drive.

Find the Onboard VGA Driver by expanding the Driver directory from Smart Setup DVD in the following order, Drivers -> AT310 F 2 -> Graphics Adapters -> Aspeed Onboard VGA and select Windows Server 2008 R2 SP1. Then click on Setup.

Follow the instruction to install the VGA driver and reboot the server after the driver is installed.

After installing the driver, you would see ASPEED Graphic Family listed in Display adapters.

### TPM Driver Installation (Optional)

NOTE: TPM driver is only needed when TPM module is installed.

Windows Server 2008 R2 has built-in driver for TPM. You don’t need to install additional TPM driver manually.

### RAID Utility Installation

- Please insert the Smart Setup DVD into the optical drive.

Find the RAID utility by expanding the directory from Smart Setup DVD in the following order, Utilities -> AR320 F2 -> RAID Controller, select LSI MegaRAID SAS 9240-4i (MSM)/LSI MegaRAID SAS 9240-8i (MSM) and then click on Setup.

Follow the instruction and use the default setting to complete the RAID Utility Installation.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

# Windows Server 2008

## Intel Onboard SATA RAID

Below information describes how to manually install Windows Server 2008 on AR320 F2 with Intel Onboard SATA RAID.

### BIOS Required

AR320 F2 BIOS P03 (or later) can support Windows Server 2008.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SATA RAID |  | Smart Setup v2.0 |
| Chipset | Package 9.2.0.1025 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 11.11.43.0 (Package 16.5) | Smart Setup v2.0 |
| TPM | N/A | OS Built-in |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SATA RAID |  | Smart Setup v2.0 |
| Chipset | Package 9.2.0.1025 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 11.11.43.0 (Package 16.5) | Smart Setup v2.0 |
| TPM | N/A | OS Built-in |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel Onboard SATA RAID Utility | 10.6.1.1001 | Smart Setup v2.0 |
| PROSet | Package 16.5 | Smart Setup v2.0 |

### Configuring Intel Onboard SATA RAID

Please refer to Appendix A. for Intel Onboard SATA RAID configuration.

### Installation Tips

NOTE. The Windows Server 2008 cannot detect Intel Onboard SATA RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SATA RAID driver from Smart Setup DVD to a floppy diskette or USB flash drive.

- Please boot the system from the Windows Server 2008 DVD. Follow the instructions to do the installation.

When “Load Driver” message displayed, insert the USB flash which includes the Onboard SATA RAID driver and click on “Load Driver”.

Specify the folder that includes the onboard SATA RAID driver and the system will show the available driver. Select “Intel Desktop/Workstation/Server Express Chipset SATA RAID Controller (A:\iaStor.inf)” as target driver.

After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- You can find the folder in Smart Setup DVD by expanding Drivers -> AR320 F2 -> Chipset -> Intel Chipset and  selecting Windows Server 2008

- Follow the instruction to install the driver and reboot the server after the chipset driver is installed.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup DVD into the optical drive

- Find the Gigabit Ethernet Driver by expanding the Driver directory from Smart Setup DVD in the following order, Driver -> AR320 F2 -> Network Adapters -> Intel Onboard NIC and select the operating system. Then click on Setup.

Select Install Drivers and Software.

Follow the instruction, accept the license agreement and use the default setting to complete the driver installation.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup DVD.

- Please insert the Smart Setup DVD into the optical drive.

Find the Onboard VGA Driver by expanding the Driver directory from Smart Setup DVD in the following order, Drivers -> AR320 F2 -> Graphics Adapters -> Aspeed Onboard VGA and select the operating system. Then click on Setup.

Follow the instruction to install the VGA driver and reboot the server after the driver is installed.

After installing the driver, you would see ASPEED Graphic Family listed in Display adapters.

### TPM Driver Installation (Optional)

NOTE: TPM driver is only needed when TPM module is installed.

Windows Server 2008 has built-in driver for TPM. You don’t need to install additional TPM driver manually.

### RAID Utility Installation

Note. Before installing Intel RAID Utility, please enable .NET Framework 3.5 feature.

- Please insert the Smart Setup DVD into the optical drive.

Find the RAID Utility by expanding the directory from Smart Setup DVD in the following order, Utilities -> AR320 F2-> RAID Controller, select Intel Onboard SATA RAID and then click on Setup.

Follow the instruction and use the default setting to complete the RAID Utility Installation.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## LSI Onboard SATA RAID

Below information describes how to manually install Windows Server 2008 on AR320 F2 with LSI Onboard SATA RAID.

### BIOS Required

AR320 F2 BIOS P03 (or later) can support LSI Onboard SATA RAID.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| LSI Onboard SATA RAID | 14.05.0816. 2011 | Smart Setup v2.0 |
| Chipset | Package 9.2.0.1025 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 11.11.43.0 (Package 16.5) | Smart Setup v2.0 |
| TPM | N/A | OS Built-in |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| LSI Onboard SATA RAID | 14.05.0816. 2011 | Smart Setup v2.0 |
| Chipset | Package 9.2.0.1025 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 11.11.43.0 (Package 16.5) | Smart Setup v2.0 |
| TPM | N/A | OS Built-in |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| LSI Onboard SATA RAID Utility | 11.06.00-03 | Smart Setup v2.0 |
| PROSet | (Package 16.5) | Smart Setup v2.0 |

### Configuring LSI Onboard SATA RAID

Please refer to Appendix B. for LSI Onboard SATA RAID configuration.

### Installation Tips

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy LSI Onboard SATA RAID driver from Smart Setup DVD to a floppy diskette or USB flash drive.

- Please boot the system from the Windows Server 2008 R2 DVD. Follow the instructions to do the installation.

When “Load Driver” message displayed, please insert the USB flash which includes the LSI Onboard SATA RAID driver and click on “Load Driver”.

Specify the folder that includes the LSI onboard SATA RAID driver and the system will show the available driver. Select “A:\MegaSR.INF” as target driver.

After loading the RAID driver, you could click OK

Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- You can find the folder in Smart Setup DVD by expanding Drivers -> AR320 F2 -> Chipset -> Intel Chipset and  selecting Windows Server 2008

- Follow the instruction to install the driver and reboot the server after the chipset driver is installed.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup DVD into the optical drive

- Find the Gigabit Ethernet Driver by expanding the Driver directory from Smart Setup DVD in the following order, Driver -> AR320 F2 -> Network Adapters -> Intel Onboard NIC and select the operating system. Then click on Setup.

Select Install Drivers and Software.

Follow the instruction, accept the license agreement and use the default setting to complete the driver installation.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup DVD.

- Please insert the Smart Setup DVD into the optical drive.

Find the Onboard VGA Driver by expanding the Driver directory from Smart Setup DVD in the following order, Drivers -> AR320 F2 -> Graphics Adapters -> Aspeed Onboard VGA and select the operating system. Then click on Setup.

Follow the instruction to install the VGA driver and reboot the server after the driver is installed.

After installing the driver, you would see ASPEED Graphic Family listed in Display adapters.

### TPM Driver Installation (Optional)

NOTE: TPM driver is only needed when TPM module is installed.

Windows Server 2008 has built-in driver for TPM. You don’t need to install additional TPM driver manually.

### RAID Utility Installation

- Please insert the Smart Setup DVD into the optical drive.

- Find the RAID Utility by expanding the directory from Smart Setup DVD in the following order, Utilities -> AR320 F2 -> RAID Controller select LSI Onboard SATA RAID (MSM) and then click on Setup.

- Follow the instruction and use the default setting to complete the RAID Utility Installation.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## 3041E-R

Below information describes how to manually install Windows Server 2008 on AR320 F2 with 3041E-R.

### BIOS Required

AR320 F2 BIOS P03 (or later) can support 3041E-R.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| 3041E-R | 1.34.02 | Smart Setup v2.0 |
| Chipset | Package 9.2.0.1025 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 11.11.43.0 (Package 16.5) | Smart Setup v2.0 |
| TPM | N/A | OS Built-in |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| 3041E-R | 1.34.02 | Smart Setup v2.0 |
| Chipset | Package 9.2.0.1025 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 11.11.43.0 (Package 16.5) | Smart Setup v2.0 |
| TPM | N/A | OS Built-in |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-03 | Smart Setup v2.0 |
| PROSet | Package 16.5 | Smart Setup v2.0 |

### Configuring 3041E-R

Please refer to Appendix C for 3041E-R configuration.

### Installation Tips

NOTE. Though Windows Server 2008 can recognize the 3041E-R, please still update the driver from Smart Setup. Please copy 3041E-R driver to a floppy or USB flash first before the installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

- Please boot the system from the Windows Server 2008 DVD. Follow the instructions to do the installation.

- When you see the “Where do you want to install Windows?” on the screen, please insert the floppy diskette or USB flash with 3041E-R driver and click on Load Driver.

- Click on Browser and select directory of the floppy or USB flash that contains the driver.

- Click on OK. You will see the supported devices listed.

- Select “LSI Adapter, SAS 3000 series, 4-port with 1064E –StorPort (A:\lsi_sas.inf)” and click on Next.

- After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

- After the partition created, click on Next to continue the installation and follow the instructions to finish the installation.

### Chipset Driver Package Installation

- You can find the folder in Smart Setup DVD by expanding Drivers -> AR320 F2 -> Chipset -> Intel Chipset and  selecting Windows Server 2008

- Follow the instruction to install the driver and reboot the server after the chipset driver is installed.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup DVD into the optical drive

- Find the Gigabit Ethernet Driver by expanding the Driver directory from Smart Setup DVD in the following order, Driver -> AR320 F2 -> Network Adapters -> Intel Onboard NIC and select the operating system. Then click on Setup.

Select Install Drivers and Software.

Follow the instruction, accept the license agreement and use the default setting to complete the driver installation.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup DVD.

- Please insert the Smart Setup DVD into the optical drive.

Find the Onboard VGA Driver by expanding the Driver directory from Smart Setup DVD in the following order, Drivers -> AR320 F2 -> Graphics Adapters -> Aspeed Onboard VGA and select the operating system. Then click on Setup.

Follow the instruction to install the VGA driver and reboot the server after the driver is installed.

After installing the driver, you would see ASPEED Graphic Family listed in Display adapters.

### TPM Driver Installation (Optional)

NOTE: TPM driver is only needed when TPM module is installed.

Windows Server 2008 has built-in driver for TPM. You don’t need to install additional TPM driver manually.

### RAID Utility Installation

- Please insert the Smart Setup DVD into the optical drive.

- Find the RAID utility by expanding the directory from Smart Setup DVD in the following order, Utilities -> AR320 F2 -> SAS HBA, select LSI 3041E-R (MSM) and then click on Setup.

Follow the instruction and use the default setting to complete the RAID Utility Installation.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## MegaRAID 9240-4i/9260-8i

Below information describes how to manually install Windows Server 2008 on AR320 F2 with MegaRAID 9240-4i/9260-8i.

### BIOS Required

AR320 F2 BIOS P03 (or later) can support Windows Server 2008.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| MegaRAID 9240-4i/9260-8i | 5.1.112.64 | Smart Setup v2.0 |
| Chipset | Package 9.2.0.1025 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 11.11.43.0 (Package 16.5) | Smart Setup v2.0 |
| TPM | N/A | OS Built-in |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| MegaRAID 9240-4i/9260-8i | 5.1.112.32 | Smart Setup v2.0 |
| Chipset | Package 9.2.0.1025 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 11.11.43.0 (Package 16.5) | Smart Setup v2.0 |
| TPM | N/A | OS Built-in |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-03 | Smart Setup v2.0 |
| PROSet | Package 16.5 | Smart Setup v2.0 |

### Configuring MegaRAID 9240-4i/9260-8i

Please refer to Appendix D for MegaRAID 9240-4i/9260-8i configuration.

### Installation Tips

NOTE. The Windows Server 2008 cannot detect MegaRAID 9240-4i/9260-8i. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy MegaRAID 9240-4i/9260-8i driver from Smart Setup DVD to a floppy diskette or USB flash drive.

- Please boot the system from the Windows Server 2008 DVD. Follow the instructions to do the installation.

- When you see the “Where do you want to install Windows?” on the screen, please insert the floppy diskette or USB flash with MegaRAID 9240-4i/9260-8i driver and click on Load Driver.

- Click on Browser and select directory of the floppy or USB flash that contains the driver.

- Click on OK. You will see the supported devices listed.

- Select “load driver: LSI MegaRAID SAS 9240-4i (A:\oemsetup.inf)” and click on Next.

- After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

- After the partition created, click on Next to continue the installation and follow the instructions to finish the installation.

### Chipset Driver Package Installation

- You can find the folder in Smart Setup DVD by expanding Drivers -> AR320 F2 -> Chipset -> Intel Chipset and  selecting Windows Server 2008

- Follow the instruction to install the driver and reboot the server after the chipset driver is installed.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup DVD into the optical drive

- Find the Gigabit Ethernet Driver by expanding the Driver directory from Smart Setup DVD in the following order, Driver -> AR320 F2 -> Network Adapters -> Intel Onboard NIC and select the operating system. Then click on Setup.

Select Install Drivers and Software.

Follow the instruction, accept the license agreement and use the default setting to complete the driver installation.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup DVD.

- Please insert the Smart Setup DVD into the optical drive.

Find the Onboard VGA Driver by expanding the Driver directory from Smart Setup DVD in the following order, Drivers -> AR320 F2 -> Graphics Adapters -> Aspeed Onboard VGA and select the operating system. Then click on Setup.

Follow the instruction to install the VGA driver and reboot the server after the driver is installed.

After installing the driver, you would see ASPEED Graphic Family listed in Display adapters.

### TPM Driver Installation (Optional)

NOTE: TPM driver is only needed when TPM module is installed.

Windows Server 2008 has built-in driver for TPM. You don’t need to install additional TPM driver manually.

### RAID Utility Installation

- Please insert the Smart Setup DVD into the optical drive.

- Find the RAID utility by expanding the directory from Smart Setup DVD in the following order, Utilities -> AR320 F2 -> RAID Controller, select LSI MegaRAID SAS 9240-4i (MSM)/LSI MegaRAID SAS 9240-8i (MSM) and then click on Setup.

Follow the instruction and use the default setting to complete the RAID Utility Installation.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

# Red Hat Enterprise Linux 6 UPDATE 1

## LSI Onboard SATA RAID

Below information describes how to manually install Red Hat Enterprise Linux 6 Update 1 on AR320 F2 with LSI Onboard SATA RAID.

### BIOS Required

AR320 F2 BIOS P03 (or later) can support Red Hat Enterprise Linux 6 Update 1.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| LSI Onboard SATA RAID | 14.05.0727.2011-1 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0 |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| LSI Onboard SATA RAID | 14.05.0727.2011-1 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0 |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-05 | Smart Setup v2.0 |

### Configuring LSI Onboard SATA RAID

Please refer to Appendix B for LSI Onboard SATA RAID configuration

### Installation Tips

NOTE. Please copy LSI Onboard SATA RAID driver to a floppy first before the installation

NOTE. 32-bit Red Hat Enterprise Linux 6 does not support OS installation in EFI mode. Please refer appendix D to set RAID controller in Legacy Mode.

- Please boot the system from the Red Hat Enterprise Linux 6.

- At Welcome Menu, Please press ESC and type below command:

linux dd blacklist=ahci

- Follow the instruction to load the driver for LSI Onboard SATA RAID from the driver diskette.

- Follow the instruction for the installation.

- Please Select Software Development Workstation.

- Please follow the normal procedure to finish the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod e1000e

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf e1000e-<version>.tar.gz

# cd e1000e-<version>/src/

# make install

# modprobe e1000e

- Start the network service to bring up both of the network interfaces.

# service network start

- Use the network configuration utility like system-config-network to configure the network interfaces.

### VGA Driver Installation

NOTE. The onboard VGA driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Please change directory to /tmp.

# cd /tmp/

- Run the install script to install VGA driver. For 64-bit Linux, please run below command:

# ./auto-update.sh

For 32-bit Linux, please run below command:

# ./auto-update.sh

After the driver is installed, please restart the X server by pressing “ctrl + alt + backspace” or rebooting the system to take effect.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

NOTE. For RHEL 6 64-bit, please install below package first from RHEL 6 64-bit DVD.

libstdc++-4.4.5-6.el6.i686.rpm

compat-libstdc++-33-3.2.3-69. i686.rpm

libXau-1.0.5-1.el6. i686.rpm

libxcb-1.5-1.el6. i686.rpm

libX11-1.3-2.el6. i686.rpm

libXext-1.1-3.el6. i686.rpm

libXi-1.3-3.el6. i686.rpm

libXtst-1.0.99.2-3.el6. i686.rpm

- Install RAID Utility

# cd /tmp/

# ./install.sh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Applications -> System Tools -> MegaRAID Storage Manager StartupUI.

## 3041E-R

Below information describes how to manually install Red Hat Enterprise Linux 6 Update 1 on AR320 F2 with 3041E-R.

### BIOS Required

AR320 F2 BIOS P03 (or later) can support Red Hat Enterprise Linux 6 Update 1.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| 3041E-R | Built-in | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| 3041E-R | Built-in | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-05 | Smart Setup v2.0. |

### Configuring 3041E-R

Please refer to Appendix C for 3041E-R configuration

### Installation Tips

NOTE. 32-bit Red Hat Enterprise Linux 6 does not support OS installation in EFI mode. Please refer appendix C to set RAID controller in Legacy Mode.

- Please boot the system from the Red Hat Enterprise Linux 6 Update 1.

- At Welcome Menu, select Install or upgrade an existing system.

- Follow the instruction for the installation.

- Please Select Software Development Workstation.

- Please follow the normal procedure to finish the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod e1000e

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf e1000e-<version>.tar.gz

# cd e1000e-<version>/src/

# make install

# modprobe e1000e

- Start the network service to bring up both of the network interfaces.

# service network start

- Use the network configuration utility like system-config-network to configure the network interfaces.

### VGA Driver Installation

NOTE. The onboard VGA driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

1.     Please change directory to /tmp.

# cd /tmp/

2.      Run the install script to install VGA driver. For 64-bit Linux, please run below command:

# ./auto-update.sh

For 32-bit Linux, please run below command:

# ./auto-update.sh

- After the driver is installed, please restart the X server by pressing “ctrl + alt + backspace” or rebooting the system to take effect.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

NOTE. For RHEL 6 64-bit, please install below package first from RHEL 6 64-bit DVD.

libstdc++-4.4.5-6.el6.i686.rpm

compat-libstdc++-33-3.2.3-69.i686.rpm

libXau-1.0.5-1.el6.i686.rpm

libxcb-1.5-1.el6.i686.rpm

libX11-1.3-2.el6.i686.rpm

libXext-1.1-3.el6.i686.rpm

libXi-1.3-3.el6.i686.rpm

libXtst-1.0.99.2-3.el6.i686.rpm

- Install RAID Utility

# cd /tmp/

# ./install.csh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Applications -> System Tools -> MegaRAID Storage Manager StartupUI.

## MegaRAID 9240-4i/9260-8i

Below information describes how to manually install Red Hat Enterprise Linux 6 on AR320 F2 with MegaRAID 9240-4i/9260-8i.

### BIOS Required

AR320 F2 BIOS P03 (or later) can support Red Hat Enterprise Linux 6 Update 1

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| MegaRAID 9240-4i/9260-8i | Package 5.4 | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| MegaRAID 9240-4i/9260-8i | Package 5.4 | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-05 | Smart Setup v2.0. |

### Configuring MegaRAID 9240-4i/9260-8i

Please refer to Appendix D for MegaRAID 9240-4i/9260-8i configuration

### Installation Tips

- Please boot the system from the Red Hat Enterprise Linux 6 Update 1.

- At Welcome Menu, Please press ESC and type linux dd blacklist=ahci and press Enter.

Please select the sda as the Driver Disk Source.

- Follow the instruction for the installation.

- Please Select Software Development Workstation.

- Please follow the normal procedure to finish the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod e1000e

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf e1000e-<version>.tar.gz

# cd e1000e-<version>/src/

# make install

# modprobe e1000e

- Start the network service to bring up both of the network interfaces.

# service network start

- Use the network configuration utility like system-config-network to configure the network interfaces.

### VGA Driver Installation

NOTE. The onboard VGA driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

1.     Please change directory to /tmp.

# cd /tmp/

2.      Run the install script to install VGA driver. For 64-bit Linux, please run below command:

# ./auto-update.sh

For 32-bit Linux, please run below command:

# ./auto-update.sh

- After the driver is installed, please restart the X server by pressing “ctrl + alt + backspace” or rebooting the system to take effect.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

NOTE. For RHEL 6 64-bit, please install below package first from RHEL 6 64-bit DVD.

libstdc++-4.4.5-6.el6.i686.rpm

compat-libstdc++-33-3.2.3-69.i686.rpm

libXau-1.0.5-1.el6.i686.rpm

libxcb-1.5-1.el6.i686.rpm

libX11-1.3-2.el6.i686.rpm

libXext-1.1-3.el6.i686.rpm

libXi-1.3-3.el6.i686.rpm

libXtst-1.0.99.2-3.el6.i686.rpm

- Install RAID Utility

# cd /tmp/

# ./install.sh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Applications -> System Tools -> MegaRAID Storage Manager StartupUI.

# Red Hat Enterprise Linux 5 UPDATE 6

## LSI Onboard SATA RAID

Below information describes how to manually install Red Hat Enterprise Linux 5 Update 6 on AR320 F2 with LSI Onboard SATA RAID.

### BIOS Required

AR320 F2 BIOS P03 (or later) can support Red Hat Enterprise Linux 5 Update 6..

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| LSI Onboard SATA RAID | 14.05.0727.2011-1 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0 |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| LSI Onboard SATA RAID | 14.05.0727.2011-1 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0 |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0 |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-05 | Smart Setup v2.0 |

### Configuring LSI Onboard SATA RAID

Please refer to Appendix B for LSI Onboard SATA RAID configuration

### Installation Tips

NOTE. You need an external USB floppy drive to load RAID driver during the OS installation.

- Please boot the system from the Red Hat Enterprise Linux 5 Update 6.

- At Welcome Menu, please press ESC and type below command:

linux dd noprobe=ata1 noprobe=ata2 noprobe=ata3 noprobe=ata4

- Follow the instruction to load the LSI onboard SATA RAID driver from the driver diskette.

- At the package selection step, select Software Development for the installation package.

- When the installation complete message on the screen, please press Ctrl + Alt + F2 to command mode.

- Please mount the USB floppy drive, and run below command to replace the AHCI driver.

# sh replace_ahci.sh

NOTE. To check the USB floppy drive device, please use the following command.

# cat /proc/partitions
major minor  #blocks  name
  7      0      85516 loop0
  8      0  974608386 sda
  8      1     104391 sda1
  8      2  974502029 sda2
  8     16       1440 sdb
253      0  972455936 dm-0
253      1    2031616 dm-1

In this example, the USB floppy drive device name is sdb.

NOTE. To create USB floppy drive device, please use below command with the major and minor information.

# mknod /dev/sdb b 8 16

NOTE. To mount the USB floppy drive, please use below command.

# mkdir /update
# mount /dev/sdb /update
# cd /update

- After AHCI driver is replaced, press Ctrl + Alt + Del to reboot the system to finish the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod e1000e

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf e1000e-<version>.tar.gz

# cd e1000e-<version>/src/

# make install

# modprobe e1000e

- Start the network service to bring up both of the network interfaces.

# service network start

- Use the network configuration utility like system-config-network to configure the network interfaces.

### VGA Driver Installation

NOTE. The onboard VGA driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Please change directory to /tmp.

# cd /tmp/

- Run the install script to install VGA driver. For 64-bit Linux, please run below command:

# ./auto-update.sh

For 32-bit Linux, please run below command:

# ./auto-update.sh

After the driver is installed, please restart the X server by pressing “ctrl + alt + backspace” or rebooting the system to take effect.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

NOTE. For RHEL 5 64-bit, it is necessary to install compat-libstdc++ version 33-3.x before installing rpm. Before installing MSM, this RPM is available in the OS DVD

libstdc++-4.4.4-13.el6.i686.rpm

compat-libstdc++-33-3.2.3-69. i686.rpm

libXau-1.0.5-1.el6. i686.rpm

libxcb-1.5-1.el6. i686.rpm

libX11-1.3-2.el6. i686.rpm

libXext-1.1-3.el6. i686.rpm

libXi-1.3-3.el6. i686.rpm

libXtst-1.0.99.2-3.el6. i686.rpm

- Install RAID Utility

# cd /tmp/

# ./install.sh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Applications -> System Tools -> MegaRAID Storage Manager StartupUI.

## 3041E-R

Below information describes how to manually install Red Hat Enterprise Linux 5 Update 6 on AR320 F2 with 3041E-R.

### BIOS Required

AR320 F2 BIOS P03 (or later) can support Red Hat Enterprise Linux 5 Update 6.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| 3041E-R | Built-in | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| 3041E-R | Built-in | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-05 | Smart Setup v2.0. |

### Configuring 3041E-R

Please refer to Appendix C for 3041E-R configuration

### Installation Tips

- Please boot the system from the Red Hat Enterprise Linux 5 Update 6.

- At Welcome Menu, select Install or upgrade an existing system.

- Follow the instruction for the installation.

- Please Select Software Development Workstation.

- Please follow the normal procedure to finish the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod e1000e

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf e1000e-<version>.tar.gz

# cd e1000e-<version>/src/

# make install

# modprobe e1000e

- Start the network service to bring up both of the network interfaces.

# service network start

- Use the network configuration utility like system-config-network to configure the network interfaces.

### VGA Driver Installation

NOTE. The onboard VGA driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

1.     Please change directory to /tmp.

# cd /tmp/

2.      Run the install script to install VGA driver. For 64-bit Linux, please run below command:

# ./auto-update.sh

For 32-bit Linux, please run below command:

# ./auto-update.sh

- After the driver is installed, please restart the X server by pressing “ctrl + alt + backspace” or rebooting the system to take effect.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

NOTE. For RHEL 5 64-bit, it is necessary to install compat-libstdc++ version 33-3.x before installing rpm. Before installing MSM, this RPM is available in the OS DVD

libstdc++-4.4.4-13.el6.i686.rpm

compat-libstdc++-33-3.2.3-69.i686.rpm

libXau-1.0.5-1.el6.i686.rpm

libxcb-1.5-1.el6.i686.rpm

libX11-1.3-2.el6.i686.rpm

libXext-1.1-3.el6.i686.rpm

libXi-1.3-3.el6.i686.rpm

libXtst-1.0.99.2-3.el6.i686.rpm

1.  Install RAID Utility

# cd /tmp/

# ./install.csh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Applications -> System Tools -> MegaRAID Storage Manager StartupUI.

## MegaRAID 9240-4i/9260-8i

Below information describes how to manually install Red Hat Enterprise Linux 5 Update 6 on AR320 F2 with MegaRAID 9240-4i/9260-8i.

### BIOS Required

AR320 F2 BIOS P03 (or later) can support Red Hat Enterprise Linux 5 Update 6

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| MegaRAID 9240-4i/9260-8i | Package 5.4 | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| MegaRAID 9240-4i/9260-8i | Package 5.4 | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-05 | Smart Setup v2.0. |

### Configuring MegaRAID 9240-4i/9260-8i

Please refer to Appendix D for MegaRAID 9240-4i/9260-8i configuration

NOTE. Please copy 9240-4i/9260-8i driver (“megaraid_sas-v00.00.05.40-1-rhel50-u6-all.img”) from Smart Setup DVD to a USB flash drive.

### Installation Tips

1.  Please boot the system from the Red Hat Enterprise Linux 5 Update 6.

2.	When you see the boot menu on the screen, please select Installation and press Esc and type linux dd, then press Enter to continue.

3.  Please select the sda as the Driver Disk Source.

- At Welcome Menu, select Install or upgrade an existing system.

- Follow the instruction for the installation.

- Please Select Software Development Workstation.

- Please follow the normal procedure to finish the installation.

- Boot the system into OS, download and copy the driver to HDD (e.g. /tmp directory).

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

1.  Stop network service

# service network stop

2.  Remove the OS built-in NIC driver

# rmmod e1000e

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf e1000e-<version>.tar.gz

# cd e1000e-<version>/src/

# make install

# modprobe e1000e

- Start the network service to bring up both of the network interfaces.

# service network start

- Use the network configuration utility like system-config-network to configure the network interfaces.

### VGA Driver Installation

NOTE. The onboard VGA driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

1.  Please change directory to /tmp.

# cd /tmp/

2.  Run the install script to install VGA driver. For 64-bit Linux, please run below command:

# ./auto-update.sh

For 32-bit Linux, please run below command:

# ./auto-update.sh

- After the driver is installed, please restart the X server by pressing “ctrl + alt + backspace” or rebooting the system to take effect.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

NOTE. For RHEL 5 64-bit, please install below package first from RHEL 5 64-bit DVD.

libstdc++-4.4.5-6.el6.i686.rpm

compat-libstdc++-33-3.2.3-69.i686.rpm

libXau-1.0.5-1.el6.i686.rpm

libxcb-1.5-1.el6.i686.rpm

libX11-1.3-2.el6.i686.rpm

libXext-1.1-3.el6.i686.rpm

libXi-1.3-3.el6.i686.rpm

libXtst-1.0.99.2-3.el6.i686.rpm

- Install RAID Utility

# cd /tmp/

# ./install.sh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Applications -> System Tools -> MegaRAID Storage Manager StartupUI.

# SuSE Linux Enterprise Server 11 SP1

## LSI Onboard SATA RAID

Below information describes how to manually install SUSE Linux Enterprise Server 11 SP1 on AR320 F2 with LSI Onboard SATA RAID

### BIOS Required

AR320 F2 BIOS P03 (or later) can support SuSE Linux Enterprise Server 11 SP1.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| LSI Onboard SATA RAID | 14.05.0727.2011-1 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| LSI Onboard SATA RAID | 14.05.0727.2011-1 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-05 | Smart Setup v2.0. |

### Configuring Onboard SATA RAID

Please refer to Appendix B for LSI Onboard SATA RAID configuration.

### Installation Tips

NOTE. Please copy LSI Onboard SATA RAID driver to a floppy first before the installation

NOTE. 32-bit SuSE Linux Enterprise Server 11 SP1 does not support OS installation in EFI mode. Please refer appendix D to set RAID controller in Legacy Mode.

- Please boot the system from the SuSE Linux Enterprise Server 11 DVD and follow the instruction to do the installation.

- When you see the boot menu on the screen, please select Installation and type in below command in the text line.

brokenmodules=ahci

- Press F6 and then select Yes for driver loading. Then press Enter to continue.

- At Installation Setting, select the Software.

- Check C/C++ Compiler and Tools under Development to add C/C++ compiler tools.

- Click on Accept and continue the installation.

- Follow the instruction to complete the installation.

- Boot the system into OS, download and copy the driver to HDD (e.g. /tmp directory).

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod e1000e

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf e1000e-<version>.tar.gz

# cd e1000e-<version>/src/

# make install

# modprobe e1000e

- Start the network service to bring up both of the network interfaces.

# service network start

- Network configuration

# YaST2

- Select Network Devices -> Network Settings to configure the network setting.

### VGA Driver Installation

NOTE. The onboard VGA driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

1.     Please change directory to /tmp.

# cd /tmp/

2.      Run the install script to install VGA driver. For 64-bit Linux, please run below command:

# ./auto-update.sh

For 32-bit Linux, please run below command:

# ./auto-update.sh

- After the driver is installed, please restart the X server by pressing “ctrl + alt + backspace” or rebooting the system to take effect.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Install RAID Utility

# cd /tmp/

# ./install.sh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Computer -> More Applications -> System -> MegaRAID Storage Manager StartupUI.

## 3041E-R

Below information describes how to manually install SUSE Linux Enterprise Server 11 SP1 on AR320 F2 with 3041E-R

### BIOS Required

AR320 F2 BIOS P03 (or later) can support SuSE Linux Enterprise Server 11 SP1.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| 3041E-R | 4.26.00.00-1 | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| 3041E-R | 4.26.00.00-1 | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-05 | Smart Setup v2.0. |

### Configuring 3041E-R

Please refer to Appendix C for 3041E-R configuration.

### Installation Tips

NOTE. You need an external USB Flash drive to load RAID driver from Smart Setup DVD

NOTE. 32-bit SuSE Linux Enterprise Server 11 SP1 does not support OS installation in EFI mode. Please refer appendix D to set RAID controller in Legacy Mode.

NOTE. Though SuSE Linux Enterprise Server 11 can detect 3041E-R, please still update the driver after OS is installed.

- Please boot the system from the SuSE Linux Enterprise Server 11 SP1 DVD.

- When you see the boot menu on the screen, please select Installation and press F6 to select Yes. Then press Enter to continue.

- Follow the instruction to load the MegaRAID 3041E-R driver from the driver diskette.

- Follow the instruction to install the OS.

- At the Installation Settings, click on the Software.

- Check C/C++ Compiler and Tools under Development to add C/C++ compiler tools.

- Click on Accept and continue the installation.

- Follow the instruction to complete the installation.

#mkdir /mnt/flash

#mount /dev/sdb1 /mnt/flash

#mount –o loop /mnt/flash/mptlinux-4.26.00.00-1-sles11.XXXX.dd /media/flash

#cd /media/flash/linux/suse/i386-sles11/install (for 32-bit )

#cd /media/flash/linux/suse/x86_64-sles11/install (for 64-bit)

#rpm –ivh lsi-mptlinux-kmp-default-4.26.00.00_2.6.32.12_0.7-1.i586.rpm (for 32-bit)

#rpm –ivh lsi-mptlinux-kmp-default-4.26.00.00_2.6.32.12_0.7-1.x86_64.rpm (for 64-bit)

#cd /

#umount /media/flash

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod e1000e

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf e1000e-<version>.tar.gz

# cd e1000e-<version>/src/

# make install

# modprobe e1000e

- Start the network service to bring up both of the network interfaces.

# service network start

- Network configuration

# YaST2

- Select Network Devices -> Network Settings to configure the network setting.

### VGA Driver Installation

NOTE. The onboard VGA driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

1.     Please change directory to /tmp.

# cd /tmp/

2.      Run the install script to install VGA driver. For 64-bit Linux, please run below command:

# ./auto-update.sh

For 32-bit Linux, please run below command:

# ./auto-update.sh

- After the driver is installed, please restart the X server by pressing “ctrl + alt + backspace” or rebooting the system to take effect.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Install RAID Utility

# cd /tmp/

# ./install.sh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Computer -> More Applications -> System -> MegaRAID Storage Manager StartupUI.

## MegaRAID 9240-4i/9260-8i

Below information describes how to manually install SUSE Linux Enterprise Server 11 SP1 on AR320 F2 with MegaRAID 9240-4i/9260-8i

### BIOS Required

AR320 F2 BIOS P03 (or later) can support SUSE Linux Enterprise Server 11 SP1.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| MegaRAID 9240-4i/9260-8i | Package 5.4 | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| MegaRAID 9240-4i/9260-8i | Package 5.4 | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-05 | Smart Setup v2.0. |

### Configuring MegaRAID 9240-4i/9260-8i

Please refer to Appendix D for MegaRAID 9240-4i/9260-8i configuration.

### Installation Tips

NOTE. 32-bit SuSE Linux Enterprise Server 11 SP1 does not support OS installation in EFI mode. Please refer appendix D to set RAID controller in Legacy Mode.

NOTE. Please make driver diskette of MegaRAID 9240-4i/9260-8i from Smart Setup DVD to a floppy diskette.

NOTE. You need an external USB floppy drive to load RAID driver during the OS installation.

- Please boot the system from the SuSE Linux Enterprise Server 11 SP1 DVD.

- When you see the boot menu on the screen, please select Installation and press F6 to select Yes. Then press Enter to continue.

- Follow the instruction to load the MegaRAID 9240-4i/9260-8i driver from the driver diskette.

- Follow the instruction to install the OS.

- At the Installation Settings, click on the Software.

- Check C/C++ Compiler and Tools under Development to add C/C++ compiler tools.

- Click on Accept and continue the installation.

- Follow the instruction to complete the installation.

- Boot the system into OS, download and copy the driver to HDD (e.g. /tmp directory).

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod e1000e

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf e1000e-<version>.tar.gz

# cd e1000e-<version>/src/

# make install

# modprobe e1000e

- Start the network service to bring up both of the network interfaces.

# service network start

- Network configuration

# YaST2

- Select Network Devices -> Network Settings to configure the network setting.

### VGA Driver Installation

NOTE. The onboard VGA driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

1. Please change directory to /tmp.

# cd /tmp/

2.  Run the install script to install VGA driver. For 64-bit Linux, please run below command:

# ./auto-update.sh

For 32-bit Linux, please run below command:

# ./auto-update.sh

- After the driver is installed, please restart the X server by pressing “ctrl + alt + backspace” or rebooting the system to take effect.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Install RAID Utility

# cd /tmp/

# ./install.sh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

To start the RAID Utility, click on Computer -> More Applications -> System -> MegaRAID Storage Manager StartupUI.

# SuSE Linux Enterprise Server 10 SP4

## LSI Onboard SATA RAID

Below information describes how to manually install SUSE Linux Enterprise Server 10 SP4 on AR320 F2 with LSI Onboard SATA RAID

### BIOS Required

AR320 F2 BIOS P03 (or later) can support SuSE Linux Enterprise Server 10 SP4.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| LSI Onboard SATA RAID | 14.05.0727.2011-1 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| LSI Onboard SATA RAID | 14.05.0727.2011-1 | Smart Setup v2.0 |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-05 | Smart Setup v2.0. |

### Configuring Onboard SATA RAID

Please refer to Appendix B for LSI Onboard SATA RAID configuration.

### Installation Tips

NOTE. Please copy LSI Onboard SATA RAID driver from Smart Setup DVD to a floppy first before the installation

- Please boot the system from the SuSE Linux Enterprise Server 10 DVD and follow the instruction to do the installation.

- When you see the boot menu on the screen, please select Installation and type in below command in the text line.

brokenmodules=ahci

- Press F6 and then select Yes for driver loading. Then press Enter to continue.

- At Installation Setting, select the Software.

- Check C/C++ Compiler and Tools under Development to add C/C++ compiler tools.

- Click on Accept and continue the installation.

- Follow the instruction to complete the installation.

- Boot the system into OS, download and copy the driver to HDD (e.g. /tmp directory).

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod e1000e

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf e1000e-<version>.tar.gz

# cd e1000e-<version>/src/

# make install

# modprobe e1000e

- Start the network service to bring up both of the network interfaces.

# service network start

- Network configuration

# YaST2

- Select Network Devices -> Network Settings to configure the network setting.

### VGA Driver Installation

NOTE. The onboard VGA driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

1.     Please change directory to /tmp.

# cd /tmp/

2.      Run the install script to install VGA driver. For 64-bit Linux, please run below command:

# ./auto-update.sh

For 32-bit Linux, please run below command:

# ./auto-update.sh

- After the driver is installed, please restart the X server by pressing “ctrl + alt + backspace” or rebooting the system to take effect.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Install RAID Utility

# cd /tmp/

# ./install.sh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Computer -> More Applications -> System -> MegaRAID Storage Manager StartupUI.

## 3041E-R

Below information describes how to manually install SUSE Linux Enterprise Server 11 SP1 on AR320 F2 with 3041E-R

### BIOS Required

AR320 F2 BIOS P03 (or later) can support SuSE Linux Enterprise Server 10 SP4.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| 3041E-R | Built-in | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| 3041E-R | Built-in | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-05 | Smart Setup v2.0. |

### Configuring 3041E-R

Please refer to Appendix C for 3041E-R configuration.

### Installation Tips

1.  Please boot the system from the SuSE Linux Enterprise Server 10 SP4 DVD.

2.  When you see the boot menu on the screen, please select Installation and press F6 to select Yes. Then press Enter to continue.

3.  Follow the instruction to load the MegaRAID 3041E-R driver from the driver diskette.

4.  Follow the instruction to install the OS.

5.  At the Installation Settings, click on the Software.

6.  Check C/C++ Compiler and Tools under Development to add C/C++ compiler tools.

7.  Click on Accept and continue the installation.

8.  Follow the instruction to complete the installation.

- Boot the system into OS, download and copy the driver to HDD (e.g. /tmp directory).

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod e1000e

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf e1000e-<version>.tar.gz

# cd e1000e-<version>/src/

# make install

# modprobe e1000e

- Start the network service to bring up both of the network interfaces.

# service network start

- Network configuration

# YaST2

- Select Network Devices -> Network Settings to configure the network setting.

### VGA Driver Installation

NOTE. The onboard VGA driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

1.  Please change directory to /tmp.

# cd /tmp/

2.  Run the install script to install VGA driver. For 64-bit Linux, please run below command:

# ./auto-update.sh

For 32-bit Linux, please run below command:

# ./auto-update.sh

3.  After the driver is installed, please restart the X server by pressing “ctrl + alt + backspace” or rebooting the system to take effect.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Install RAID Utility

# cd /tmp/

# ./install.sh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Computer -> More Applications -> System -> MegaRAID Storage Manager StartupUI.

## MegaRAID 9240-4i/9260-8i

Below information describes how to manually install SUSE Linux Enterprise Server 11 SP1 on AR320 F2 with MegaRAID 9240-4i/9260-8i

### BIOS Required

AR320 F2 BIOS P03 (or later) can support SUSE Linux Enterprise Server 10 SP4.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| MegaRAID 9240-4i/9260-8i | Package 5.4 | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| MegaRAID 9240-4i/9260-8i | Package 5.4 | Smart Setup v2.0. |
| Onboard VGA | Package 0.93 | Smart Setup v2.0. |
| Onboard Gigabit Ethernet | 1.5.1 (Package 16.5) | Smart Setup v2.0. |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 11.06.00-05 | Smart Setup v2.0. |

### Configuring MegaRAID 9240-4i/9260-8i

Please refer to Appendix D for MegaRAID 9240-4i/9260-8i configuration.

### Installation Tips

NOTE. Please refer to AR320 F2 FAQ (Frequently Asked Questions) to select OS installation in EFI mode or Legacy mode if the OS media supports EFI.

NOTE. Please make driver diskette of MegaRAID 9240-4i/9260-8i from Smart Setup DVD to a floppy diskette.

NOTE. You need an external USB floppy drive to load RAID driver during the OS installation.

- Please boot the system from the SuSE Linux Enterprise Server 11 SP1 DVD.

- When you see the boot menu on the screen, please select Installation and press F6 to select Yes. Then press Enter to continue.

- Follow the instruction to load the MegaRAID 9240-4i/9260-8i driver from the driver diskette.

- Follow the instruction to install the OS.

- At the Installation Settings, click on the Software.

- Check C/C++ Compiler and Tools under Development to add C/C++ compiler tools.

- Click on Accept and continue the installation.

- Follow the instruction to complete the installation.

- Boot the system into OS, download and copy the driver to HDD (e.g. /tmp directory).

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod e1000e

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf e1000e-<version>.tar.gz

# cd e1000e-<version>/src/

# make install

# modprobe e1000e

- Start the network service to bring up both of the network interfaces.

# service network start

- Network configuration

# YaST2

- Select Network Devices -> Network Settings to configure the network setting.

### VGA Driver Installation

NOTE. The onboard VGA driver is included in Smart Setup DVD. Please check path of the driver in Windows OS environment first and copy the driver from the Smart Setup DVD to HDD (e.g. /tmp directory)

1.  Please change directory to /tmp.

# cd /tmp/

2.  Run the install script to install VGA driver. For 64-bit Linux, please run below command:

# ./auto-update.sh

For 32-bit Linux, please run below command:

# ./auto-update.sh

3.  After the driver is installed, please restart the X server by pressing “ctrl + alt + backspace” or rebooting the system to take effect.

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Install RAID Utility

# cd /tmp/

# ./install.sh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

To start the RAID Utility, click on Computer -> More Applications -> System -> MegaRAID Storage Manager StartupUI.

# APPENDIX A: Intel onboard SATA RAID CONFIGURATION

## Enabling Intel Onboard SATA RAID

- Turn on the server and the display monitor. If the server is already turned on, please close all open applications and then restart the server.

- Please enter BIOS Setup during POST.

- Please select Advanced.

- Please select SATA Configuration.

- You would see below information:

SATA Controller           [Enabled] 
SATA Mode                 [AHCI Mode]

- Please change SATA Mode from AHCI Mode to RAID Mode

SATA Mode                 [RAID Mode]

- Please specify RAID Mode as Intel RAID

RAID Mode                 [Intel RAID]

- Please save the setting and exit from BIOS Setup.

## Entering Intel onboard SATA RAID BIOS Utility

Please press CTRL-I when you see the RAID BIOS during POST. The Intel(R) Rapid Storage Technology – Option ROM will display on the screen.

## Loading Factory Default Setting

- In the Configuration menu, select third option Reset Disks to Non-RAID. The current adapter settings appear. Please click on Next to change the setting.

- Select the hard disk drive that should be reset and press ENTER to complete your selection.

- Then press Y to reset RAID data on selected hard disks.

## Creating a RAID Volume

- Select Create RAID Volume.

- The CREATE VOLUME MENU displayed.

- Type in the name of RAID volume.

- Select RAID 5 level.

- Select desired HDD to create the RAID.

- Select Create Volume.

- Press Y when “Are you sure you want to create the volume? (Y/N):” displayed.

- Now the RAID volume is created, you can press ESC and select Exit to exit.

## Initializing a RAID Volume

During Intel onboard SATA RAID volume creation process, the Intel onboard SATA RAID volume will be automatically initiated once the onboard SATA RAID volume has been created.

## Assigning a Hot Spare Drive

The Intel onboard SATA RAID BIOS utility does not provide the function to create hot spare drive. Please create the hot spare drive with the Intel onboard SATA RAID utility in operating system.

# APPENDIX B: LSI onboard SATA RAID CONFIGURATION

NOTE. Currently, LSI onboard SATA RAID only supports Legacy mode.

## Enabling LSI Onboard SATA RAID

- Turn on the server and the display monitor. If the server is already turned on, please close all open applications and then restart the server.

- Please enter BIOS Setup during POST.

- Please select Advanced.

- Please select SATA Configuration.

- You would see below information:

SATA Controller           [Enabled] 
SATA Mode                 [AHCI Mode]

- Please change SATA Mode from AHCI Mode to RAID Mode

SATA Mode                 [RAID Mode]

- Please change RAID Mode from Intel RAID to LSI RAID

RAID Mode                 [LSI RAID]

- Please save the setting and exit from BIOS Setup.

## Entering LSI onboard SATA RAID BIOS Utility

Please press Ctrl-M when you see the RAID BIOS during POST.

## Loading Factory default setting

- Select Objects from Management menu.

- Select Adapter from Objects. The selectable adapter will be listed.

- Press Enter on the adapter and the adapter setting will be shown on the screen. You can change the setting from this menu.

- Select Factory Default and YES to load the default settings.

- Exit the configuration utility and press <Ctrl> + <Alt> + <Del> to reboot the server.

## Creating a RAID Volume

- Select Configuration from Management Menu.

- Select New Configuration from the Configuration menu and select YES to continue. An array selection window displays the devices connected to the current controller.

- Press the arrow keys to choose specific physical drives and press spacebar to associate the selected drive with the current array. The indicator for selected drive change from READY to ONLINE

- After adding 2 drives to current array, press <Enter> to finish creating current array.

- Press Enter again to select array to configure.

- Press spacebar to select the array and press <F10> to configure the logical drive.

- The default RAID level for 2 disk drives is RAID1. Just select Accept to use the default setting and press <Enter> to return to the ARRAY SELECTION MENU.

- Press <Enter> to end the array configuration.

- Select YES to Save Configuration and press any key to return to the Configure menu.

## Initializing a RAID Volume

- Press <Esc> to return to the Management Menu.

- Select Initialize from Management menu. All logical drives should be listed under Logical Drives.

- Press <Spacebar> to select drives for initialization. The selected drive will be shown in yellow.

- After selecting the drives, press <F10> and select YES to start the initialization process.

- When initialization is complete, press any <ESC> to continue.

- Press <Esc> again to return to the Management Menu.

## Assigning a Hot Spare Drive

- Select Objects from Management menu.

- Select Physical Drive from Objects. All of the drives will be listed.

- Select a drive marked as READY and press Enter.

- Select Make Hot Spare and press Enter.

- Select Yes then you will see the HDD is changed from READY to HOTSP.

- Press <ESC> to return to the Management Menu.

## Saving and Exiting Onboard RAID Configuration Utility

- When RAID configuration, initialization and assigning hot spare are completed, press <Esc> in the Management Menu and select YES to exit the Software RAID Configuration Utility.

- Press <Ctrl> + <Alt> + <Del> to reboot the server.

- Now you can start to install OS.

# APPENDIX C: 3041E-R RAID CONFIGuration

## Set RAID Controller in Legacy Mode

NOTE. Currently, 3041E-R only supports Legacy mode. Please change PCI ROM Priority setting from EFI Compatible ROM to Legacy ROM in BIOS Setup.

PCI ROM Priority             [Legacy ROM]

## Entering RAID BIOS Utility

Please press CTRL-C when you see the RAID BIOS during POST. After POST finished, the Adapter Selection page will show on the screen.

## Loading Factory Default Setting

- Please press <Alt> + <N> to launch Global Properties.

Select Restore Defaults please press <Enter>.

Press <ESC> select Save changes then exit this menu and press <Enter>.

The setting will change to default.

## Creating a RAID Volume

- Select SAS3041E and press <Enter>.

- Select RAID Properties and press <Enter>.

- Select Create IM Volume to create RAID 1 and press <Enter>.

- Move selection to RAID Disk and press <+>, press <D> to create new array.

- Press <C> to create array.

- Select Save change then exit this menu and press <Enter>

Press <ESC> 2 times and select Exit the configuration Utility and Reboot. Press <Enter>.

## Initializing a RAID Volume

- After you create the array by pressing <C>, it initializes the RAID Volume automatically.

## Assigning a Hot Spare Drive

- Select SAS3041E and press <Enter>.

- Select RAID Properties and press <Enter>.

- Select View Existing Array and press <Enter>.

- Select Manage Array and press <Enter>.

- Select Manage Hot Spares and press <Enter>.

- Move selection to Hot Spr and press <+> .

- Press <C> to commit changes.

- Select Save changes then exit this menu and press <Enter>.

Press <ESC> 4 times and select Exit the configuration Utility and Reboot. Press <Enter>.

# APPENDIX D: mEGARAID  9240-4i/ MEGARAID 9260-8i RAID CONFIGuration

## Set RAID Controller in EFI Mode or Legacy Mode

- Please enter BIOS Setup during POST

Please select Advanced.

Please select PCI Configuration.

You would see below information.

PCI ROM Priority    [EFI Compatible ROM]

NOTE. The default setting is EFI Compatible ROM.

To enable EFI mode of RAID controller, please keep PCI ROM Priority as EFI Compatible ROM. To enable Legacy mode of RAID controller, please change PCI ROM Priority as Legacy ROM.

Please save the setting and exit from BIOS Setup.

## Entering RAID BIOS Utility (Legacy Mode)

Please press CTRL-H when you see the RAID BIOS during POST. After POST finished, the Adapter Selection page will show on the screen. Please click on Start to launch the configuration menu.

## Entering RAID EFI Utility (EFI Mode)

- Please enter EFI shell during POST.

In EFI Shell, please type in drvcfg –s.

You will see below options.

Press 1 for EFI WebBIOS

2 for EFI CLI

or any other key to return:

Please select 1 for EFI WebBIOS.

Please click on Start to launch the configuration menu.

## Loading Factory Default Setting

- In the left panel, select Controller Properties. The current adapter settings appear. Please click on Next to change the setting.

Change the setting of Set Factory Defaults from No to Yes then click on submit.

Press Home button

Please select Exit in left panel

Press Ctrl+Alt+Del to reboot the server.

## Creating a RAID Volume

- Launch the configuration menu.

Select Configuration Wizard in left panel

Select New Configuration and click on Next.

Select Manual Configuration and click on Next.

Hold the Ctrl key and select the drives that you want to add into the array. After you selecting the drives, click on Add to Array.

Click on Accept DG and then click on Next.

Select the array you just created, click on Add to SPAN and then Next.

Select the RAID Level you want to use, create the logical volume by specify the size at Select Size and click on Accept to create the logical volume.

Click on Next after you creating the logical volume.

Click on Accept and Yes to save the configuration.

## Initializing a RAID Volume

- After you create the logical volumes and click on Accept to save the configuration, the new logical volume will be automatically initialized after you click on Yes to confirm the change.

You will see all the logical drives listed.

Click on Home to go back to the configuration menu.

## Assigning a Hot Spare Drive

- Select a free disk marked as UNCONF GOOD and listed under Physical Drives.

Select Make Global HSP or Make Dedicated HSP options and then click on Go.

Click on Home to go back to the configuration menu. You will see the disk marked as Hot Spare in pink and listed under Physical Drives.

Now you can reboot the system and install the Operating System. Select Exit, click on Yes and press Ctrl+Alt+Del to reboot the system.