Version 1.0

September 2012

Revision History

| Ver. | Date | Description |
| --- | --- | --- |
| 1.0 | Sept 25, 2012 | First release |

Contents

Introduction	1

Windows server 2008 R2	2

Intel Onboard SAS/SATA RSTe RAID	2

BIOS Required	2

Drivers Required	2

Software Required	2

Configuring Onboard Intel Onboard SAS/SATA RSTe RAID	2

Installation Tips	2

Chipset Driver Package Installation	3

Gigabit Ethernet Driver Installation	3

VGA Driver Installation	4

InfiniBand Driver Installation (only required for AW170hq F2 and AW170hf F2)	4

RAID Utility Installation	4

Network Utility Installation	5

Intel Onboard SAS/SATA ESRTII RAID	5

BIOS Required	5

Drivers Required	5

Software Required	5

Configuring Intel Onboard SAS/SATA ESRTII RAID	6

Installation Tips	6

Chipset Driver Package Installation	6

Gigabit Ethernet Driver Installation	7

VGA Driver Installation	7

InfiniBand Driver Installation (only required for AW170hq F2 and AW170hf F2)	7

RAID Utility Installation	8

Network Utility Installation	8

Windows Server 2008	9

Intel Onboard SAS/SATA RSTe RAID	9

BIOS Required	9

Drivers Required (64 bit)	9

Drivers Required (32 bit)	9

Software Required	9

Configuring Intel Onboard SAS/SATA RSTe RAID	10

Installation Tips	10

Chipset Driver Package Installation	10

Gigabit Ethernet Driver Installation	11

VGA Driver Installation	11

InfiniBand Driver Installation (only required for AW170hq F2 and AW170hf F2)	11

RAID Utility Installation	12

Network Utility Installation	12

Intel Onboard SAS/SATA ESRTII RAID	12

BIOS Required	12

Drivers Required (64 bit)	13

Drivers Required (32 bit)	13

Software Required	13

Configuring Intel Onboard SAS/SATA ESRTII RAID	13

Installation Tips	13

Chipset Driver Package Installation	14

Gigabit Ethernet Driver Installation	14

VGA Driver Installation	15

InfiniBand Driver Installation (only required for AW170hq F2 and AW170hf F2)	15

RAID Utility Installation	16

Network Utility Installation	16

Red Hat Enterprise Linux 6 UPDATE 2	17

Intel Onboard SAS/SATA ESRTII RAID	17

BIOS Required	17

Drivers Required (64 bit)	17

Drivers Required (32 bit)	17

Software Required	17

Configuring Intel Onboard SAS/SATA ESRTII RAID	17

Installation Tips	17

Gigabit Ethernet Driver Installation	18

VGA Driver Installation	19

InfiniBand Driver Installation (only required for AW170hq F2 and AW170hf F2)	19

RAID Utility Installation	19

Red Hat Enterprise Linux 5 UPDATE 8	21

Intel Onboard SAS/SATA ESRTII RAID	21

BIOS Required	21

Drivers Required (64 bit)	21

Drivers Required (32 bit)	21

Software Required	21

Configuring Intel Onboard SAS/SATA ESRTII RAID	21

Installation Tips	21

Gigabit Ethernet Driver Installation	22

VGA Driver Installation	23

InfiniBand Driver Installation (only required for AW170hq F2 and AW170hf F2)	23

RAID Utility Installation	23

SuSE Linux Enterprise Server 11 SP2	25

Intel Onboard SAS/SATA ESRTII RAID	25

BIOS Required	25

Drivers Required (64 bit)	25

Drivers Required (32 bit)	25

Software Required	25

Configuring Intel Onboard SAS/SATA ESRTII RAID	25

Installation Tips	25

Gigabit Ethernet Driver Installation	26

VGA Driver Installation	27

InfiniBand Driver Installation (only required for AW170hq F2 and AW170hf F2)	27

RAID Utility Installation	28

VMware ESXi 5.0 Update 1	29

Intel Onboard SAS/SATA RSTe w/o RAID	29

BIOS Required	29

Drivers Required	29

Configuring Intel Onboard SAS/SATA RSTe w/o RAID	29

Installation Tips	29

Configure the VMware ESXi 5.0 Update 1 host	30

Downloading the vSphere Client to the PC	30

vSphere Client Installation on the PC	30

Launch vSphere Client on the PC	30

Gigabit Ethernet Driver Installation	32

VGA Driver Installation	32

APPENDIX A: Intel onboard SAS/SATA RSTe RAID CONFIGURATION	33

Enabling Intel Onboard SAS/SATA RSTe RAID	33

Entering Intel onboard SAS/SATA RSTe RAID BIOS Utility	33

Loading Factory Default Setting	33

Creating a RAID Volume	33

Initializing a RAID Volume	34

Assigning a Hot Spare Drive	34

APPENDIX B: Intel onboard SAS/SATA ESRTII RAID CONFIGURATION	35

Enabling Intel Onboard SAS/SATA ESRTII RAID	35

Entering Intel onboard SAS/SATA ESRTII RAID BIOS Utility	35

Loading Factory Default Setting	35

Creating a RAID Volume	35

Initializing a RAID Volume	36

Assigning a Hot Spare Drive	36

Saving and Exiting Intel Onboard SAS/SATA ESRTII RAID Configuration Utility	36

# Introduction

The driver required for installing the OS manually is included in Smart Setup Resource Kit, this document provides you a OS installation guide on AW2000h-AW170h F2 Series, including,

Windows Server 2008 R2

Windows Server 2008

Red Hat Enterprise Linux 6 Update 2

Red Hat Enterprise Linux 5 Update 8

SuSE Linux Enterprise Server 11 SP2

VMware ESXi 5.0 Update 1

# Windows server 2008 R2

## Intel Onboard SAS/SATA RSTe RAID

Below information describes how to manually install Windows Server 2008 R2 on AW2000h-AW170h F2 Series with Intel Onboard SAS/SATA RSTe RAID.

### BIOS Required

AW2000h-AW170h F2 Series BIOS 01.03.0002 (or later) can support Windows Server 2008 R2.

### Drivers Required

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA RSTe RAID | 3.1.0.1082 (Package 3.1.0.1085) | Smart Setup Resource Kit v1.0 |
| Chipset | Package 9.2.3.1022 | Smart Setup Resource Kit v1.0 |
| Onboard VGA | 2.2.1.0 (Package 20110516i) | Smart Setup Resource Kit v1.0 |
| Onboard Gigabit Ethernet | 11.14.48.0 (Package 17.1) | Smart Setup Resource Kit v1.0 |
| InfiniBand | Package 3.0.0 | Download from Mellanox website |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA RSTe RAID Utility | 3.1.0.1068 (Package 3.1.0.1085) | Download form Acer Global Download website |
| PROSet | 17.1.55.0 (Package 17.1) | Smart Setup Resource Kit v1.0 |

### Configuring Intel Onboard SAS/SATA RSTe RAID

Please refer to Appendix A. for Intel Onboard SAS/SATA RSTe RAID configuration.

### Installation Tips

NOTE. Please refer to AW2000h-AW170h F2 Series FAQ (Frequently Asked Questions) to select OS installation in EFI mode or Legacy mode if the OS media supports EFI.

NOTE. Windows Server 2008 R2 cannot detect Intel Onboard SAS/SATA RSTe RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SAS/SATA RSTe RAID driver from Smart Setup Resource Kit DVD to a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Windows Server 2008 R2 DVD. Follow the instructions to do the installation.

- When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Onboard SAS/SATA RSTe RAID driver and click on “Load Driver”.

- Specify the folder iaStorS.free.64bit.3.1.0.1082 that includes the Intel onboard SAS/SATA RSte RAID driver and the system will show the available driver. Select “Intel(R) C600 Series Chipset SAS RAID Controller (C:\isStorS.free.64bit.3.1.1082\iaStorS.inf)” as target driver.

- After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

- Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Chipset Driver by expanding the directory in the following order, AW170hx F2 -> Chipset -> Intel Chipset

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Setup.exe and follow the instructions to complete the driver installation.

- After the installation is completed, reboot the system.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Gigabit Ethernet Driver by expanding the directory in the following order, AW170hx F2 -> Network -> Intel LAN (onboard I350-T2).

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Autorun.exe.

- Follow the instructions, accept the license agreement and use the default setting to complete the driver installation.

- The driver and PROSet utility will be installed together automatically.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup Resource Kit DVD.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Drivers.

- Find the VGA Driver by expanding the directory in the following order, AW170hX F2 -> Graphics -> Nuvoton onboard VGA (Emulex IBMC video).

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Install.bat.

- Accept the license agreement to install the VGA driver.

- After the installation is completed, reboot the system.

- After installing the driver, you would see Matrox G200e (ServerEngines) listed in Display adapters.

### InfiniBand Driver Installation (only required for AW170hq F2 and AW170hf F2)

NOTE. This InfiniBand driver is only required for AW170hq F2 and AW170hf F2. The AW170h F2 does not require InfiniBand driver.

- You can download the InfiniBand driver from Mellanox website (http://www.mellanox.com/downloads/WinOF/MLNX_WinOF_VPI-3_0_0_win7_x64.exe).

- The download link can also be found in Smart Setup Resource Kit DVD.

- After you download the driver, follow the instruction to install the InfiniBand driver.

- When the installation is completed, you can find the InfiniBand tools in the folder below.

C:\Program Files\Mellanox\MLNX_VPI\IB\Tools

### RAID Utility Installation

Note. Before installing Intel RAID Utility, please enable .NET Framework 3.0 (or later) features.

- Please download the Intel Onboard SAS/SATA RSTe RAID utility form Acer Global Download website. (http://www.acer.com/worldwide/support/download.htm)

- Double-click on iata_cd.exe and follow the instruction and use the default setting to install the RAID Utility Installation.

- Reboot the system after the installation completed.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## Intel Onboard SAS/SATA ESRTII RAID

Below information describes how to manually install Windows Server 2008 R2 on AW2000h-AW170h F2 Series with Intel Onboard SAS/SATA ESRTII RAID.

### BIOS Required

AW2000h-AW170h F2 Series BIOS 01.03.0002 (or later) can support Windows Server 2008 R2.

### Drivers Required

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.0.528.2012 | Smart Setup Resource Kit v1.0 |
| Chipset | Package 9.2.3.1022 | Smart Setup Resource Kit v1.0 |
| Onboard VGA | 2.2.1.0 (Package 20110516i) | Smart Setup Resource Kit v1.0 |
| Onboard Gigabit Ethernet | 11.14.48.0 (Package 17.1) | Smart Setup Resource Kit v1.0 |
| InfiniBand | 3.0.0 | Download from Mellanox website |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.01.03.01 | Smart Setup Resource Kit v1.0 |
| PROSet | 17.1.55.0 (Package 17.1) | Smart Setup Resource Kit v1.0 |

### Configuring Intel Onboard SAS/SATA ESRTII RAID

Please refer to Appendix B. for Intel Onboard SAS/SATA ESRTII RAID configuration.

### Installation Tips

NOTE. Please refer to AW2000h-AW170h F2 Series FAQ (Frequently Asked Questions) to select OS installation in EFI mode or Legacy mode if the OS media supports EFI.

NOTE. Windows Server 2008 R2 cannot detect Intel Onboard SAS/SATA ESRTII RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SAS/SATA ESRTII RAID driver from Smart Setup Resource Kit DVD to a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Windows Server 2008 R2 DVD. Follow the instructions to do the installation.

- When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Onboard SAS/SATA ESRTII RAID driver and click on “Load Driver”.

- Specify the folder that includes the Intel onboard SAS/SATA ESRTII RAID driver and the system will show the available driver. Select “Intel Embedded Server RAID Technology II (C:\MegaSR1.inf)” as target driver.

- After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

- Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Chipset Driver by expanding the directory in the following order, AW170hx F2 -> Chipset -> Intel Chipset

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Setup.exe and follow the instructions to complete the driver installation.

- After the installation is completed, reboot the system.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Gigabit Ethernet Driver by expanding the directory in the following order, AW170hx F2 -> Network -> Intel LAN (onboard I350-T2).

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Autorun.exe.

- Follow the instructions, accept the license agreement and use the default setting to complete the driver installation.

- The driver and PROSet utility will be installed together automatically.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup Resource Kit DVD.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Drivers.

- Find the VGA Driver by expanding the directory in the following order, AW170hX F2 -> Graphics -> Nuvoton onboard VGA (Emulex IBMC video).

- Select Windows Server 2008 R2 SP1 then click on Browse.

- Double-click on Install.bat.

- Accept the license agreement to install the VGA driver.

- After the installation is completed, reboot the system.

- After installing the driver, you would see Matrox G200e (ServerEngines) listed in Display adapters.

### InfiniBand Driver Installation (only required for AW170hq F2 and AW170hf F2)

NOTE. This InfiniBand driver is only required for AW170hq F2 and AW170hf F2. The AW170h F2 does not require InfiniBand driver.

- You can download the InfiniBand driver from Mellanox website (http://www.mellanox.com/downloads/WinOF/MLNX_WinOF_VPI-3_0_0_win7_x64.exe).

- The download link can also be found in Smart Setup Resource Kit DVD.

- After you download the driver, follow the instruction to install the InfiniBand driver.

- When the installation is completed, you can find the InfiniBand tools in the folder below.

C:\Program Files\Mellanox\MLNX_VPI\IB\Tools

### RAID Utility Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Utilities.

- Find the Intel onboard SAS/SATA ESRTII RAID Utility by expanding the directory in the following order, AW170hx F2 -> IO Module -> Intel Integrated RAID Module RMS25PB040.

- Select Windows Server 2008 R2 SP1.

- Double-click on Setup.exe.

- Accept the license and follow the instruction to install the RAID Utility. Reboot the system after the installation completed.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

# Windows Server 2008

## Intel Onboard SAS/SATA RSTe RAID

Below information describes how to manually install Windows Server 2008 on AW2000h-AW170h F2 Series with Intel Onboard SAS/SATA RSTe RAID.

### BIOS Required

AW2000h-AW170h F2 Series BIOS 01.03.0002 (or later) is required to support Windows Server 2008.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA RSTe RAID | 3.1.0.1082 (Package 3.1.0.1085) | Smart Setup Resource Kit v1.0 |
| Chipset | Package 9.2.3.1022 | Smart Setup Resource Kit v1.0 |
| Onboard VGA | 2.2.1.0 (Package 20110516i) | Smart Setup Resource Kit v1.0 |
| Onboard Gigabit Ethernet | 11.14.48.0 (Package 17.1) | Smart Setup Resource Kit v1.0 |
| InfiniBand | 3.0.0 | Download from Mellanox website |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA RSTe RAID | 3.1.0.1082 (Package 3.1.0.1085) | Smart Setup Resource Kit v1.0 |
| Chipset | Package 9.2.3.1022 | Smart Setup Resource Kit v1.0 |
| Onboard VGA | 2.2.1.0 (Package 20110516i) | Smart Setup Resource Kit v1.0 |
| Onboard Gigabit Ethernet | 11.14.48.0 (Package 17.1) | Smart Setup Resource Kit v1.0 |
| InfiniBand | 3.0.0 | Download from Mellanox website |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA RSTe RAID Utility | 3.1.0.1068 (Package 3.1.0.1085) | Download form Acer Global Download website |
| PROSet | 17.1.55.0 (Package 17.1) | Smart Setup Resource Kit v1.0 |

### Configuring Intel Onboard SAS/SATA RSTe RAID

Please refer to Appendix A. for Intel Onboard SAS/SATA RSTe RAID configuration.

### Installation Tips

NOTE. Please refer to AW2000h-AW170h F2 Series FAQ (Frequently Asked Questions) to select OS installation in EFI mode or Legacy mode if the OS media supports EFI.

NOTE. Windows Server 2008 cannot detect Intel Onboard SAS/SATA RSTe RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SAS/SATA RSTe RAID driver from Smart Setup Resource Kit DVD to a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Windows Server 2008 DVD. Follow the instructions to do the installation.

- When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Onboard SAS/SATA RSTe RAID driver and click on “Load Driver”.

- Specify the folder (iaStorS.free.64bit.3.1.0.1082 for 64-bit Windows Server 2008 and iaStorS.free.32bit.3.1.0.1082 for 32-bit Windows Server 2008) that includes the Intel onboard SAS/SATA RSte RAID driver and the system will show the available driver.

- Select “Intel(R) C600 Series Chipset SAS RAID Controller (C:\isStorS.free.64bit.3.1.1082\iaStorS.inf)” for 64-bit Windows Server 2008 and “Intel(R) C600 Series Chipset SAS RAID Controller (C:\isStorS.free.64bit.3.1.1082\iaStorS.inf)” for 32-bit Windows Server 2008 as target driver.

- After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

- Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Chipset Driver by expanding the directory in the following order, AW170hx F2 -> Chipset -> Intel Chipset

- Select Windows Server 2008 SP2 (32-bit/64-bit) then click on Browse.

- Double-click on Setup.exe and follow the instructions to complete the driver installation.

- After the installation is completed, reboot the system.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Gigabit Ethernet Driver by expanding the directory in the following order, AW170hx F2 -> Network -> Intel LAN (onboard I350-T2).

- Select Windows Server 2008 SP2 (32-bit/64-bit) then click on Browse.

- Double-click on Autorun.exe.

- Follow the instructions, accept the license agreement and use the default setting to complete the driver installation.

- The driver and PROSet utility will be installed together automatically.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup Resource Kit DVD.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Drivers.

- Find the VGA Driver by expanding the directory in the following order, AW170hX F2 -> Graphics -> Nuvoton onboard VGA (Emulex IBMC video).

- Select Windows Server 2008 SP2 (32-bit/64-bit) then click on Browse.

- Double-click on Install.bat.

- Accept the license agreement to install the VGA driver.

- After the installation is completed, reboot the system.

- After installing the driver, you would see Matrox G200e (ServerEngines) listed in Display adapters.

### InfiniBand Driver Installation (only required for AW170hq F2 and AW170hf F2)

NOTE. This InfiniBand driver is only required for AW170hq F2 and AW170hf F2. The AW170h F2 does not require InfiniBand driver.

- You can download the InfiniBand driver from Mellanox website:

For 64-bit:

http://www.mellanox.com/downloads/WinOF/MLNX_WinOF_VPI-3_0_0_wlh_x64.exe

For 32-bit:

http://www.mellanox.com/downloads/WinOF/MLNX_WinOF_VPI-3_0_0_wlh_x86.exe

- The download link can also be found in Smart Setup Resource Kit DVD.

- After you download the driver, follow the instruction to install the InfiniBand driver.

- When the installation is completed, you can find the InfiniBand tools in the folder below.

C:\Program Files\Mellanox\MLNX_VPI\IB\Tools

### RAID Utility Installation

Note. Before installing Intel RAID Utility, please enable .NET Framework 3.0 (or later) features.

- Please download the Intel Onboard SAS/SATA RSTe RAID utility form Acer Global Download website. (http://www.acer.com/worldwide/support/download.htm)

- Double-click on iata_cd.exe and follow the instruction and use the default setting to install the RAID Utility Installation.

- Reboot the system after the installation completed.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## Intel Onboard SAS/SATA ESRTII RAID

Below information describes how to manually install Windows Server 2008 on AW2000h-AW170h F2 Series with Intel Onboard SAS/SATA ESRTII RAID.

### BIOS Required

AW2000h-AW170h F2 Series BIOS 01.03.0002 (or later) can support Windows Server 2008.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.0.528.2012 | Smart Setup Resource Kit v1.0 |
| Chipset | Package 9.2.3.1022 | Smart Setup Resource Kit v1.0 |
| Onboard VGA | 2.2.1.0 (Package 20110516i) | Smart Setup Resource Kit v1.0 |
| Onboard Gigabit Ethernet | 11.14.48.0 (Package 17.1) | Smart Setup Resource Kit v1.0 |
| InfiniBand | 3.0.0 | Download from Mellanox website |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.0.528.2012 | Smart Setup Resource Kit v1.0 |
| Chipset | Package 9.2.3.1022 | Smart Setup Resource Kit v1.0 |
| Onboard VGA | 2.2.1.0 (Package 20110516i) | Smart Setup Resource Kit v1.0 |
| Onboard Gigabit Ethernet | 11.14.48.0 (Package 17.1) | Smart Setup Resource Kit v1.0 |
| InfiniBand | 3.0.0 | Download from Mellanox website |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.01.03.01 | Smart Setup Resource Kit v1.0 |
| PROSet | 17.1.55.0 (Package 17.1) | Smart Setup Resource Kit v1.0 |

### Configuring Intel Onboard SAS/SATA ESRTII RAID

Please refer to Appendix B. for Intel Onboard SAS/SATA ESRTII RAID configuration.

### Installation Tips

NOTE. Windows Server 2008 cannot detect Intel Onboard SAS/SATA ESRTII RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SAS/SATA ESRTII RAID driver from Smart Setup Resource Kit DVD to a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Windows Server 2008 DVD. Follow the instructions to do the installation.

- When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Onboard SAS/SATA RSTEII RAID driver and click on “Load Driver”.

- Specify the folder that includes the Intel onboard SAS/SATA ESRTIIR RAID driver and the system will show the available driver. Select “Intel Embedded Server RAID Technology II (C:\MegaSR1.inf)” as target driver.

- After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

- Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Chipset Driver by expanding the directory in the following order, AW170hx F2 -> Chipset -> Intel Chipset

- Select Windows Server 2008 SP2 (32-bit/64-bit) then click on Browse.

- Double-click on Setup.exe and follow the instructions to complete the driver installation.

- After the installation is completed, reboot the system.

### Gigabit Ethernet Driver Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive

- Select model and click on Drivers.

- Find the Gigabit Ethernet Driver by expanding the directory in the following order, AW170hx F2 -> Network -> Intel LAN (onboard I350-T2).

- Select Windows Server 2008 SP2 (32-bit/64-bit) then click on Browse.

- Double-click on Autorun.exe.

- Follow the instructions, accept the license agreement and use the default setting to complete the driver installation.

- The driver and PROSet utility will be installed together automatically.

### VGA Driver Installation

NOTE. Windows will treat onboard VGA as Standard VGA device. Please install onboard VGA driver from Smart Setup Resource Kit DVD.

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Drivers.

- Find the VGA Driver by expanding the directory in the following order, AW170hX F2 -> Graphics -> Nuvoton onboard VGA (Emulex IBMC video).

- Select Windows Server 2008 SP2 (32-bit/64-bit) then click on Browse.

- Double-click on Install.bat.

- Accept the license agreement to install the VGA driver.

- After the installation is completed, reboot the system.

- After installing the driver, you would see Matrox G200e (ServerEngines) listed in Display adapters.

### InfiniBand Driver Installation (only required for AW170hq F2 and AW170hf F2)

NOTE. This InfiniBand driver is only required for AW170hq F2 and AW170hf F2. The AW170h F2 does not require InfiniBand driver.

- You can download the InfiniBand driver from Mellanox website:

For 64-bit:

http://www.mellanox.com/downloads/WinOF/MLNX_WinOF_VPI-3_0_0_wlh_x64.exe

For 32-bit:

http://www.mellanox.com/downloads/WinOF/MLNX_WinOF_VPI-3_0_0_wlh_x86.exe

- The download link can also be found in Smart Setup Resource Kit DVD.

- After you download the driver, follow the instruction to install the InfiniBand driver.

- When the installation is completed, you can find the InfiniBand tools in the folder below.

C:\Program Files\Mellanox\MLNX_VPI\IB\Tools

### RAID Utility Installation

- Please insert the Smart Setup Resource Kit DVD into the optical drive.

- Select model and click on Utilities.

- Find the Intel onboard SAS/SATA ESRTII RAID Utility by expanding the directory in the following order, AW170hx F2 -> IO Module -> Intel Integrated RAID Module RMS25PB040.

- Select Windows Server 2008 SP2 (64-bit/32-bit).

- Double-click on Setup.exe.

- Accept the license and follow the instruction to install the RAID Utility. Reboot the system after the installation completed.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

# Red Hat Enterprise Linux 6 UPDATE 2

## Intel Onboard SAS/SATA ESRTII RAID

Below information describes how to manually install Red Hat Enterprise Linux 6 Update 2 on AW2000h-AW170h F2 Series with Intel Onboard SAS/SATA ESRTII RAID.

### BIOS Required

AW2000h-AW170h F2 Series BIOS 01.03.0002 (or later) is required to support Red Hat Enterprise Linux 6 Update 2.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.00.0528.2012 | Smart Setup Resource Kit v1.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 3.4.7 (Package 17.1) | Smart Setup Resource Kit v1.0. |
| InfiniBand | 1.5.3-3.0.0 | Download from Mellanox Website |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.00.0528.2012 | Smart Setup Resource Kit v1.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 3.4.7 (Package 17.1) | Smart Setup Resource Kit v1.0. |
| InfiniBand | 1.5.3-3.0.0 | Download from Mellanox Website |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.01.03.01 | Smart Setup Resource Kit v1.0. |

### Configuring Intel Onboard SAS/SATA ESRTII RAID

Please refer to Appendix B. for Intel Onboard SAS/SATA ESRTII RAID configuration

### Installation Tips

NOTE. Red Hat Enterprise Linux 6 Update 2 cannot detect Intel Onboard SAS/SATA ESRTII RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SAS/SATA ESRTII RAID driver (DUDs\megasr-15.00.0528.2012-1-rhel62-ga-x86_64.img for 64-bit and DUDs\megasr-15.00.0528.2012-1-rhel62-ga-x86.img for 32-bit) from Smart Setup Resource Kit DVD onto a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Red Hat Enterprise Linux 6 Update 2.

- At Welcome Menu, Please press ESC and type below command. Then press Enter to continue.

linux dd

- Follow the instruction to select the Driver Disk Source to load the driver for Intel Onboard SAS/SATA ESRTII RAID.

- Follow the instruction and select Intel MegaSR as the install target device for the installation.

- Please Select Software Development Workstation.

- Please follow the normal procedure to finish the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup Resource Kit DVD. Please check path of the RAID utility in Windows OS environment first and copy the driver from the Smart Setup Resource Kit DVD to HDD (e.g. \PRO1000\LINUX\igb-<version>.tar.gz to /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod igb

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf igb-<version>.tar.gz

# cd igb-<version>/src/

# make install

# modprobe igb

- Start the network service to bring up both of the network interfaces.

# service network start

- Use the network configuration utility like system-config-network in command line or select System -> Preferences-> Network Connections in GUI to configure the network interfaces.

### VGA Driver Installation

Red Hat Enterprise Linux 6 Update 2 has the built-in driver for onboard VGA. You don’t need to install the VGA driver manually.

### InfiniBand Driver Installation (only required for AW170hq F2 and AW170hf F2)

NOTE. This InfiniBand driver is only required for AW170hq F2 and AW170hf F2. The AW170h F2 does not require InfiniBand driver.

NOTE. For RHEL 6.2, please install below package first from RHEL 6.2 DVD.

tcl-8.5.7-6

tk-8.5.7-5

- You can download the InfiniBand driver from Mellanox website:

For 64-bit:

http://www.mellanox.com/downloads/ofed/MLNX_OFED_LINUX-1.5.3-3.0.0-rhel6.2-x86_64.tgz

For 32-bit

http://www.mellanox.com/downloads/ofed/MLNX_OFED_LINUX-1.5.3-3.0.0-rhel6.2-i686.tgz

- Extract the downloaded driver.

# tar zxvf MLNX_OFED_LINUX-<version>.tgz

- Install the InfiniBand driver

# cd MLNX_OFED_LINUX-<version>

# ./mlnxofedinstall

- Follow the instruction to complete the installation

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup Resource Kit DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup Resource Kit DVD to HDD (e.g. /tmp directory)

NOTE. For RHEL 6.2 64-bit, please install below package first from RHEL 6.2 64-bit DVD.

libstdc++-4.4.6-3.el6.i686.rpm

compat-libstdc++-33-3.2.3-69.i686.rpm

libXau-1.0.5-1.el6.i686.rpm

libxcb-1.5-1.el6.i686.rpm

libX11-1.3-2.el6.i686.rpm

libXext-1.1-3.el6.i686.rpm

libXi-1.3-3.el6.i686.rpm

libXtst-1.0.99.2-3.el6.i686.rpm

- Install RAID Utility

# cd /tmp/

# ./install.csh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Applications -> System Tools -> RAID Web Console 2 StartupUI.

# Red Hat Enterprise Linux 5 UPDATE 8

## Intel Onboard SAS/SATA ESRTII RAID

Below information describes how to manually install Red Hat Enterprise Linux 5 Update 8 on AW2000h-AW170h F2 Series with Intel Onboard SAS/SATA ESRTII RAID.

### BIOS Required

AW2000h-AW170h F2 Series BIOS 01.03.0002 (or later) is required to support Red Hat Enterprise Linux 5 Update 8.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.00.0528.2012 | Smart Setup Resource Kit v1.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 3.4.7 (Package 17.1) | Smart Setup Resource Kit v1.0. |
| InfiniBand | 1.5.3-3.0.0 | Download from Mellanox Website |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.00.0528.2012 | Smart Setup Resource Kit v1.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 3.4.7 (Package 17.1) | Smart Setup Resource Kit v1.0. |
| InfiniBand | 1.5.3-3.0.0 | Download from Mellanox Website |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.01.03.01 | Smart Setup Resource Kit v1.0. |

### Configuring Intel Onboard SAS/SATA ESRTII RAID

Please refer to Appendix B. for Intel Onboard SAS/SATA ESRTII RAID configuration.

### Installation Tips

NOTE. Red Hat Enterprise Linux 5 Update 8 cannot detect Intel Onboard SAS/SATA ESRTII RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SAS/SATA ESRTII RAID driver (DUDs\megasr-15.00.0528.2012-1-rhel50-U8-64.img for 64-bit and DUDs\megasr-15.00.0528.2012-1-rhel50-U8-32.img for 32-bit) from Smart Setup Resource Kit DVD onto a floppy diskette or USB flash drive.

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB floppy/flash drive and USB optical drive connected.

- Please boot the system from the Red Hat Enterprise Linux 5 Update 8.

- When the prompt boot: appears on the screen, please type linux dd then press Enter to continue.

- Follow the instruction to select the Driver Disk Source to load the driver for Intel Onboard SAS/SATA ESRTII RAID.

- Follow the instruction and select Intel MegaSR as the install target device for the installation.

- At the package selection step, select Software Development for the installation package.

- Please follow the normal procedure to finish the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup Resource Kit DVD. Please check path of the RAID utility in Windows OS environment first and copy the driver from the Smart Setup Resource Kit DVD to HDD (e.g. \PRO1000\LINUX\igb-<version>.tar.gz  to /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod igb

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf igb-<version>.tar.gz

# cd igb-<version>/src/

# make install

# modprobe igb

- Start the network service to bring up both of the network interfaces.

# service network start

- Use the network configuration utility like system-config-network in command line or select System -> Preferences-> Network Connections in GUI to configure the network interfaces.

### VGA Driver Installation

Red Hat Enterprise Linux 5 Update 8 has the built-in driver for onboard VGA. You don’t need to install the VGA driver manually.

### InfiniBand Driver Installation (only required for AW170hq F2 and AW170hf F2)

NOTE. This InfiniBand driver is only required for AW170hq F2 and AW170hf F2. The AW170h F2 does not require InfiniBand driver.

- You can download the InfiniBand driver from Mellanox website:

For 64-bit:

http://www.mellanox.com/downloads/ofed/MLNX_OFED_LINUX-1.5.3-3.0.0-rhel5.8-x86_64.tgz

For 32-bit

http://www.mellanox.com/downloads/ofed/MLNX_OFED_LINUX-1.5.3-3.0.0-rhel5.8-i686.tgz

- Extract the downloaded driver.

# tar zxvf MLNX_OFED_LINUX-<version>.tgz

- Install the InfiniBand driver

# cd MLNX_OFED_LINUX-<version>

# ./mlnxofedinstall

- Follow the instruction to complete the installation

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup Resource Kit DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

NOTE. For RHEL 5, please install below package first from RHEL 5 DVD.

compat-libstdc++ version 33-3.x

- Install RAID Utility

# cd /tmp/

# ./install.csh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Applications -> System Tools -> RAID Web Console 2 StartupUI.

# SuSE Linux Enterprise Server 11 SP2

## Intel Onboard SAS/SATA ESRTII RAID

Below information describes how to manually install SUSE Linux Enterprise Server 11 SP2 on AW2000h-AW170h F2 series with Intel Onboard SAS/SATA ESRTII RAID.

### BIOS Required

AW2000h-AW170h F2 Series BIOS 01.03.0002 (or later) is required to support SUSE Linux Enterprise Server 11 SP2.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.00.0528.2012 | Smart Setup Resource Kit v1.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 3.4.7 (Package 17.1) | Smart Setup Resource Kit v1.0. |
| InfiniBand | 1.5.3-3.0.0 | Download from Mellanox Website |

### Drivers Required (32 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA ESRTII RAID | 15.00.0528.2012 | Smart Setup Resource Kit v1.0. |
| Onboard VGA | N/A | OS Built-in |
| Onboard Gigabit Ethernet | 3.4.7 (Package 17.1) | Smart Setup Resource Kit v1.0. |
| InfiniBand | 1.5.3-3.0.0 | Download from Mellanox Website |

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel RAID Web Console 2 | 12.01.03.01 | Smart Setup Resource Kit v1.0. |

### Configuring Intel Onboard SAS/SATA ESRTII RAID

Please refer to Appendix B for Intel Onboard SAS/SATA ESRTII RAID configuration

### Installation Tips

NOTE. SUSE Linux Enterprise Server 11 SP2 cannot detect Intel Onboard SAS/SATA ESRTII RAID. Please load the RAID driver during OS installation.

NOTE. You need an USB Flash drive to load RAID driver during the OS installation.

NOTE. Please copy Intel Onboard SAS/SATA ESRTII RAID driver (DUDs\megasr-15.00.0528.2012-1-sles11-sp2-x86_64.img for 64-bit and DUDs\megasr-15.00.0528.2012-1- sles11-sp2-x86.img for 32-bit) from Smart Setup Resource Kit DVD and then write the .img onto an USB flash drive. The steps of write the .img file driver into USB flash drive as below.

  - Copy the image file to any linux system.

  - Create a directory ex: "mkdir image"

  - Mount the dud image file to image directory using the below command.

"mount –o loop megasr-15.00.0528.2012-1-sles11-sp2-XXX.img image"

  - Change the directory to image ("cd image").

  - Copy the contents of the image directory into USB drive. (Contents of the image starts with 01 directory, copy the 01 directory to USB Drive)

NOTE. For OS installation, a USB optical drive is required as well. Please prepare a USB Hub to have USB keyboard, USB mouse, USB flash drive and USB optical drive connected.

- Please boot the system from the SuSE Linux Enterprise Server 11 SP2 DVD.

- When you see the boot menu on the screen, please select Installation and press F6 to select Yes. Then press Enter to continue.

- Follow the instruction to load the driver for Intel Onboard SAS/SATA ESRTII RAID.

- Press back to boot the system.

- Follow the instruction to install the OS.

- At the Installation Settings, click on the Software.

- Check C/C++ Compiler and Tools under Development to add C/C++ compiler tools.

- Click on Accept and continue the installation.

- Follow the instruction to complete the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in Smart Setup Resource Kit DVD. Please check path of the RAID utility in Windows OS environment first and copy the driver from the Smart Setup Resource Kit DVD to HDD (e.g. \PRO1000\LINUX\igb-<version>.tar.gz  to /tmp directory)

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod igb

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf igb-<version>.tar.gz

# cd igb-<version>/src/

# make install

# modprobe igb

- Start the network service to bring up both of the network interfaces.

# service network start

- Network configuration

# YaST2

- Select Network Devices -> Network Settings to configure the network setting.

### VGA Driver Installation

SUSE Linux Enterprise Server 11 SP2 has the built-in driver for onboard VGA. You don’t need to install the VGA driver manually.

### InfiniBand Driver Installation (only required for AW170hq F2 and AW170hf F2)

NOTE. This InfiniBand driver is only required for AW170hq F2 and AW170hf F2. The AW170h F2 does not require InfiniBand driver.

- You can download the InfiniBand driver from Mellanox website:

For 64-bit:

http://www.mellanox.com/downloads/ofed/MLNX_OFED_LINUX-1.5.3-3.0.0-sles11sp2-x86_64.tgz

For 32-bit

http://www.mellanox.com/downloads/ofed/MLNX_OFED_LINUX-1.5.3-3.0.0-sles11sp2-i686.tgz

- Extract the downloaded driver.

# tar zxvf MLNX_OFED_LINUX-<version>.tgz

- Install the InfiniBand driver

# cd MLNX_OFED_LINUX-<version>

# ./mlnxofedinstall

- Follow the instruction to complete the installation

### RAID Utility Installation

NOTE. The RAID utility is included in Smart Setup Resource Kit DVD. Please check path of the RAID utility in Windows OS environment first and copy the RAID utility from the Smart Setup DVD to HDD (e.g. /tmp directory)

- Install RAID Utility

# cd /tmp/

# ./install.csh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Computer -> More Applications ->  System -> RAID Web Console 2 StartupUI.

# VMware ESXi 5.0 Update 1

## Intel Onboard SAS/SATA RSTe w/o RAID

Below information describes how to manually install VMware ESXi 5.0 update 1 on AW2000h-AW170h F2 with Intel onboard SAS/SATA RSTe w/o RAID.

### BIOS Required

AW2000h-AW170h F2 BIOS 01.03.0002 (or later) is required to support VMware ESXi 5.0 update 1.

### Drivers Required

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS/SATA RSTe w/o RAID | 2.0.2.0088 | OS built-in |
| Onboard VGA | N/A | OS built-in |
| Onboard Gigabit Ethernet | 2.1.11.1 | OS built-in |

### Configuring Intel Onboard SAS/SATA RSTe w/o RAID

Please refer to Appendix A to enable Intel Onboard SAS/SATA RSTe and do not configure RAID.

### Installation Tips

NOTE. Please use the built-in driver of VMware ESXi 5.0 Update 1 to install the OS.

NOTE. Please enable the Intel Virtualization Technology in BIOS before installation.

- Boot the system with VMware ESXi 5.0 Update 1 installation CD

- Select ESXi-5.0.0-20120302001-standard Installer from the boot menu.

- At the Welcome screen, press Enter to continue with the installation.

- Accept VMware license by pressing F11.

- At the Select a Disk screen, select the disk drive on which to install ESXi 5.0 update 1 and press Enter.

- Follow the instructions to select the keyboard layout, root password.

- At Confirm Install screen, press F11 to start the installation.

- When the installation is completed, press Enter to reboot the host. Please remove the installation CD before the host rebooted.

### Configure the VMware ESXi 5.0 Update 1 host

- When the installation is completed, reboot the host into VMware ESXi 5.0 update 1.

- Press F2 t configure the host.

- Select Configure Management Network to set IP address.

- Select the network adapter which you want to configure in Network Adapters and set the IP address in IP configuration.

- Press ESC when complete the configuration.

- Press Y to save the change.

### Downloading the vSphere Client to the PC

The vSphere Client is a Windows program that you can use to configure the host and to manage virtual machines.

- On a Windows-based PC, please launch the web browser.

- Please use the browser to connect to IP address of AW2000h-AW170h F2 server which is installed with VMware ESXi 5.0 update 1.

- At the welcome page, please click Download the vSphere Client under Getting Started (This will redirect you to VMware website to download the vSphere Client).

### vSphere Client Installation on the PC

NOTE. The vSphere Client requires the Microsoft .NET Framwork 3.5 SP1. If it is not installed, the vSphere Client installer will install it. The Microsoft .NET Framwork 3.5 SP1 installation might require Internet connectivity.

- To install the vSphere Client on the PC by double-clicking the downloaded VMware-vicient.exe file.

- Choose a language for the installer and click OK.

- Follow the instructions and accept the license agreement to complete the installation.

### Launch vSphere Client on the PC

- Open vSphere Client on the PC.

- Type in the information to login VMware ESXi 5.0

- IP address of AW2000h-AW170h F2 which is installed with VMware ESXi 5.0 update

- User name (“root” by default)

- Password (set during the VMware ESXi 5.0 update 1 installation)

- When you see the Security Warning pop-up window, please check the checkbox for Install this certificate and do not display any security warnings for “IP address/Name of your system” and click on Ignore.

- Now, you can manage the VMware ESXi 5.0 update 1 or create virtual machines with the vSphere Client.

### Gigabit Ethernet Driver Installation

VMwaer ESXi 5.0 update 1 has the built-in driver for onboard NIC. You don’t need to install the onboard NIC driver manually.

### VGA Driver Installation

VMwaer ESXi 5.0 update 1 has the built-in driver for onboard VGA. You don’t need to install the VGA driver manually.

# APPENDIX A: Intel onboard SAS/SATA RSTe RAID CONFIGURATION

## Enabling Intel Onboard SAS/SATA RSTe RAID

- Enter BIOS Setup by Press F2 during POST

- Load default BIOS settings by press F9.

- In BIOS Main Page, change Quiet Boot from Enabled to Disabled.

- Select Advanced.

- Select Mass Storage Controller Configuration

- You might see below information:

SAS/SATA Capable Controller       [INTEL(R) RSTe]

- Make sure the setting of SAS/SATA Capable Controller is Intel (R) RSTe.

- Save the setting and exit from BIOS Setup

## Entering Intel onboard SAS/SATA RSTe RAID BIOS Utility

Please press CTRL-I when you see the RAID BIOS during POST.

## Loading Factory Default Setting

The Intel onboard SAS/SATA RSTe RAID BIOS utility does not provide the function to load factory default setting.

## Creating a RAID Volume

- Select Create RAID Volume.

- The CREATE VOLUME MENU displayed.

- Type in the name of RAID volume.

- Select RAID level.

- Select desired HDD to create the RAID.

- Select Strip Size.

- Select Capacity.

- Select Create Volume.

- Press Y when “Are you sure you want to create the volume? (Y/N):” displayed.

- Now the RAID volume is created, you can press ESC and select Exit to exit.

## Initializing a RAID Volume

During Intel onboard SAS/SATA RSTe RAID volume creation process, the Intel onboard SAS/SATA RSTe RAID volume will be automatically initiated once the onboard SAS/SATA RSTe RAID volume has been created.

## Assigning a Hot Spare Drive

The Intel onboard SAS RAID BIOS utility does not provide the function to create hot spare drive. Please create the hot spare drive with the Intel onboard SAS/SATA RSTe RAID utility in operating system.

# APPENDIX B: Intel onboard SAS/SATA ESRTII RAID CONFIGURATION

## Enabling Intel Onboard SAS/SATA ESRTII RAID

- Enter BIOS Setup by Press F2 during POST

- Load default BIOS settings by press F9.

- In BIOS Main Page, change Quiet Boot from Enabled to Disabled.

- Select Advanced.

- Select Mass Storage Controller Configuration

- You might see below information:

SAS/SATA Capable Controller       [INTEL(R) RSTe]

- Make sure the setting of SAS/SATA Capable Controller is INTEL ESRT2 (LSI*).

- Save the setting and exit from BIOS Setup

## Entering Intel onboard SAS/SATA ESRTII RAID BIOS Utility

Please press CTRL-E when you see the RAID BIOS during POST.

## Loading Factory Default Setting

- Select Objects from Management menu.

- Select Adapter from Objects. The selectable adapter will be listed.

- Press Enter on the adapter and the adapter setting will be shown on the screen. You can change the setting from this menu.

- Select Factory Default and Yes to load the default settings.

- Exit the configuration utility and press Ctrl + Alt + Del to reboot the server.

## Creating a RAID Volume

- Select Configuration from Management Menu.

- Select New Configuration from the Configuration menu and select Yes to continue. An array selection window displays the devices connected to the current controller.

- Press the arrow keys to choose specific physical drives and press SPACE key to associate the selected drive with the current array. The indicator for selected drive change from READY to ONLINE

- After adding 2 drives to current array, press Enter to finish creating current array.

- Press Enter again to select array to configure.

- Press SPACE key to select the array and press F10 to configure the logical drive.

- The default RAID level for 2 disk drives is RAID1. Just select Accept to use the default setting and press Enter to return to the ARRAY SELECTION MENU.

- Press Enter to end the array configuration.

- Select Yes to Save Configuration and press any key to return to the Configure menu.

## Initializing a RAID Volume

- Press Esc to return to the Management Menu.

- Select Initialize from Management menu. All logical drives should be listed under Logical Drives.

- Press SPACE key to select drives for initialization. The selected drive will be shown in yellow.

- After selecting the drives, press F10 and select YES to start the initialization process.

- When initialization is complete, press any Esc to continue.

- Press Esc again to return to the Management Menu.

## Assigning a Hot Spare Drive

- Select Objects from Management menu.

- Select Physical Drive from Objects. All of the drives will be listed.

- Select a drive marked as READY and press Enter.

- Select Make Hot Spare and press Enter.

- Select Yes then you will see the HDD is changed from READY to HOTSP.

- Press Esc to return to the Management Menu.

## Saving and Exiting Intel Onboard SAS/SATA ESRTII RAID Configuration Utility

- When RAID configuration, initialization and assigning hot spare are completed, press Esc in the Management Menu and select Yes to exit the Software RAID Configuration Utility.

- Press Ctrl + Alt + Del to reboot the server.

- Now you can start to install OS.