Version 1.1

October 2013

Revision History

| Ver. | Date | Description |
| --- | --- | --- |
| 1.0 | Jul 12, 2013 | First release |
| 1.1 | Oct 2, 2013 | Added OS Installation with MegaRAID 9240-4i/9260-4i/9260-8i |

Contents

Introduction	1

Windows 8	2

Intel Onboard SAS RAID (SATA Mode)	2

BIOS Required	2

Drivers Required (64-bit)	2

Software Required	2

Configuring Intel Onboard SAS RAID (SATA Mode)	2

Installation Tips	2

Chipset Driver Package Installation	3

Gigabit Ethernet Driver Installation	3

Graphics Card Driver Installation	4

TPM Driver Installation (Optional)	4

Audio Driver Installation	4

USB 3.0 Driver Installation	4

RAID Utility Installation	4

Network Utility Installation	4

Intel Onboard SATA RAID	4

BIOS Required	4

Drivers required (64-bit)	5

Software Required	5

Configuring Intel Onboard SATA RAID	5

Installation Tips	5

Chipset Driver Package Installation	6

Gigabit Ethernet Driver Installation	6

Graphics Card Driver Installation	6

TPM Driver Installation (Optional)	7

Audio Driver Installation	7

USB 3.0 Driver Installation	7

RAID Utility Installation	7

Network Utility Installation	7

MegaRAID 9240-4i/9260-4i/9260-8i	7

BIOS Required	7

Drivers required (64-bit)	7

Software Required	8

Configuring MegaRAID 9240-4i/9260-4i/9260-8i	8

Installation Tips	8

Chipset Driver Package Installation	9

Gigabit Ethernet Driver Installation	9

Graphics Card Driver Installation	9

TPM Driver Installation (Optional)	9

Audio Driver Installation	9

USB 3.0 Driver Installation	9

RAID Utility Installation	10

Network Utility Installation	10

Windows 7 SP1	11

Intel Onboard SAS RAID (SATA Mode)	11

BIOS Required	11

Drivers required (64-bit)	11

Software Required	11

Configuring Intel Onboard SAS RAID (SATA Mode)	11

Installation Tips	11

Chipset Driver Package Installation	12

Gigabit Ethernet Driver Installation	12

Graphics Card Driver Installation	12

TPM Driver Installation (Optional)	13

Audio Driver Installation	13

USB 3.0 Driver Installation	13

RAID Utility Installation	13

Network Utility Installation	13

Intel Onboard SATA RAID	13

BIOS Required	13

Drivers required (64-bit)	13

Software Required	14

Configuring Intel Onboard SATA RAID	14

Installation Tips	14

Chipset Driver Package Installation	15

Gigabit Ethernet Driver Installation	15

Graphics Card Driver Installation	15

TPM Driver Installation (Optional)	15

Audio Driver Installation	15

USB 3.0 Driver Installation	15

RAID Utility Installation	16

Network Utility Installation	16

MegaRAID 9240-4i/9260-4i/9260-8i	16

BIOS Required	16

Drivers required (64-bit)	16

Software Required	16

Configuring MegaRAID 9240-4i/9260-4i/9260-8i	17

Installation Tips	17

Chipset Driver Package Installation	17

Gigabit Ethernet Driver Installation	17

Graphics Card Driver Installation	18

TPM Driver Installation (Optional)	18

Audio Driver Installation	18

USB 3.0 Driver Installation	18

RAID Utility Installation	18

Network Utility Installation	18

Red Hat Enterprise Linux 6 WoRkstation Update 4	19

Onboard SATA	19

BIOS Required	19

Drivers Required (64 bit)	19

Installation Tips	19

Gigabit Ethernet Driver Installation	19

Graphics Card Driver Installation	20

MegaRAID 9240-4i/9260-4i/9260-8i	20

BIOS Required	20

Drivers Required (64 bit)	20

Installation Tips	20

Gigabit Ethernet Driver Installation	21

Graphics Card Driver Installation	21

RAID Utility Installation	21

APPENDIX A: Intel onboard SAS RAID (SATA Mode) CONFIGURATION	23

Enabling Intel Onboard SAS RAID (SATA Mode)	23

Set RAID Controller in EFI Mode or Legacy Mode	23

Entering Intel onboard SAS RAID BIOS Utility	23

Loading Factory Default Setting	24

Creating a RAID Volume	24

Initializing a RAID Volume	24

Assigning a Hot Spare Drive	24

APPENDIX B: Intel onboard SATA RAID CONFIGURATION	25

Enabling Intel Onboard SATA RAID	25

Set RAID Controller in EFI Mode or Legacy Mode	25

Entering Intel onboard SATA RAID BIOS Utility	25

Loading Factory Default Setting	26

Creating a RAID Volume	26

Initializing a RAID Volume	26

Assigning a Hot Spare Drive	26

APPENDIX C: MEGARAID  9240-4i/ MEGARAID 9260-4i/MegaRAID 9260-8i RAID CONFIGuration	27

Entering RAID BIOS Utility	27

Loading Factory Default Setting	27

Creating a RAID Volume	27

Initializing a RAID Volume	27

Assigning a Hot Spare Drive	28

# Introduction

For user wants to install the OS manually, this document provides you a OS installation guide on Veriton P330 F2, including,

Windows 8 (64-bit)

Windows 7 SP1 (64-bit)

Red Hat Enterprise Linux 6 Workstation Update 4 (64-bit)

# Windows 8

## Intel Onboard SAS RAID (SATA Mode)

Below information describes how to manually install Windows 8 on Veriton P330 F2 with Intel Onboard SAS RAID (SATA Mode).

### BIOS Required

Veriton P330 F2 BIOS 1.1 (or later) is required to support Windows 8.

### Drivers Required (64-bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SAS RAID (SATA Mode) | 3.6.0.1090 | Driver CD |
| Chipset | 9.4.0.1014 | Driver CD |
| Onboard Gigabit Ethernet | Package 18.0.1 | Driver CD |
| Graphics Card1 | Package 311 | Driver CD |
| TPM | N/A | OS Built-in |
| Audio | 6.0.1.6849 | Driver CD |
| USB 3.0 | 2.1.16.0 | Driver CD |

NOTE 1: The Driver CD only includes nVidia graphics card driver.

Package 311.15 is the driver for nVidia Quadro Series

Package 311.41 is the driver for nVidia GeForce Series

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| PROSet | 18.0.1.0 (Package 18.0.1) | Driver CD |

### Configuring Intel Onboard SAS RAID (SATA Mode)

Please refer to Appendix A. for Intel Onboard SAS RAID (SATA Mode) configuration.

### Installation Tips

NOTE. When you install OS with Intel Onboard SAS RAID (SATA Mode), please

Change the setting of Onboard SATA to AHCI Mode through SATA Configuration in BIOS Setup

SATA Mode                   [AHCI Mode]

NOTE. Windows 8 supports EFI, please press F11 during POST to select OS installation in EFI mode or Legacy mode. For example, you would see options similar to below:

UEFI: HL-DT-STDVD-ROM GSA-E60L1.00
HL-DT-STDVD-ROM GSA-E60L1.00

Please select UEFI: HL-DT-STDVD-ROM GSA-E60L1.00 and press Enter if you want to install OS in EFI mode.

NOTE. Windows 8 cannot detect Intel Onboard SAS RAID (SATA Mode). Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

Please boot the system from the Windows 8 DVD. Follow the instructions to do the installation.

When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Onboard SATA RAID driver and click on “Load Driver”.

Specify the folder that includes the Intel onboard SAS RAID driver and the system will show the available driver. Select “Intel (R) C600 Series Chipset SAS RAID (SATA mode) (C:\iaStorS.inf)” as target driver.

After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Driver CD into the optical drive.

- Select “Intel Chipset Generic Driver” to install the chipset driver.

- Follow the instruction to install the driver and reboot the server after the chipset driver is installed.

### Gigabit Ethernet Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Intel Lan Generic Driver” to install the Gigabit Ethernet driver.

- Follow the instruction, accept the license agreement and use the default setting to complete the driver installation.

The driver and PROSet utility will be installed together automatically.

### Graphics Card Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “nVidia VGA Generic Driver” to install the graphic card driver.

- Follow the instruction to install the driver and reboot the server after the graphic card driver is installed.

### TPM Driver Installation (Optional)

NOTE: TPM driver is only needed when TPM module is installed.

Windows 8 has built-in driver for TPM. You don’t need to install additional TPM driver manually.

### Audio Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Realtek Audio Generic Driver” to install the audio driver.

- Follow the instruction to complete the driver installation.

### USB 3.0 Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Renesas USB 3.0 Generic Driver” to install the USB 3.0 driver.

- Follow the instruction to complete the driver installation.

### RAID Utility Installation

- Please insert the Driver CD into the optical drive.

- Execute the RAID utility and then follow the instruction to complete the RAID Utility Installation.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## Intel Onboard SATA RAID

Below information describes how to manually install Windows 8 on Veriton P330 F2 with Intel Onboard SATA RAID.

### BIOS Required

Veriton P330 F2 BIOS 1.1 (or later) is required to support Windows 8.

### Drivers required (64-bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SATA RAID | 3.6.0.1090 | Driver CD |
| Chipset | 9.4.0.1014 | Driver CD |
| Onboard Gigabit Ethernet | Package 18.0.1 | Driver CD |
| Graphics Card1 | Package 311 | Driver CD |
| TPM | N/A | OS Built-in |
| Audio | 6.0.1.6849 | Driver CD |
| USB 3.0 | 2.1.16.0 | Driver CD |

NOTE 1: The Driver CD only includes nVidia graphics card driver.

Package 311.15 is the driver for nVidia Quadro Series

Package 311.41 is the driver for nVidia GeForce Series

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel Onboard SAS RAID Utility | 3.6.0.1094 | Driver CD |
| PROSet | 18.0.1.0 (Package 18.0.1) | Driver CD |

### Configuring Intel Onboard SATA RAID

Please refer to Appendix B. for Intel Onboard SATA RAID configuration.

### Installation Tips

NOTE. When you install OS with Intel Onboard SATA RAID, please

Disable Onboard SAS RAID (SATA Mode) through SCU Configuration in BIOS Setup

Storage Controller Unit     [Disabled]

NOTE. Windows 8 supports EFI, please press F11 during POST to select OS installation in EFI mode or Legacy mode. For example, you would see options similar to below:

UEFI: HL-DT-STDVD-ROM GSA-E60L1.00
HL-DT-STDVD-ROM GSA-E60L1.00

Please select UEFI: HL-DT-STDVD-ROM GSA-E60L1.00 and press Enter if you want to install OS in EFI mode.

NOTE. The Windows 8 cannot detect Intel Onboard SATA RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

- Please boot the system from the Windows 8 DVD. Follow the instructions to do the installation.

When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Onboard SATA RAID driver and click on “Load Driver”.

Specify the folder that includes the Intel onboard SAS RAID driver and the system will show the available driver. Select “Intel C600/C220 series chipset SATA RAID Controller (C:\iaStorA.inf)” as target driver.

After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Driver CD into the optical drive.

- Select “Intel Chipset Generic Driver” to install the chipset driver.

- Follow the instruction to install the driver and reboot the server after the chipset driver is installed.

### Gigabit Ethernet Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Intel Lan Generic Driver” to install the Gigabit Ethernet driver.

- Follow the instruction, accept the license agreement and use the default setting to complete the driver installation.

The driver and PROSet utility will be installed together automatically.

### Graphics Card Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “nVidia VGA Generic Driver” to install the graphic card driver.

- Follow the instruction to install the driver and reboot the server after the graphic card driver is installed.

### TPM Driver Installation (Optional)

NOTE: TPM driver is only needed when TPM module is installed.

Windows 8 has built-in driver for TPM. You don’t need to install additional TPM driver manually.

### Audio Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Realtek Audio Generic Driver” to install the audio driver.

- Follow the instruction to complete the driver installation.

### USB 3.0 Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Renesas USB 3.0 Generic Driver” to install the USB 3.0 driver.

- Follow the instruction to complete the driver installation.

### RAID Utility Installation

- Please insert the Driver CD into the optical drive.

- Execute the RAID utility and then follow the instruction to complete the RAID Utility Installation.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## MegaRAID 9240-4i/9260-4i/9260-8i

Below information describes how to manually install Windows 8 on Veriton P330 F2 with MegaRAID 9240-4i/9260-4i/9260-8i.

### BIOS Required

Veriton P330 F2 BIOS 1.1 (or later) is required to support Windows 8.

### Drivers required (64-bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| MegaRAID 9240-4i/9260-4i/9260-8i | 6.600.23.00 | Acer website |
| Chipset | 9.4.0.1014 | Driver CD |
| Onboard Gigabit Ethernet | Package 18.0.1 | Driver CD |
| Graphics Card1 | Package 311 | Driver CD |
| TPM | N/A | OS Built-in |
| Audio | 6.0.1.6849 | Driver CD |
| USB 3.0 | 2.1.16.0 | Driver CD |

NOTE 1: The Driver CD only includes nVidia graphics card driver.

Package 311.15 is the driver for nVidia Quadro Series

Package 311.41 is the driver for nVidia GeForce Series

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 13.04.03.01 | Acer website |
| PROSet | 18.0.1.0 (Package 18.0.1) | Driver CD |

### Configuring MegaRAID 9240-4i/9260-4i/9260-8i

Please refer to Appendix C for MegaRAID 9240-4i/9260-4i/9260-8i configuration.

### Installation Tips

NOTE. When you install OS with MegaRAID, please

Disable Onboard SAS RAID (SATA Mode) through SCU Configuration in BIOS Setup

Storage Controller Unit     [Disabled]

Change the setting of Onboard SATA to AHCI Mode through SATA Configuration in BIOS Setup

SATA Mode                   [AHCI Mode]

NOTE. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

- Please boot the system from the Windows 8 DVD. Follow the instructions to do the installation.

When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Onboard SATA RAID driver and click on “Load Driver”.

Specify the folder that includes the Intel onboard SAS RAID driver and the system will show the available driver. Select “LSI MegaRAID SAS PCI Express ROMB (C:\megasas2.inf)” as target driver.

After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Driver CD into the optical drive.

- Select “Intel Chipset Generic Driver” to install the chipset driver.

- Follow the instruction to install the driver and reboot the server after the chipset driver is installed.

### Gigabit Ethernet Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Intel Lan Generic Driver” to install the Gigabit Ethernet driver.

- Follow the instruction, accept the license agreement and use the default setting to complete the driver installation.

The driver and PROSet utility will be installed together automatically.

### Graphics Card Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “nVidia VGA Generic Driver” to install the graphic card driver.

- Follow the instruction to install the driver and reboot the server after the graphic card driver is installed.

### TPM Driver Installation (Optional)

NOTE: TPM driver is only needed when TPM module is installed.

Windows 8 has built-in driver for TPM. You don’t need to install additional TPM driver manually.

### Audio Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Realtek Audio Generic Driver” to install the audio driver.

- Follow the instruction to complete the driver installation.

### USB 3.0 Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Renesas USB 3.0 Generic Driver” to install the USB 3.0 driver.

- Follow the instruction to complete the driver installation.

### RAID Utility Installation

- Execute the RAID utility and then follow the instruction to complete the RAID Utility Installation.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

# Windows 7 SP1

## Intel Onboard SAS RAID (SATA Mode)

Below information describes how to manually install Windows 7 SP1 on Veriton P330 F2 with Intel Onboard SAS RAID (SATA Mode).

### BIOS Required

Veriton P330 F2 BIOS 1.1 (or later) is required to support Windows 7 SP1.

### Drivers required (64-bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SATA RAID | 3.6.0.1090 | Driver CD |
| Chipset | 9.4.0.1014 | Driver CD |
| Onboard Gigabit Ethernet | Package 18.0.1 | Driver CD |
| Graphics Card1 | Package 311 | Driver CD |
| TPM | N/A | OS Built-in |
| Audio | 6.0.1.6849 | Driver CD |
| USB 3.0 | 2.1.16.0 | Driver CD |

NOTE 1: The Driver CD only includes nVidia graphics card driver.

Package 311.15 is the driver for nVidia Quadro Series

Package 311.41 is the driver for nVidia GeForce Series

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel Onboard SAS RAID Utility | 3.6.0.1094 | Driver CD |
| PROSet | 18.0.1.0 (Package 18.0.1) | Driver CD |

### Configuring Intel Onboard SAS RAID (SATA Mode)

Please refer to Appendix A. for Intel Onboard SAS RAID (SATA Mode) configuration.

### Installation Tips

NOTE. When you install OS with Intel Onboard SAS RAID (SATA Mode), please

Change the setting of Onboard SATA to AHCI Mode through SATA Configuration in BIOS Setup

SATA Mode                   [AHCI Mode]

NOTE. Windows 7 SP1 cannot detect Intel Onboard SAS RAID (SATA Mode). Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

- Please boot the system from the Windows 7 SP1 DVD. Follow the instructions to do the installation.

When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Onboard SATA RAID driver and click on “Load Driver”.

Specify the folder that includes the Intel onboard SAS RAID driver and the system will show the available driver. Select “Intel (R) C600 Series Chipset SAS RAID (SATA mode) (C:\iaStorS.inf)” as target driver.

After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Driver CD into the optical drive.

- Select “Intel Chipset Generic Driver” to install the chipset driver.

- Follow the instruction to install the driver and reboot the server after the chipset driver is installed.

### Gigabit Ethernet Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Intel Lan Generic Driver” to install the Gigabit Ethernet driver.

- Follow the instruction, accept the license agreement and use the default setting to complete the driver installation.

The driver and PROSet utility will be installed together automatically.

### Graphics Card Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “nVidia VGA Generic Driver” to install the graphic card driver.

- Follow the instruction to install the driver and reboot the server after the graphic card driver is installed.

### TPM Driver Installation (Optional)

NOTE: TPM driver is only needed when TPM module is installed.

Windows 7 SP1 has built-in driver for TPM. You don’t need to install additional TPM driver manually.

### Audio Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Realtek Audio Generic Driver” to install the audio driver.

- Follow the instruction to complete the driver installation.

### USB 3.0 Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Renesas USB 3.0 Generic Driver” to install the USB 3.0 driver.

- Follow the instruction to complete the driver installation.

### RAID Utility Installation

- Please insert the Driver CD into the optical drive.

- Execute the RAID utility and then follow the instruction to complete the RAID Utility Installation.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## Intel Onboard SATA RAID

Below information describes how to manually install Windows 7 SP1 on Veriton P330 F2 with Intel Onboard SATA RAID.

### BIOS Required

Veriton P330 F2 BIOS 1.1 (or later) is required to support Windows 7 SP1.

### Drivers required (64-bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Intel Onboard SATA RAID | 3.6.0.1090 | Driver CD |
| Chipset | 9.4.0.1014 | Driver CD |
| Onboard Gigabit Ethernet | Package 18.0.1 | Driver CD |
| Graphics Card1 | Package 311 | Driver CD |
| TPM | N/A | OS Built-in |
| Audio | 6.0.1.6849 | Driver CD |
| USB 3.0 | 2.1.16.0 | Driver CD |

NOTE 1: The Driver CD only includes nVidia graphics card driver.

Package 311.15 is the driver for nVidia Quadro Series

Package 311.41 is the driver for nVidia GeForce Series

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| Intel Onboard SAS RAID Utility | 3.6.0.1094 | Driver CD |
| PROSet | 18.0.1.0 (Package 18.0.1) | Driver CD |

### Configuring Intel Onboard SATA RAID

Please refer to Appendix B. for Intel Onboard SATA RAID configuration.

### Installation Tips

NOTE. When you install OS with Intel Onboard SATA RAID, please

Disable Onboard SAS RAID (SATA Mode) through SCU Configuration in BIOS Setup

Storage Controller Unit     [Disabled]

NOTE. The Windows 7 SP1 cannot detect Intel Onboard SATA RAID. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

- Please boot the system from the Windows 7 SP1 DVD. Follow the instructions to do the installation.

When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Onboard SATA RAID driver and click on “Load Driver”.

Specify the folder that includes the Intel onboard SAS RAID driver and the system will show the available driver. Select “Intel C600/C220 series chipset SATA RAID Controller (C:\iaStorA.inf)” as target driver.

After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Driver CD into the optical drive.

- Select “Intel Chipset Generic Driver” to install the chipset driver.

- Follow the instruction to install the driver and reboot the server after the chipset driver is installed.

### Gigabit Ethernet Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Intel Lan Generic Driver” to install the Gigabit Ethernet driver.

- Follow the instruction, accept the license agreement and use the default setting to complete the driver installation.

The driver and PROSet utility will be installed together automatically.

### Graphics Card Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “nVidia VGA Generic Driver” to install the graphic card driver.

- Follow the instruction to install the driver and reboot the server after the graphic card driver is installed.

### TPM Driver Installation (Optional)

NOTE: TPM driver is only needed when TPM module is installed.

Windows 7 SP1 has built-in driver for TPM. You don’t need to install additional TPM driver manually.

### Audio Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Realtek Audio Generic Driver” to install the audio driver.

- Follow the instruction to complete the driver installation.

### USB 3.0 Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Renesas USB 3.0 Generic Driver” to install the USB 3.0 driver.

- Follow the instruction to complete the driver installation.

### RAID Utility Installation

- Please insert the Driver CD into the optical drive.

- Execute the RAID utility and then follow the instruction to complete the RAID Utility Installation.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

## MegaRAID 9240-4i/9260-4i/9260-8i

Below information describes how to manually install Windows 7 SP1 on Veriton P330 F2 with MegaRAID 9240-4i/9260-4i/9260-8i.

### BIOS Required

Veriton P330 F2 BIOS 1.1 (or later) is required to support Windows 7 SP1.

### Drivers required (64-bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| MegaRAID 9240-4i/9260-4i/9260-8i | 6.600.23.00 | Acer website |
| Chipset | 9.4.0.1014 | Driver CD |
| Onboard Gigabit Ethernet | Package 18.0.1 | Driver CD |
| Graphics Card1 | Package 311 | Driver CD |
| TPM | N/A | OS Built-in |
| Audio | 6.0.1.6849 | Driver CD |
| USB 3.0 | 2.1.16.0 | Driver CD |

NOTE 1: The Driver CD only includes nVidia graphics card driver.

Package 311.15 is the driver for nVidia Quadro Series

Package 311.41 is the driver for nVidia GeForce Series

### Software Required

| Software | Version | Software Source |
| --- | --- | --- |
| MegaRAID Storage Manager | 13.04.03.01 | Acer website |
| PROSet | 18.0.1.0 (Package 18.0.1) | Driver CD |

### Configuring MegaRAID 9240-4i/9260-4i/9260-8i

Please refer to Appendix C for MegaRAID 9240-4i/9260-4i/9260-8i configuration.

### Installation Tips

NOTE. When you install OS with MegaRAID, please

Disable Onboard SAS RAID (SATA Mode) through SCU Configuration in BIOS Setup

Storage Controller Unit     [Disabled]

Change the setting of Onboard SATA to AHCI Mode through SATA Configuration in BIOS Setup

SATA Mode                   [AHCI Mode]

NOTE. Please load the RAID driver during OS installation.

NOTE. You need an external USB floppy drive or USB Flash drive to load RAID driver during the OS installation.

- Please boot the system from the Windows 7 SP1 DVD. Follow the instructions to do the installation.

When “Where do you want to install Windows” message displayed, please Insert the USB flash which includes the Intel Onboard SATA RAID driver and click on “Load Driver”.

Specify the folder that includes the Intel onboard SAS RAID driver and the system will show the available driver. Select “LSI MegaRAID SAS PCI Express ROMB (C:\megasas2.inf)” as target driver.

After loading the RAID driver, you could click “Drive options” to partition the drive or click “Next” to use default disk partition setting directly.

Follow the normal procedure to finish the installation.

### Chipset Driver Package Installation

- Please insert the Driver CD into the optical drive.

- Select “Intel Chipset Generic Driver” to install the chipset driver.

- Follow the instruction to install the driver and reboot the server after the chipset driver is installed.

### Gigabit Ethernet Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Intel Lan Generic Driver” to install the Gigabit Ethernet driver.

- Follow the instruction, accept the license agreement and use the default setting to complete the driver installation.

The driver and PROSet utility will be installed together automatically.

### Graphics Card Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “nVidia VGA Generic Driver” to install the graphic card driver.

- Follow the instruction to install the driver and reboot the server after the graphic card driver is installed.

### TPM Driver Installation (Optional)

NOTE: TPM driver is only needed when TPM module is installed.

Windows 7 SP1 has built-in driver for TPM. You don’t need to install additional TPM driver manually.

### Audio Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Realtek Audio Generic Driver” to install the audio driver.

- Follow the instruction to complete the driver installation.

### USB 3.0 Driver Installation

- Please insert the Driver CD into the optical drive.

- Select “Renesas USB 3.0 Generic Driver” to install the USB 3.0 driver.

- Follow the instruction to complete the driver installation.

### RAID Utility Installation

- Execute the RAID utility and then follow the instruction to complete the RAID Utility Installation.

### Network Utility Installation

The PROSet utility for the onboard Gigabit Ethernet controller will be installed automatically when you installing the onboard Gigabit Ethernet driver.

# Red Hat Enterprise Linux 6 WoRkstation Update 4

## Onboard SATA

Below information describes how to manually install Red Hat Enterprise Linux 6 Workstation Update 4 on Veriton P330 F2 with Onboard SATA.

### BIOS Required

Veriton P330 F2 BIOS 1.1 (or later) is required to support Onboard SATA.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| Graphics Card | N/A | OS Built-in |
| Onboard Gigabit Ethernet | Package 18.0.1 | Driver CD |

### Installation Tips

- Please boot the system from the Red Hat Enterprise Linux 6 Workstation Update 4.

- At Welcome Menu, please press Enter.

- Follow the instruction for the installation.

- Please Select Software Development Workstation.

- Please follow the normal procedure to finish the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in the Drive CD. Please check path of the driver in Windows OS environment first and copy the driver from the Drive CD (\PRO1000\Linux) to HDD (e.g. /tmp directory)

- Please switch to console mode.

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod e1000e

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf e1000e-<version>.tar.gz

# cd e1000e-<version>/src/

# make install

# modprobe e1000e

- Start the network service to bring up both of the network interfaces.

# service network start

- Use the network configuration utility like system-config-network to configure the network interfaces.

### Graphics Card Driver Installation

NOTE. Red Hat Enterprise Linux 6 Workstation Update 4 has a built-in driver to support graphics card. You would see the graphics card detected by below command:

# lspci | grep VGA

## MegaRAID 9240-4i/9260-4i/9260-8i

Below information describes how to manually install Red Hat Enterprise Linux 6 Workstation Update 4 on Veriton P330 F2 with MegaRAID 9240-4i/9260-4i/9260-8i.

### BIOS Required

Veriton P330 F2 BIOS 1.1 (or later) is required to support MegaRAID 9240-4i/9260-4i/9260-8i.

### Drivers Required (64 bit)

| Device | Version | Driver Source |
| --- | --- | --- |
| MegaRAID 9240-4i/9260-4i/9260-8i | N/A | OS Built-in |
| Graphics Card | N/A | OS Built-in |
| Onboard Gigabit Ethernet | Package 18.0.1 | Driver CD |

### Installation Tips

- Please boot the system from the Red Hat Enterprise Linux 6 Workstation Update 4.

- At Welcome Menu, please press Enter.

- Follow the instruction for the installation.

- Please Select Software Development Workstation.

- Please follow the normal procedure to finish the installation.

### Gigabit Ethernet Driver Installation

NOTE. The onboard Gigabit Ethernet driver is included in the Drive CD. Please check path of the driver in Windows OS environment first and copy the driver from the Drive CD (\PRO1000\Linux) to HDD (e.g. /tmp directory)

- Please switch to console mode.

- Stop network service

# service network stop

- Remove the OS built-in NIC driver

# rmmod e1000e

- Change the directory to the driver source and install the driver

# cd /tmp

# tar zxvf e1000e-<version>.tar.gz

# cd e1000e-<version>/src/

# make install

# modprobe e1000e

- Start the network service to bring up both of the network interfaces.

# service network start

- Use the network configuration utility like system-config-network to configure the network interfaces.

### Graphics Card Driver Installation

NOTE. Red Hat Enterprise Linux 6 Workstation Update 4 has a built-in driver to support graphics card. You would see the graphics card detected by below command:

# lspci | grep VGA

### RAID Utility Installation

- Unzip RAID Utility file

# tar zxvf <version>_MSM.tar.gz

- Install RAID Utility

# cd disk

# ./install.csh

- Input Y to accept the license agreement.

- Please select 3 for StandAlone installation.

- To start the RAID Utility, click on Applications -> System Tools -> MegaRAID Storage Manager StartupUI.

# APPENDIX A: Intel onboard SAS RAID (SATA Mode) CONFIGURATION

## Enabling Intel Onboard SAS RAID (SATA Mode)

NOTE. The Intel Onboard SAS RAID on Veriton P330 F2 only support SATA mode.

- Turn on the server. If the server is already turned on, please close all open applications and then restart the server.

Please enter BIOS Setup during POST.

Please select Advanced.

Select SCU Configuration.

You would see below information:

Storage Controller Unit          [Enabled] 
SCU RAID Option ROM/UEFI Driver  [Enabled]

Make sure the Storage Controller Unit and SCU RAID Option ROM/UEFI Driver options are enabled

Please press F4 to save the setting and exit.

## Set RAID Controller in EFI Mode or Legacy Mode

NOTE. For EFI mode, we recommended completing the RAID configuration in Legacy mode first and then enter BIOS Setup to change Launch Storage OpROM Policy option to “EFI only” mode.

- Please enter BIOS Setup during POST

- Please select Advanced.

Please select PCIe/PCI/PnP Configuration.

- You would see below information.

Launch Storage OpROM Policy    [Legacy Only]

NOTE. The default setting is Legacy Only.

- To enable Legacy mode of RAID controller, please keep Launch Storage OpROM Policy as “Legacy only”. To enable EFI mode of RAID controller, please change Launch Storage OpROM Policy as “UEFI only”.

- Please press F4 to save the setting and exit.

## Entering Intel onboard SAS RAID BIOS Utility

Please press CTRL-I when you see the RAID BIOS during POST. The Intel(R) Rapid Storage Technology enterprise – SCU Option ROM will display on the screen.

## Loading Factory Default Setting

- In the Main Menu, select third option Reset Disks to Non-RAID.

Select the hard disk drive desired and press ENTER to complete your selection.

Then press Y to reset RAID data on selected hard disks.

## Creating a RAID Volume

- Select Create RAID Volume.

The CREATE VOLUME MENU displayed.

Type in the name of RAID volume.

Select RAID level.

Select desired HDD to create the RAID.

Select Create Volume.

Press Y when “Are you sure you want to create the volume? (Y/N):” displayed.

Now the RAID volume is created, you can press ESC and select Exit to exit.

## Initializing a RAID Volume

During Intel onboard SAS RAID (SATA Mode) volume creation process, the Intel onboard SAS RAID (SATA Mode) volume will be automatically initiated once the onboard SAS RAID (SATA Mode) volume has been created.

## Assigning a Hot Spare Drive

The Intel onboard SAS RAID BIOS utility does not provide the function to create hot spare drive. Please create the hot spare drive with the Intel onboard SAS RAID utility in operating system.

# APPENDIX B: Intel onboard SATA RAID CONFIGURATION

## Enabling Intel Onboard SATA RAID

- Turn on the server. If the server is already turned on, please close all open applications and then restart the server.

Please enter BIOS Setup during POST.

Please select Advanced.

Please select SATA Configuration.

You would see below information:

SATA Mode                        [AHCI Mode]

Please change SATA Mode option to “RAID Mode”

You would see updated information as below:

SATA Mode                        [RAID Mode] 
SATA RAID Option ROM/UEFI Driver [Enabled]

Please press F4 to save the setting and exit.

## Set RAID Controller in EFI Mode or Legacy Mode

NOTE. For EFI mode, we recommended completing the RAID configuration in Legacy mode first and then enter BIOS Setup to change Launch Storage OpROM Policy option to “EFI only” mode.

- Please enter BIOS Setup during POST

- Please select Advanced.

Please select PCIe/PCI/PnP Configuration.

- You would see below information.

Launch Storage OpROM Policy    [Legacy Only]

NOTE. The default setting is Legacy Only.

- To enable Legacy mode of RAID controller, please keep Launch Storage OpROM Policy as “Legacy only”. To enable EFI mode of RAID controller, please change Launch Storage OpROM Policy as “UEFI only”.

- Please press F4 to save the setting and exit.

## Entering Intel onboard SATA RAID BIOS Utility

Please press CTRL-I when you see the RAID BIOS during POST. The Intel(R) Rapid Storage Technology enterprise – SATA Option ROM will display on the screen.

## Loading Factory Default Setting

- In the Main Menu, select third option Reset Disks to Non-RAID.

Select the hard disk drive desired and press ENTER to complete your selection.

Then press Y to reset RAID data on selected hard disks.

## Creating a RAID Volume

- Select Create RAID Volume.

The CREATE VOLUME MENU displayed.

Type in the name of RAID volume.

Select RAID level.

Select desired HDD to create the RAID.

Select Create Volume.

Press Y when “Are you sure you want to create the volume? (Y/N):” displayed.

Now the RAID volume is created, you can press ESC and select Exit to exit.

## Initializing a RAID Volume

During Intel onboard SATA RAID volume creation process, the Intel onboard SATA RAID volume will be automatically initiated once the onboard SATA RAID volume has been created.

## Assigning a Hot Spare Drive

The Intel onboard SATA RAID BIOS utility does not provide the function to create hot spare drive. Please create the hot spare drive with the Intel onboard SATA RAID utility in operating system.

# APPENDIX C: MEGARAID 9240-4i/ MEGARAID 9260-4i/MegaRAID 9260-8i RAID CONFIGuration

## Set RAID Controller in Legacy Mode

- Please enter BIOS Setup during POST

- Select Advanced.

- Select PCIe/PCI/PnP Configuration

- You would see below information.

Launch Storage OpROM policy    [Legacy only]

- To enable legacy mode for MegaRAID 9240-4i/9260-4i/9260-8i, please make sure the option is “Legacy only”.

Launch Storage OpROM policy    [Legacy only]

- Save the setting and exit from BIOS Setup.

## Entering RAID BIOS Utility (Legacy Mode)

Please press CTRL-H when you see the RAID BIOS during POST. After POST finished, the Adapter Selection page will show on the screen. Please click on Start to launch the configuration menu.

## Loading Factory Default Setting

- In the left panel, select Controller Properties. The current adapter settings appear. Please click on Next to change the setting.

- Change the setting of Set Factory Defaults from No to Yes then click on submit.

- Press Home button

- Please select Exit in left panel

- Press Ctrl + Alt + Del to reboot the server.

## Creating a RAID Volume

- Launch the configuration menu.

- Select Configuration Wizard in left panel

- Select New Configuration and click on Next.

- Select Manual Configuration and click on Next.

- Hold the Ctrl key and select the drives that you want to add into the array. After you selecting the drives, click on Add to Array.

- Click on Accept DG and then click on Next.

- Select the array you just created, click on Add to SPAN and then Next.

- Select the RAID Level you want to use, create the logical volume by specify the size at Select Size and click on Accept to create the logical volume.

- Click on Next after you creating the logical volume.

- Click on Accept and Yes to save the configuration.

## Initializing a RAID Volume

- After you create the logical volumes and click on Accept to save the configuration, the new logical volume will be automatically initialized after you click on Yes to confirm the change.

- You will see all the logical drives listed.

- Click on Home to go back to the configuration menu.

## Assigning a Hot Spare Drive

- Select a free disk marked as UNCONF GOOD and listed under Physical Drives.

- Select Make Global HSP or Make Dedicated HSP options and then click on Go.

- Click on Home to go back to the configuration menu. You will see the disk marked as Hot Spare in pink and listed under Physical Drives.

Now you can reboot the system and install the Operating System. Select Exit, click on Yes and press Ctrl + Alt + Del to reboot the system.